## Slide 1
Title Sheet
Drawing #:
1
List of Drawings
1 Title Sheet
Site Plans
C4 Floor Layout
Demolition Plan (typical)
New Construction Plan (Typical)
Typical Wall Construction Details
Typical Wall Accessories Plan
Typical Electrical Plan
Miscellaneous Details
C5 Floor Layout
TEWKSBURY HOSPITAL
SAUNDERS BUILDING
DMH Project No: 2019-106

## Slide 2
Site Plan
Drawing #:
2
Aerial photograph of the Saunders Building
Location of “C” wing
C Wing
DMH Project No: 2019-106

## Slide 3
C4 Floor Layout
Room #061
Room #060
Room #056
Room #035
Room #034
Room #040
Drawing #:
3
DMH Project No: 2019-106
Note: Rooms 061, 060, 056, 035, 034, and 040 are the rooms where the work will occur.

## Slide 4
Typical Demolition Plan
4
Drawing #:
Remove existing tile & CMU needed for installation of new door frame
Remove existing tile needed for installation of new wall
Remove existing heating system needed for installation of new wall
Remove existing light fixtures and smoke detector
Legend
smoke detector
1’ x 4’ lighting fixture
heating unit
mullion in window glass
DEMOLITION NOTES
Cut existing tile and CMU at new door frame locations to inside dimension of frame.
Cut interior and corridor tile back to edge of frame.
Cut existing interior title at proposed connection to new wall assembly.
Remove and properly store existing fixtures and smoke detectors.
Disconnect heating unit and remove required components to allow new wall assembly to be flush with existing window mullion.
Remove existing lighting wall switch at pipe chase.
Remove existing light switch
DMH Project No: 2019-106

## Slide 5
Typical New Construction Plan
Drawing #:
5
New Light Switches (one double switch per bedroom)
New Door Frame
New Wicket Doors
New Gypsum Wall Assembly
New Lighting Fixtures
New Smoke Detectors
New Night Lights (two per bedroom)
New Thermostat
(one per bedroom)
Cover existing light switch opening with epoxy-painted 12 GA. Steel covers.
DMH Project No: 2019-106

## Slide 6
Typical Wall Construction Details
Drawing #:
6
Fire Stop Track w/ fasteners 24 in. o.c. max
Bottom rail w/ fasteners 24 in. o.c. max
25-ga. 3-5/8” metal studs 16”o.c.
Thermafiber Sound Attenuation Blankets (SAFB)
5/8” Plywood
5/8” Gypsum Panel
FLOOR SLAB
CEILING SLAB
Wall Assembly At Corridor Wall
Wall Assembly At Window Mullion
Tile
4” CMU
Window Mullion
Isolation strip
2” to 6”
Steel Stud
Wall Assembly At Corner
DMH Project No: 2019-106
Direct Furring Strip

## Slide 7
Typical Wall Accessories
Plan
Legend
night light (recessed)
Lighting switch (recessed)
Thermostat (recessed)
access panel (surface mount)
7
Drawing #:
5’ -0”
2’ -0”
8’ - 9”
WALL ACCESSORIES NOTES
Three 1’ x 1’ plastic access panels are to be installed in six of the bedrooms providing access to the electrical and smoke detector junction boxes.
One new light switch shall be installed in each bedroom and shall be approximately 3’ from interior side of corridor wall.
Two night lights shall be installed in each bedroom with a switch connection at the lighting switch location. Night lights shall be installed at approximately 8’ and 16’ from interior side of corridor wall.
One new thermostat shall be installed in each bedroom. Thermostat shall be installed at approximately 12’ from interior side of corridor wall.
DMH Project No: 2019-106

## Slide 8
Typical Electrical Plan
Drawing #:
8
Existing Electrical Layout
Proposed Electrical Layout
Legend
night light (recessed)
Smoke Detector (Surface Mounted)
Thermostat (recessed)
1’ x 4’ surface mounted light fixture
Existing Junction Box
New surface mounted wiremold
DMH Project No: 2019-106

## Slide 9
Miscellaneous Details
Drawing #:
9
Metal Door Frame Detail
DMH Project No: 2019-106

## Slide 10
C5 Floor Layout
Room #061
Room #060
Room #056
Room #035
Room #034
Room #040
Drawing #:
10
DMH Project No: 2019-106
Note: Rooms 061, 060, 056, 035, 034, and 040 are the rooms where the work will occur.