## Slide 1
Inquiry On Pole Attachment and Conduit Access on Public Rights of Way
D.P.U. 25-10/D.T.C. 25-1
Technical Session Presentations
Topic 2: ROW Planning and Coordination with Municipalities, MassDOT, and Public Safety
Alan Denapoli and Al Bessette

## Slide 2: Roadway Moratoriums
Permit Delays: Key Factors
Seasonal Moratoriums:
  When: Typically November - April
  Impact: Delays obtaining street opening permits for trench work.
Paving Moratoriums (Some Communities):
  When: Typically 5 years from road resurfacing
  Impact: Prevents trench activities.
Note: Surveys and Pole work are not affected by these moratoriums

## Slide 3: Permitting for Survey and Make Ready Work
Survey Work:
  No permit required.
  No police detail or flaggers needed.
Working on MassDOT Roads:
  Permit required for any work performed by Verizon’s Operations Department.
  Police details/flaggers likely required based on permit conditions (e.g., traffic impact).
New Pole Installation on Municipal Roads:
  Permit required.
  Police details/flaggers likely required based on permit & field conditions (e.g., traffic impact).

## Slide 4: Jointly Owned Poles: Permitting Requirements
General Principle: When a pole is jointly owned, the permitting requirements vary based on the road authority.
MassDOT Roads:
  Each company must obtain its own separate permit for the specific work it performs.
Municipal Roads:
  Only the company that originally placed the pole is required to obtain the permit for the work being conducted.

## Slide 5: ROW Licenses/Permits: Detail Requirements
Simple Make-Ready (e.g., cable rearrangement):
  Municipal & MassDOT Permits: Standard permit application process; no additional detailed sketches typically required.
Complex Make Ready (e.g., New Pole Installation, Pole Replacement):
  Municipal & MassDOT Permits: A detailed sketch showing the full scope of work is required as part of the permit application.

## Slide 6: Separate Permits for Attachments
Must each attacher obtain separate licenses/permits to shift its attachments and/or add new attachments?
Municipal Roads:
  No, typically separate permits are not required for each attacher.
MassDOT Roads:
  Yes, each attacher must obtain its own separate permit for shifting existing attachments or adding new ones.

## Slide 7: Make-Ready Timelines
Municipal and MassDOT requirements significantly impact the duration of make-ready work, while survey work remains largely unaffected.
Survey Work:
  No impact from permitting requirements or moratoriums. Can proceed independently.
Simple Make Ready (e.g., cable rearrangement):
  Municipal: Generally less stringent permitting, potentially quicker turnaround.
  MassDOT: Requires permits, which can add some processing time.
Complex Make-Ready (e.g., new pole installation, pole replacement):
  Municipal: New pole requires a permit, varies from 2-3 month interval.
  MassDOT: Obtaining a permit typically has a 3-4 month interval.

## Slide 8: Approval Timelines with Mandatory Timelines
If agencies adopted mandatory timelines for survey and make-ready work, the time required for obtaining necessary approvals from MassDOT and/or municipalities for complete make-ready would typically be:
MassDOT: 3-4 month interval
Municipalities: 2-3 month interval (new pole)

## Slide 9: Municipal Requirements: Pole & Attachment Work
Public Hearings for Existing Pole Replacements:
  Municipalities do not require public hearings for the replacement of existing utility poles.
Public Hearings for Wireless Attachments:
  There have been cases where municipalities have required public hearings for new wireless attachments.
Limitations on Pole Heights:
  Verizon is not aware of any municipal limitations on increases to pole heights.

## Slide 10: Grants-of-Location: Restrictions on Attachments
Question: Do grants-of-location provided by municipalities for placing utility poles on public right-of-way include restrictions or requirements applicable to municipal or other attachments?
Answer: No