## Slide 1: Distributed Energy Resources Interconnection
Massachusetts
August 28, 2025

## Slide 2: Steps to Interconnection
Step One
Submit Application with Supporting Documents
Step Two
Application Processing
Step Three
System Installation
Step Four
Permission to Operate
Utilize PowerClerk to submit and manage your application
Unitil processes application through applicable process track
Applicant installs system and Utility completes system upgrades
Permission to Operate system is granted after system is installed and all approval conditions are met

## Slide 3: Application Submission
Applications are submitted online in the Unitil Interconnection Program Portal
Software used is PowerClerk
PowerClerk will assist you in entering the correct application and applicable supporting documents
URL for PowerClerk login page with instructions to register for new users
  https://unitil-eri.powerclerk.com/MvcAccount/Login
How to Submit your Application Package
How to Submit your Application Fee
Step One
Submit Application with Supporting Documents
Utilize PowerClerk to submit and manage your application
Check is the only payment method available
Check made out to Unitil with ERI # on memo line
Check is mailed to:
  Unitil DER Interconnections
  30 Energy Way
  Exeter, NH 03833

## Slide 4: Application Types
Listed Inverter Based Facilities Less Than or Equal to
  15 kW (AC) Single Phase
  25 kW (AC) Three Phase
  Area Network Exceptions May Apply
Simplified Application
Listed Facilities which do not qualify for Simplified Process
Expedited/Standard Application
Step One
Submit Application with Supporting Documents
Utilize PowerClerk to submit and manage your application
Pre-Application
Required for all applications 250 kW (AC) or larger prior to submission of an Expedited/Standard application
Optional for all applications smaller than 250 kW (AC)
Report containing non-binding information for the location of Facility
  Circuit Characteristics (e.g. Voltage at substation and location, phasing at location, distances to substation and stepdowns, loading)
  Substation Characteristics (e.g. Transformer rating, 3V0 status)
  Aggregate kW of in service and queued DER on the circuit and substation transformer

## Slide 5: Supporting Documents
Exhibit H - Agreement between Company (Unitil) and Retail Customer
  Exhibit I – Landowner Consent
  Exhibit A/C Attachment 1A and 1B – Landownership Self-Certification/Consent
  Schedule Z – Net Metering
  Energy Storage System Survey – ESS Questionnaire
Agreement, Consent, and Informational Forms
System One-Line or Three-Line Diagram
  Minimum Design Requirements outlined in Unitil Guideline for Design and Interconnection of Distributed Generation Section 4.2
  Site Plan
    Minimum Site Plan Requirements outlined in Unitil Guideline for Design and Interconnection of Distributed Generation Section 4.2
Facility Design Drawings
Step One
Submit Application with Supporting Documents
Utilize PowerClerk to submit and manage your application
Facility Equipment Specification Sheets
Manufacturers Technical Documentation for installed equipment (e.g. Inverter Data Sheets, Battery data sheets, Power Control Systems etc.)

## Slide 6: Application Fees
No Fee Required for Application
Simplified Application
Expedited/Standard Application
Step One
Submit Application with Supporting Documents
Utilize PowerClerk to submit and manage your application
Pre-Application
Tiered fee based on Facility size
$4.50/kW(AC) with $300 Minimum and $7,500 Maximum

## Slide 7: Application Processing
Processing Track Assigned
  Application type submitted determines initial processing track
Meter Inspection
  A Unitil employee will visit the location to inspect the existing metering
  Technical Screening
    Screening of the Facility is performed. Screens are technical in nature and vary in complexity based on Processing Track.
    If applicable - Supplemental Review and/or Impact Studies
      If initial technical screening fails or system upgrades can’t be determined by screening an enhanced screening and/or an impact study will be performed
      Enhanced screening is called a Supplemental Review and performed for a fee
      Impact Studies are performed for a fee. Standard Process Track bypasses screening and proceeds directly to impact study
      If applicable - Estimating for Unitil System Upgrades
        Technical Screens or Studies may identify upgrades to Unitil’s infrastructure are required to accommodate the DER
        Management Review and Approval
      Final results of technical screens, study reports, and/or estimates receive a final management review and followed by contingent Approval to Install
Steps Involved to Process an Application
Step Two
Application Processing
Unitil processes application through applicable process track

## Slide 8: Processing Tracks
Step Two
Application Processing
Unitil processes application through applicable process track
Simplified Track
  25-30 Business Days for Approval to Install
  Expedited Track
  45-65 Business Days for Approval to Install
  Standard Track
  135-160 Business Days for Approval to Install
Three Processing Tracks for Applications
Application type submitted determines the initial processing track
An application may be moved from one process track to another based on screening failures or other circumstances
Determining Process Track and Changing Process Track
Timeframes
Timeframes to process are net of Applicant hold periods. Exceptions apply to timeframes as outlined in MA Interconnection Tariff

## Slide 9: Technical Screening
Step Two
Application Processing
Unitil processes application through applicable process track
Simplified Track
Three qualification screens (i.e. the application meets Simplified Track criteria)
  Facility size is ≤15 kW (AC) Single Phase or ≤25 kW (AC) Three Phase
  Connecting to a radial distribution circuit (provisions for Simplified Area Network track)
  Listed Inverter based generator
Two additional screens
  Aggregate generation on circuit less than 15% of circuit peak load
  Service type – Verifies electric service is the correct type for the DER
Service Transformer Criteria
Service Type Screen will verify the service transformer can accommodate the DER
  Aggregate generation on the service transformer is 120% of nameplate or less
  Aggregate generation on the service transformer does not exceed 25 kW (AC) if there is a shared secondary
  Service Transformer Query Tool
  New PowerClerk feature for checking the service transformer rating and aggregate generation prior to submitting an application

## Slide 10: Technical Screening Cont.
Step Two
Application Processing
Unitil processes application through applicable process track
Expedited Track
Initial Screens
  Aggregate generation on circuit less than 15% of circuit peak load
  Listed Equipment
  Service type
  Starting Voltage Drop – Spinning Machines
  Fault Current Contribution
  Service Configuration
  Transient Stability – Known Concern
Enhanced Screens in Supplemental Review
  Penetration Test
  Power Quality and Voltage Test
  Safety and Reliability Test
  System Modifications Determined without Impact Study

## Slide 11: Impact Studies
Step Two
Application Processing
Unitil processes application through applicable process track
Standard Track
Distribution Impact Studies
  Performed on an Individual application or group of applications
  Study scope may include but is not limited to:
    Steady State Analysis – Voltage and Thermal
    Protection and Short Circuit Analysis
    Stability Analysis
    Risk of Islanding
    Facility Grounding
Affected System Operator Impact Studies
An Affected System Operator such as the owner of the Transmission System or ISO-NE may require an impact study of the transmission system.
Unitil will assist in coordinating as necessary. All related costs are Applicants responsibility

## Slide 12: System Modification Estimates
Step Two
Application Processing
Unitil processes application through applicable process track
System Modification Estimates
Technical Screening or Impact Studies may identify system modifications are required
  Estimates are +/- 25%
  Valid for 60 Days

## Slide 13: Management Review and Approval
Step Two
Application Processing
Unitil processes application through applicable process track
Final Review of the Application
Management review of the application package including applicable screening and study results takes place
Applicant receives Contingent Approval to Install once Management review is complete
    If system modifications are required the Contingent Approval to Install will be accompanied by an Interconnection Service Agreement (ISA).
    ISA will outline the required system modifications and applicable costs

## Slide 14: System Installation
Applicant installs system and Utility completes system upgrades
System Installation
Installation of the Facility can begin once the Contingent Approval to Install is received
Step Three
System Installation
System Modifications that are the responsibility of the applicant are addressed
  This typically involves addressing deficiencies identified during the Meter Inspection
Equipment labeling – Permanent
  Meter Socket – Net Meter Alternate Power Source
  AC Disconnect – Description of source being disconnected
Unitil System Upgrades
If applicable, Unitil will complete system modifications required to accommodate the DER
  Utility work does not begin until applicant pays for estimated costs related to system modifications

## Slide 15: Permission to Operate
Permission to Operate system is granted after system is installed and all approval conditions are met
Completion Documentation
After system installation is complete the following documentation is submitted to PowerClerk
  Certificate of Completion
  Photos to include
    Service meter and production meter if applicable. Capture meter number and labeling
    Disconnect Switches. Capture labeling
    Inverter Nameplate/s
    ESS Nameplates/s if applicable
    Wide view photo that captures all equipment
Witness Test
For certain Facilities a Witness Test will be required
Step Four
Permission to Operate
Net and Production Meter Set
After completion documentation is approved including the Witness Test if applicable appropriate metering will be installed
Permission to Operate
After appropriate metering is installed an Approval to Interconnect will be sent authorizing the Facility to commence operation

## Slide 16: Common Errors
Incorrect Account or Meter number
  Account and Meter number should come from a current electric bill
Incomplete Application Submission
Errors cause delays in processing the application and/or approving the Facility to begin operation
Impact of Errors
Incorrect Supporting Documentation
  Equipment Specification Sheets do not match the equipment in the application
  One-line and/or Site Plan do not include required details as outlined in the Unitil Guideline for Design and Interconnection of DG section 4.2 (e.g. driveway and street not labeled on site plan etc.)
Photo Quality
  Photos are out of focus and text can’t be read
Incomplete Completion Documentation Submission
Incorrect Equipment in Photos

## Slide 17: Additional Resources
Helpful resources located on Unitil’s website:
  MA Distributed Generation Interconnection Tariff
  MA Hosting Capacity Map
  Guideline for Design and Interconnection of Distributed Generation (Update Pending)
  Unitil Metering Requirements
  Unitil DER Website URL
    https://unitil.com/ways-to-save/solar-private-generation
    General Interconnection Questions
      Generator@Unitil.com
    Service Transformer Query Tool
      Located at the start of all application types in PowerClerk except pre-applications
Interconnection Resources
MA SMART Program
  SMART@Unitil.com
MA Net Metering
  https://www.mass.gov/net-metering
Programs

## Slide 18: Ongoing Efforts
Updates to the Model Interconnection Tariff
Interconnection Tariff
ESS Operational Tariff in development for ESS larger than 250kW
ESS Operational Tariff
PowerClerk Improvements – Feedback welcomed!
Unitil Efforts