## Slide 1: MassDEP
Massachusetts Water Works Association
Membership Meeting
March 15, 2018
Cyanobacteria &
Cyanotoxins:
What PWSs
should know
Photo Credit: G. Zoto, MassDEP

## Slide 2
Naturally occurring microorganisms (bacteria) formerly known as blue-green algae
Present in all waterbodies in low numbers
Cyanobacterial species number in the thousands
Single cells, thread-like filaments or colonies and groups
Grow as benthic or planktonic populations
Four most common cyanobacteria in Massachusetts
Cyanobacteria: The Basics
  Anabaena
  Aphanizomenon
Microcystis
Planktothrix

## Slide 3: Cyanobacteria: Blooms
Dramatic cyanobacteria increases can lead to cyanobacterial Harmful Algal Blooms (CyanoHABs)
May cause dissolved oxygen, taste and odor, public health issues
Discoloration

## Slide 8: Cyanobacteria: Misidentifications
  Pollen
  Paint or dye spills
  Duckweed
  Green algae

## Slide 9: CyanoHABs: Risk Factors
  Predominant Indicators
  Reduced flow/high residence time
  Wind
Potential for cyanobacterial blooms in waterbodies based upon environmental factors. |  |  |  | 
Bloom Risk level | History of Blooms | Water Temp oC | Total Phosphorous micrograms per liter (µg/L) | Thermal Stratification
Very low | No | <15 | <10 | Rare or never
Low | Yes | <15-20 | <10 | Infrequent
Moderate | Yes | 20-25 | 10-25 | Occasional
High | Yes | >25 | 25-100 | Frequent and persistent
Very high | Yes | >25 | >100 | Frequent and persistent/strong
Based on Newcombe et.al., 2010 |  |  |  | 

## Slide 10: Cyanotoxins
Cyanotoxins Produced
  Anabaena – Anatoxins, Microcystins, Saxitoxins
  Aphanizomenon – Saxitoxins, Cylindrospermopsins
  Microcystis – Microcystins
  Planktothrix – Anatoxins, Aplysiatoxins, Microcystins, Saxitoxins
Intracellular and Extracellular
Number of species that produce toxins is unknown
Cyanotoxin identification requires laboratory analysis

## Slide 11: Cyanotoxins: Exposure & Health Effects
Exposure Routes
  Dermal, oral and inhalation
Health Effects
Dermatological Effects & Illness
Hepatotoxins
Neurotoxins
Possible Reactions
  Rashes, abdominal pain, fever, vomiting, diarrhea, respiratory irritation, liver and kidney damage; and, and effects to the nervous system

## Slide 12
USEPA Human Health Risks to Cyanotoxins Exposure: https://www.epa.gov/nutrient-policy-data/health-and-ecological-effects#what1 |  | 
CYANOTOXINS | ACUTE HEALTH EFFECTS IN HUMANS | MOST COMMON CYANOBACTERIA PRODUCING TOXIN
Microcystin-LR | Abdominal pain, Headache, Sore throat, Vomiting and nausea, Dry cough, Diarrhea, Blistering around the mouth, and Pneumonia | Microcystis, Anabaena, Nodularia, Planktothrix, Fisherella, Nostoc, Oscillatoria, and Gloeotrichia
Cylindrospermopsin | Fever, Headache, Vomiting, Bloody diarrhea | Cylindrospermopsis raciborskii, Aphanizomenon flos-aquae, Aphanizomenon gracile, Aphanizomenon ovalisporum, Umezakia natans, Anabaena bergii, Anabaena lapponica, Anabaena planctonica, Lyngbya wollei, Rhaphidiopsis curvata, and Rhaphidiopsis mediterranea
Anatoxin-a group | Tingling, Burning, Numbness, Drowsiness, Incoherent speech, Salivation, Respiratory paralysis leading to death* | Chrysosporum (Aphanizomenon) ovalisporum, Cuspidothrix, Cylindrospermopsis, Cylindrospermum, Dolichospermum, Microcystis, Oscillatoria, Planktothrix, Phormidium, Anabaena flos-aquae, A. lemmermannii Raphidiopsis mediterranea (strain of Cylindrospermopsis raciborskii), Tychonema and Woronichinia
*Symptoms observed in animals. |  | 

## Slide 13: CyanoHABs: Regulations/Guidance
  US EPA Health Advisories (HAs)
  US EPA Required UCMR4 Monitoring
Massachusetts Department of Public Health (MDPH) Guidance (public beaches)
MassDEP Guidance for Public Water Systems (PWSs)
EMERGING ISSUE: NO current federal or Massachusetts regulations for cyanobacteria or cyanotoxins
Photo Credit: David Zapotosky

## Slide 14: US EPA DW Health Advisories
  Two (2) HAs - microcystins and cylindrospermopsin
Non-regulatory concentrations at or below which adverse health effects are not anticipated to occur by oral ingestion of DW over specific exposure durations.
US EPA DW Health Advisories |  | 
Cyanotoxin | US EPA 10-day HA | 
 | Bottle-fed infants & pre-school children | School-age children and adults
Microcystins | 0.3 µg/L | 1.6 µg/L
Cylindrospermopsin | 0.7 µg/L | 3 µg/L

## Slide 15: Cyanotoxins Monitoring: UCMR4
Cyanotoxins Sampling between 2018-2020
Ten (10) Cyanotoxins: total microcystins, microcystin-LA, microcystin-LF, microcystin-LR, microcystin-LY, microcystin-RR, microcystin-YR, nodularin, anatoxin-a, and cylindrospermopsin
Data from the UCMR serves as a primary source of research information, which US EPA utilizes to develop regulatory decisions.
Three (3) US EPA approved methods for drinking water
    EPA 544 (LC/MS/MS – MC/NOD)
    EPA 545 (LC/MS/MS – CYN/Ana)
    EPA 546 (ELISA – MC/NOD)
For further information on UCMR4 and cyanotoxins assessment monitoring, please see: https://www.epa.gov/dwucmr/fourth-unregulated-contaminant-monitoring-rule.

## Slide 16: Cyanobacteria: MDPH Guidance
MDPH has developed health-based guidance levels for recreational exposure to cyanobacteria.
MDPH recommends that beaches be posted and individuals limit all contact with a waterbody if the waterbody has
Online Photo Credit: US EPA
cyanobacteria cell counts exceeding 70,000 cells/milliliter (mL) or microcystin concentrations that meet or exceed 14 micrograms per liter (µg/L).

## Slide 17
Coming Soon: MassDEP Guidance
Collaborative Development
  MDPH, Office of Research and Standards (ORS)
  Regional DW Programs, Watershed Planning Program (WPP)
  Safe Drinking Water Act Advisory Committee (SDWAAC)
Watershed Management & Source Water Protection Focus
  Cyanobacteria/Cyanotoxin Information
  Critical factors for assessing source vulnerability
  Fact Sheet & PWS Bloom Tracking Form
  Treatment options
    In-reservoir & within treatment facility
  Additional resource materials and MassDEP contacts
Website Update & Internal/Interagency Protocols

## Slide 18
Helpful Resources
MA EOEEA Website:
https://www.mass.gov/guides/cyanobacterial-harmful-algal-blooms-cyanohabs-water
MDPH Website: https://www.mass.gov/lists/algae-information
US EPA Website: https://www.epa.gov/nutrient-policy-data/cyanohabs
University of New Hampshire Online Guide: http://cfb.unh.edu/CyanoKey/indexCyanoQuickGuide.htm

## Slide 19
SAFETY FIRST!

## Slide 20: CyanoHAB QUESTIONS/COMMENTS?
Kristin Divris
Water Utility Resilience Program (WURP)
DWP Emergency Preparedness & Security
kristin.divris@state.ma.us
508-849-4028
Contact Information