## Slide 1: Annual Toxics Reporting: Skills and Challenges
Jack Illingworth John Raschko
Office of Technical Assistance
Spring 2026 Reporting Workshop

## Slide 2: Before You Get Started
Make sure you know
Which chemicals are on the TURA & TRI reporting lists (use DEP’s Excel spreadsheet or the TRI GuideMe list)
What the reporting thresholds are for each chemical and chemical category (refer to DEP’s spreadsheet)
Gather all the data you need to quantify chemical use at your facility
Do not assume reporting done in the past was correct
Purchasing, storage, shipping and waste data
Current Safety Data Sheets (SDS)
Challenge assumptions made
Determine if additional sources of data are available
Which chemicals are PBT, HHS or LHS (refer to DEP’s spreadsheet)
Permit and emissions data

## Slide 3: Key differences between TURA and TRI reporting
Aspect of Reporting | Massachusetts TURA | US EPA TRI
Covered facilities (SIC) | 20-39 – Manufacturing 40-51 – includes Transportation, Communications, Wholesale Trade 72&73 – Personal & Business Services 75&76 – Repair Services | 20-39 – Manufacturing 40, 44-48, 50, 72 & 76 – Exempt 49 – Only coal burning (power & haz waste mgmt.) 51 – Only chemicals & allied products, petroleum bulk stations & terminals 73 – Only solvent recovery
Covered chemicals | Find the full list here: https://www.mass.gov/doc/complete-list-of-tura-chemicals/download = TRI-listed chemicals plus: CERCLA chemicals Ag, Cu, Ni, Cr, Co, Mn, Ag-Cu alloys only reportable when in aerosol form IPA and hydroquinone (only if mfd) Other TURA additions (e.g., C1-C4, crystalline silica, certain PFAS, etc.) | Find the full list here: https://www.epa.gov/toxics-release-inventory-tri-program/tri-listed-chemicals HCl and H2SO4 only reportable when in aerosol form
Report format | Form S + State-Only Form R/A for chemicals not reportable under TRI | Form R or Form A

## Slide 4: Important Reporting Practices
Evaluate chemicals previously reduced below thresholds in the previous year
Check for use of chemicals identified by different names/synonyms
Evaluate all processes where the chemical is used when determining the quantity of chemical use
Include water treatment or wastewater pretreatment chemicals (acids and bases)
Account for coincidentally manufactured chemicals

## Slide 5
Manufacture, Process or Otherwise Use?
Process
Prepare a toxic substance
after its manufacture.
Toxic chemical is intentionally incorporated in the product.
Toxic substance inputs and outputs
Product
inputs and outputs
Otherwise Use
Use a toxic substance in a way that it is not intentionally incorporated into the product (e.g., degreasing a machine)
Manufacture
Create a toxic substance:
Intentionally – to incorporate into the product (e.g., paint)
Unintentionally – either as part of the product, or as byproduct
Import the substance
Production Unit

## Slide 6: Production Unit
"A process, line, method, activity, or technique or a combination or series thereof, used to make a product“
Process or group of processes regarded as a distinct entity for the purpose of TUR planning AND reporting
Process Step 1
Process Step 2
Process Step 3
Production Unit 003
Chemical A
Chemical B

## Slide 7: Sulfuric Acid Use in Production and Waste Treatment
Anodizing Protection Inc. etches aluminum with sodium hydroxide and then anodizes the aluminum part using sulfuric acid. For reporting year 2023 the company reported a 14% increase in production from the previous year, using 130,000 pounds of sulfuric acid. 80,000 pounds was used in the anodizing production unit. 50,000 pounds of the sulfuric acid use was for pH neutralization in the wastewater pretreatment system. The company reported 57,000 pounds of byproduct for reporting year 2023. Assume the neutralization process is 100% efficient.
WHAT WAS THE COMPANY’S PRODUCTION RATIO?
IS THE MASS BALANCE COMPLETE?
  Create PFD and do some math (mass/materials balance)

## Slide 8: Anodize Production Unit Process Flow & Chemical Pathway Analysis
Etch
Countercurrent Rinse
Anodize
Countercurrent Rinse
Wastewater pretreatment system
Production Unit 1
NaOH
H2SO4
80,000 lb
H2SO4
50,000 lb
Given: Byproduct from Production Unit = R1+ R2 = 0 + 57,000 lb H2SO4
H2O
H2O
Facility Boundary
R1
R2
Remember: Under TURA, byproduct is the amount of chemical that leaves the production unit that is not in product

## Slide 9: Calculations for completing Form S
Section 1: Facility-Wide Use
1.e - Otherwise Used= 130,000 lb (given)
1.f - Byproduct = 57,000 lb (given)
Section 2: Materials Balance (around Production Unit)
Input = 80,000 lb (given)
Output = byproduct = 57,000 lb
2.d - Consumed or Transformed = 80,000 – 57,000 = 23,000 lb
Section 3: Chemicals Used in Waste Treatment Units
3.b – Amount = 50,000 lb (given)
Mass Balance
Input = output + amount consumed/transformed

## Slide 10: Form S Reporting: Facility-Wide Use of Sulfuric Acid
Section 1 (facility-wide use)
Manufactured: 0
Processed: 0
Otherwise Used: 130,000
Generated as Byproduct: 57,000
Shipped in or as Product: 0
Production or Activity Ratio: 1.14
Section 3 (chem used in waste treatment units)
Is chemical used to treat waste or control pollution? Yes
Enter amount: 50,000
Section 2 (materials balance)
Chemical Recycled Onsite: 0
Consumed or Transformed: 23,000
Chemical (Product) Held in Inventory: 0
Chemical Compound: 0
Other: 0
“Yes” if anything non-routine occurred at your facility during the reporting year that affected the data reported, if there is not a materials balance, and/or if the Prod. Ratio is <0.5 or >2.
Yes No
Mass Balance: 1c+d+e = 1f+1g+2a+b+c+d+e + 3b

## Slide 11: Commonly Missed in Reports
Higher Hazard Substances (HHS) - 1,000 lb threshold
Use of PBTs and PFAS – there is no de minimis level
Chemical Categories
Differences in TRI and TURA reporting lists of chemicals & covered facilities
Wastewater treatment and cleaning chemicals
New listings for Current RY
Coincidently manufactured chemicals, for example:
  Do you use nitric acid? (8.48 M lb HNO3 used in 2024)
  Water dissociable nitrate compounds (8.71 M lb Nitrate compounds reported in 2024)

## Slide 12: Some Differences Between TRI and TURA Reporting
Reporting of Hydrochloric Acid and Sulfuric Acid
TRI – only aerosol forms
TURA – both aerosol and non-aerosol forms
CERCLA chemicals (not TRI chemicals)
Sodium Hydroxide & Potassium Hydroxide (56.39 M lb NaOH, 17.1 M lb KOH used in 2024)
Bleach (Sodium Hypochlorite) (36.3 M lb NaOCl used in 2024)
Acetone - TRI delisted in 1993 (12.93 M lb acetone used in 2024)
Benzoic Acid (0.34 M lb benzoic acid reported in 2024)
Ferrous Sulfate – is LHS (no chemical fee) (0.21 M lb ferrous sulfate used in 2024)
Ferric chloride – is LHS (no chemical fee) (5.75 M lb ferric chloride used in 2024)
Paraformaldehyde – is not formaldehyde (has 25,000 lb. threshold) (0.09 M lb para used in 2024)
TURA HHS have 1000 lb threshold
https://www.mass.gov/doc/designation-of-tura-higher-and-lower-hazard-substances-in-massachusetts/download
(29.53 M lb HCl used in 2024)
(18.43 M lb H2SO4 used in 2024)

## Slide 13: Pay attention …
TDI is a Higher Hazard Substance
  Report each CAS# individually
2,4-Toluene diisocyanate
  2,4-TDI
  CAS 584-84-9
2,6-Toluene diisocyanate
  2,6-TDI
  CAS 91-08-7
TDI mixed isomers
  CAS 26471-62-5
Formaldehyde has several synonyms:
  Formalin
  Formol
  Methylene glycol
  Methyl aldehyde
  Methylene oxide
eDEP only gives you one (or maybe two) chemical synonyms, so it’s up to you to check against CAS #

## Slide 14: Persistent Bio-Accumulative Toxics (PBTs)
U.S. EPA PBTs are automatically designated as HHS by 2007 TURA Amendments. These chemicals have no de minimis and have lower reporting thresholds. Here’s a partial list of PBTs:
PBT Chemical | Threshold | 2024 Use Reported
Dioxin and dioxin-like compounds | 0.1 grams | 775 gram
Mercury and mercury compounds | 10 pounds | 7,850 lb Hg; 913 lb Hg cmpds
Benzo (g,h,i) perylene | 10 pounds | 3,440 lb
Hexachlorobenzene | 10 pounds | 0 lb
Polychlorinated Biphenyls (PCBs) | 10 pounds | 78K lb
Lead and lead compounds | 100 pounds | 2.63M lb Pb; 0.81M Pb cmpds
Polycyclic Aromatic Compounds (PACs) category (25 listed chems) | 100 pounds | 184,000 lb
Tetrabromobisphenol A | 100 pounds | 1,170 lb
Hexabromocyclododecane (HBCD) category | 100 pounds | 0 lb

## Slide 15: Chemical Categories – Some are HHS or PBTs – Different Thresholds
  Nickel, Silver, Zinc, Copper & Antimony Compounds Categories (25,000 lb. threshold)
  Cadmium, Cyanide & Hexavalent Chromium Compounds Categories (1,000 lb. threshold)
    Use DEP Category # 1216 for Cr (VI) compounds (total compound weight towards threshold 1,000 lb. threshold)
    Use DEP Category # 1217 for Non-Cr (VI) compounds (25,000 lb. threshold)
  Lead Compounds (100 lb. threshold)
(0.2 M lb Ni & Ni cmpds)
(0.31 M lb Ag & Ag cmpds)
(3.2 M lb Cu & Cu cmpds)
(2.4 M lb Sb & Sb cmpds)
(0.1 M lb Cd & Cd cmpds)
(0.08 M lb CN & CN cmpds)
(0.05 M lb Cr+6 cmpds)
(0.81 M lb Pb cmpds)

## Slide 16: Ammonia Reporting (CAS# 7664-41-7) (10.7 M lb used in 2024)
Anhydrous Ammonia (NH3)
The total quantity of the anhydrous ammonia manufactured, processed, or otherwise used is reportable.
When calculating byproduct, it’s the total amount of anhydrous ammonia that is released, transferred, or otherwise managed.
Aqueous Ammonia
From NH4OH & water dissociable ammonium salts in water
Use = 10 percent of the total quantity of the aqueous ammonia manufactured, processed, or otherwise used.
Byproduct = 10 percent of the total quantity of aqueous ammonia released, transferred, or otherwise managed.
TUR Reporting Appendices (page 112)
EPA Reporting Guidance

## Slide 17: Ammonia Reporting (cont’d)
Threshold Determination example (from EPA Ammonia Guidance)
In a calendar year, a facility places 25,000 pounds of anhydrous ammonia in water for processing and processes 25,000 pounds of aqueous ammonia from an ammonium salt –
Include all the 25,000 pounds of anhydrous ammonia in the determination of the processing threshold,
Include only 10 percent (or 2,500 pounds) of the aqueous ammonia from the ammonium salt in the processing threshold determination.

## Slide 18: Ammonia Reporting (cont’d)
Key Sections of EPA’s Ammonia Reporting Guidance
Section 1: Introduction
  Section 1.2: De Minimis Concentrations - ammonia listing is subject to the one percent de minimis concentration.
Section 2: Guidance for Reporting Aqueous Ammonia
  Section 2.1: Determining Threshold and Release Quantities for Ammonia
  Section 2.2: Chemical Sources of Aqueous Ammonia
    Section 2.2.1: Reporting Aqueous Ammonia Generated from Anhydrous Ammonia in Water
    Section 2.2.2: Reporting Aqueous Ammonia Generated from the Dissociation of Ammonium Salts (Other Than Ammonium Nitrate)
    Section 2.2.3: Reporting Aqueous Ammonia Generated from the Dissociation of Ammonium Nitrate
Section 3: CAS Number List of Some Chemical Sources of Aqueous Ammonia

## Slide 19: Coincidentally Manufactured Water-Dissociable Nitrate Compounds (8.71 M lb manufactured in 2024)
  Nitric acid (HNO3) neutralization can manufacture water dissociable Nitrate Compounds above reporting thresholds even though <25,000 pounds of HNO3 treated
Calculating the amount of nitric acid that must be neutralized to generate 25,000 lb nitrate compounds:
=
X = 18,529 lb (Form S reportable!)
HNO3 + NaOH  NaNO3 + H2O
Molecular Weights
63
85
TUR Reporting Appendices (page 87)
EPA Reporting Guidance

## Slide 20: Rules for Reporting Individual CERCLA Chemicals and EPCRA Chemical Categories
If a specific chemical is part of an EPCRA Category
AND
The same chemical is a specifically listed CERCLA chemical
REPORT AS PART OF THE EPCRA CATEGORY
Refer to
Excel list of reportable chemicals on DEP’s website to determine how to report
TURA Reporting Appendices - Rules for Reporting Specifically Listed Chemicals vs. Chemical Categories
TUR Reporting Appendices (page 164)

## Slide 21: Rules for Reporting Elemental Metals & Their Metal Compounds Category
If lead is used in excess of 100-pound threshold
AND
Lead compounds are used in excess of 100-pound threshold
REPORT BOTH THE LEAD AND THE LEAD COMPOUNDS AS LEAD COMPOUNDS ON THE SAME REPORTING FORM
Pay only 1 fee

## Slide 22: Lead & Lead Compounds Reporting
Boards Etc. is a contract circuit board assembler. The company attaches components to customer-supplied circuit boards via wave soldering. In reporting year 2025, the company used tin-lead solder that contained 3,354 pounds of lead. That same year they sent solder dross (containing 1,715 pounds of reportable lead compounds) off-site for recycling and received a statement back from its recycler that 1,588 pounds of lead were recovered from the dross. The amount of lead that was shipped out with the customer product was 1,766 pounds. Production of circuit boards increased by 10% from 2024 to 2025.
WHAT'S THE PRODUCTION RATIO?
HOW MUCH LEAD AND LEAD COMPOUNDS WERE USED?
HOW MUCH BYPRODUCT GENERATED?
Wave Soldering
Components
Circuit boards
Assembled circuit boards
(1,766 lb Pb)
Tin-Lead Solder
(3,354 lb Pb)
Solder Dross
(1,715 lb Pb compounds containing 1,588 lb Pb)

## Slide 23: Form S Reporting: Facility-Wide Use of Lead & Lead Compounds Note, use DEP CAS 1026 for lead compounds (1a)
Section 1
Manufactured: ?
Processed: 3,354
Otherwise Used: 0
Generated as Byproduct: ?
Shipped in or as Product: 1,766
Production or Activity Ratio: ?
Section 2
Chemical Recycled Onsite: 0
Consumed/Transformed: 1,588
Chemical (Product) Held in Inventory: 0
Chemical Compound: 127
Other: 0
“Yes” if anything non-routine occurred at your facility during the reporting year that affected the data reported, if there is not a materials balance, and/or if the Prod. Ratio is <0.5 or >2.
Yes No
1,715
1.1
1,588
Does this balance? Yes
Wave Soldering
Components
Circuit boards
Assembled circuit boards
(1,766 lb Pb)
Tin-Lead Solder
(3,354 lb Pb)
Solder Dross
(1,715 lb Pb compounds containing 1,588 lb Pb)
Mass Balance: 1c+d+e = 1f+1g+2a+b+c+d+e + 3b

## Slide 24
Process Flow and Materials Accounting Balance for Annual TURA Report
(assuming 12 batches of recycling cycle per year)
Non-Integral Recycling On Site Example
TUR Reporting Appendices (page 244)
Recycling Unit
Recycled Chemical
Production Unit
Release into Air 20,000 lbs. Byproduct
Virgin TURA Chemical Input
25,000 lbs.
otherwise used
145,000 lbs. recycled chemical
Ship out for off-site disposal
5,000 lbs.
Report as production unit use,
Not as facility-wide use
Drums wheeled to and from recycling unit
Conduct material balance around the production unit

## Slide 25: Non-Integral Recycling Example – Form S Section 1
Manufactured: 0
Processed: 0
Otherwise Used: 25,000
Generated as Byproduct: 170,000
Shipped in or as Product: 0
Production Unit
Release into Air 20,000 lb
Chemical Input
25,000 lb
otherwise used
145,000 lb recycled chemical
?
Material Balance: Inputs = Outputs
Production Unit Material Balance:
25,000 + 145,000 = 20,000 + ?
? = 170,000 – 20,000 = 150,000
Remember:
Byproduct is what leaves the production unit
Emissions are what leave the facility
Byproduct = 20,000 + 150,000 = 170,000 lb

## Slide 26: Do I Trip a Reporting Threshold for Hydrogen Fluoride?
Do you use hundreds of pounds of HF every year? (408,400 lb HF reported in 2024)
Do you use hundreds of pounds of ammonium bifluoride (ABF) or other fluoride salts every year?
  When dry ABF contacts water, it generates HF. The hydrogen fluoride derived from fluoride salts (such as ABF) is considered manufactured. (EPA guidance 745-R-00-005)
  When the manufactured HF is used to etch a metal, its otherwise use is counted at the production unit level but not reported as otherwise use at the facility-wide level
  ABF is also a reportable chemical (66,400 lb ABF reported in 2024)
  AND – ammonia formed when ABF dissolves in water may also be reportable
To determine whether you trip the 1,000-pound TURA reporting threshold for HF, review the MassDEP Guidance on Reporting Hydrofluoric Acid as a Higher Hazard Substance under the Toxics Use Reduction Act
TUR Reporting Appendices (page 107)

## Slide 27: Do You Use Cyanide Compounds?
Do you use hundreds of pounds of cyanide salts every year?
Do you plate hundreds of pounds of metal each year using a cyanide plating bath?
  82,600 lb cyanide compounds used in 2024
To determine whether you trip the 1,000-pound TURA reporting threshold for Cyanide Compounds (TURA chemical category # 1016), review the MassDEP Guidance on Quantifying Use and Reporting Cyanide Compounds
TUR Reporting Appendices (page 103)

## Slide 28: TURA & TRI Reporting Resources
TURA Reporting –
  Toxics Use Reduction Reporting Instructions
  Toxics Use Reduction Reporting Instructions Appendices
  Complete List of TURA Chemicals
  eDEP/TURA Online Filing Line by Line TIPS
TRI Reporting -
  TRI Homepage
  EPA TRI Reporting Guidance Documents
  Reporting for TRI Facilities - includes TRI chemical list, list of covered
  Sectors, TRI reporting software (TRI-MEweb), and number of guidance
  materials.

## Slide 29: Contact Us
Jack Illingworth
john.illingworth@mass.gov
(617) 997-6653
John Raschko
john.raschko@mass.gov
(617) 455-5452
mass.gov/ota