The Commonwealth of Massachusetts

Executive Office of Health and Human Services

Department of Public Health

Bureau of Environmental Health

Community Sanitation Program

5 Randolph Street

Canton, MA 02021

Telephone: 781-828-7910

Facsimile: 781-828-7703

lauren.molotnikov@state.ma.us

DEVAL L. PATRICK GOVERNOR TIMOTHY P. MURRAY LIEUTENANT GOVERNOR JUDYANN BIGBY, MD SECRETARY JOHN AUERBACH COMMISSIONER

January 26, 2011

Lynn M. Bissonette, Superintendent

MCI Framingham

P.O. Box 9007

99 Loring Drive

Framingham, MA 01704

Re: Facility Inspection

Dear Superintendent Bissonette:

In accordance with M.G.L. c. 111, §§ 5, 20, and 21, and Department of Public Health Regulations 105 CMR 451.000: Minimum Health and Sanitation Standards and Inspection Procedures for Correctional Facilities; 105 CMR 480.000: Storage and Disposal of Infectious or Physically Dangerous Medical or Biological Waste (State Sanitary Code, Chapter VIII); 105 CMR 590.000: Minimum Sanitation Standards for Food Establishments (State Sanitary Code Chapter X); the 1999 Food Code; and 105 CMR 205.000 Minimum Standards Governing Medical Records and the Conduct of Physical Examinations in Correctional Facilities; I conducted an inspection of MCI Framingham on January 19 and 20, 2011 accompanied by Chris Lakey, Director of Security, Chris Lanoue, Director of Engineering, and Pamela Britt, Fire Safety and Environmental Health Officer. Violations noted are listed below (* indicates conditions documented on previous inspection reports).

Smith Building

Lobby Area

105 CMR 451.345	Illumination in Common Passage Ways and Areas: Inadequate lighting, several light 	fixtures not functioning properly

105 CMR 451.353	Interior Maintenance: Water fountain drain dirty

Women’s Bathroom C133A

105 CMR 451.123*	Maintenance: Ceiling vent dirty

Men’s Bathroom C141A

105 CMR 451.123	Maintenance: Ceiling vent dirty

105 CMR 451.123	Maintenance: Floor dirty under sink fixture

Janitor’s Closet

No Violations Noted

Officer’s Area

Break Room

No Violations Noted

Men’s Locker Room

No Violations Noted

Women’s Locker Room

No Violations Noted

Inside Control

Lower Control

No Violations Noted

Upper Control

FC 4-204.112(A)	Design and Construction, Functionality: No functioning thermometer in refrigerator

FC 4-601.11(c)	Cleaning of Equipment and Utensils, Objective: Non-food contact surface dirty, 	gasket dirty

Slop Sink Room

105 CMR 451.353	Interior Maintenance: Wet mop left in bucket

P Trap

No Violations Noted

Inmate Bathroom 103A

105 CMR 451.123	Maintenance: Toilet seat not easily cleanable

Admissions

Storage Room C104A

105 CMR 451.350	Structural Maintenance: Floor tiles missing

Inmate Break Room 105A

No Violations Noted

Office C106A

105 CMR 451.353	Interior Maintenance: Ceiling insulation not secure properly

Staff Bathroom 106A

105 CMR 451.124*	Water Supply: Insufficient water supply in quantity and pressure at water fountain on 	handwashing sink

Storage Room 107A

No Violations Noted

Transportation Office 108A

No Violations Noted

Officer’s Room C108A

No Violations Noted

Medical Room 109A

No Violations Noted

Inmate Shower 110A

105 CMR 451.353	Interior Maintenance: Floor finish damaged

Inmate Shower 111A

No Violations Noted

Control Room 112A

105 CMR 451.350	Structural Maintenance: Ceiling leak observed near ceiling vent

Mechanical and Laundry Room 136A

105 CMR 451.353	Interior Maintenance: Strong odor observed in room

Search Room 115A & 116A

No Violations Noted

Holding Cells 117A-120A

No Violations Noted

Visiting Area

Common Area

105 CMR 451.345	Illumination in Common Passage Ways and Areas: Inadequate lighting, several light 	fixtures not functioning properly

Inmate Bathroom C138A

No Violations Noted

Janitor’s Closet

105 CMR 451.353	Interior Maintenance: No light shield provided in maintenance area

Women’s Bathroom

No Violations Noted

Men’s Bathroom

105 CMR 451.123	Maintenance: Changing table damaged and no longer easily cleanable

Visitation Play Area

No Violations Noted

Smith Food Service

Kitchen

FC 3-501.16(B)	Limitation of Growth of Organisms, Temperature and Time Control: Refrigerator 	temperature recorded at 500F

FC 4-204.112(A)	Design and Construction, Functionality: No functioning thermometer in refrigerator

FC 4-501.11(A)	Maintenance and Operation, Equipment: Equipment not maintained in a state of good 	repair, refrigerator gasket damaged

FC 4-501.11(B)*	Maintenance and Operation, Equipment: Equipment not maintained in a state of good 	repair, kick plate missing from refrigerator unit

FC 5-202.12(A)*	Plumbing System, Design: Handwashing sinks water temperature recorded at 490F

FC 6-501.12(A)	Maintenance and Operation; Cleaning: Facility not cleaned properly, interior surfaces 	of secured utensil storage cabinet dirty

Dinning Room

FC 6-501.11	Maintenance and Operation; Repairing: Facility not in good repair, floor tiles 	damaged near doorway

FC 6-501.11	Maintenance and Operation; Repairing: Facility not in good repair, base board 	damaged

FC 6-501.12(A)	Maintenance and Operation; Cleaning: Facility not cleaned properly, vent dirty

Smith Hallway

Smith Clinic

No Violations Noted

Janitor’s Closet C102

No Violations Noted

Staff Bathroom C131

No Violations Noted

Staff Bathroom C154

105 CMR 451.123	Maintenance: Ceiling vent dirty

105 CMR 451.126	Hot Water: Hot water temperature recorded at 1350F

Multi-Purpose Room

No Violations Noted

Smith Galleries

No Violations Noted

ATU East

Common Area

105 CMR 451.350*	Structural Maintenance: Ceiling damaged due to leaking Roof near cell # 217, 218, 	220, and 221

105 CMR 451.353	Interior Maintenance: Baseboard damaged near cell # 217

Storage Room C129

No Violations Noted

Day Room C130

105 CMR 451.353	Interior Maintenance: Table tops damaged and no longer easily cleanable

Break Room C124

No Violations Noted

Office C136

No Violations Noted

Lower Level Janitor’s Closet

No Violations Noted

Lower Level Showers

No Violations Noted

Upper Level Janitor’s Closet

No Violations Noted

Upper Levels Showers

105 CMR 451.123	Maintenance: Floor paint damaged in shower unit # C210, C211, and C212

105 CMR 451.123	Maintenance: Wall paint damage in shower unit # C210, C211, and C212

105 CMR 451.123	Maintenance: Door rusted in shower unit # C210, C211, and C212

105 CMR 451.123	Maintenance: Light fixture not functioning properly in shower unit # C211

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, shower head leaking in shower

# C210

Cells

105 CMR 451.353	Interior Maintenance: Ceiling paint damaged in cell # 120

ATU West

Common Area

105 CMR 451.350	Structural Maintenance: Ceiling damaged near cell # 139

Storage Room

No Violations Noted

Day Room

No Violations Noted

Office C141

FC 3-501.16(B)	Limitation of Growth of Organisms, Temperature and Time Control: Refrigerator 	temperature recorded at 450F

Lower Level Janitor’s Closet

No Violations Noted

Lower Level Showers

105 CMR 451.123	Maintenance: Wall paint damage in shower unit # C145

105 CMR 451.123	Maintenance: Floor paint damaged in shower unit # C145

105 CMR 451.123	Maintenance: Shower curtain damaged

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, tub faucet leaking

Upper Level Janitor’s Closet

No Violations Noted

Upper Level Showers

Under Renovation at the Time of Inspection

Cells

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, no hot water provided to cell

# 132

New Line

Common Area

No Violations Noted

Storage Room C155

No Violations Noted

Day Room C153

105 CMR 451.353	Interior Maintenance: Vent dirty

Office C161

No Violations Noted

Lower Level Janitor’s Closet

105 CMR 451.130	Plumbing: Bell cap missing from backflow preventer on slop sink

Lower Level Showers

No Violations Noted

Upper Level Janitor’s Closet

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, faucet loose

Upper Level Showers	Two showers occupied at the time of inspection

105 CMR 451.123	Maintenance: Wall paint damaged in right shower

Cells

105 CMR 451.353	Interior Maintenance: Ceiling paint loose in shower unit # 149, 157, 158, and 159

CCU

Common Area

No Violations Noted

Storage Room C109

No Violations Noted

Inmate Break Room and Storage Room

FC 4-501.11(A)	Maintenance and Operation, Equipment: Equipment not maintained in a state of good 	repair, refrigerator gasket damaged

Office

No Violations Noted

Medical Room

No Violations Noted

Lower Level Janitor’s Closet

105 CMR 451.345	Illumination in Common Passage Ways and Areas: Inadequate lighting, light 	fixture not functioning properly and bulb missing

Lower Level Showers

105 CMR 451.126	Hot Water: Hot water temperature recorded at 1150F

Upper Level Janitor’s Closet

No Violations Noted

Upper Level Showers

105 CMR 451.123	Maintenance: Light fixture not functioning properly in shower unit # C207

Cells

105 CMR 451.353	Interior Maintenance: Ceiling paint damaged in cell # 103 and 106

105 CMR 451.353	Interior Maintenance: Desk paint damaged in cell # 210

Second Floor Office Area

Bathroom C210A

No Violations Noted

Bathroom C211A

No Violations Noted

Janitor’s Closet C237A

105 CMR 451.345	Illumination in Common Passage Ways and Areas: Inadequate lighting, light 	fixture not functioning properly

Office 208A

105 CMR 451.353	Interior Maintenance: Ceiling vents dirty

Break Room C218A

No Violations Noted

HSU Building

Second Floor

Medical Room 2

105 CMR 451.353	Interior Maintenance: Vent dirty

Optometry Room	Locked at the time of inspection

Residential Treatment Unit	Locked at the time of inspection

Ob-Gyn Exam Room

105 CMR 451.344	Illumination in Habitable Areas: Inadequate lighting, one light fixture not functioning 	properly

Project Catch the Hope

No Violations Noted

CPOs Office

No Violations Noted

Barton Housing Unit

Hallway

No Violations Noted

Janitor’s Closet

105 CMR 451.353	Interior Maintenance: Ceiling dirty

Library

No Violations Noted

Day Room

105 CMR 451.353	Interior Maintenance: Table top damaged

FC 3-501.16(B)	Limitation of Growth of Organisms, Temperature and Time Control: Refrigerator 	temperature recorded at 500F

FC 4-204.112(A)	Design and Construction, Functionality: No functioning thermometer in refrigerator

Activity Room

No Violations Noted

Shower Room

105 CMR 451.123	Maintenance: Floor grout missing

Kitchenette

No Violations Noted

Cells

105 CMR 451.350	Structural Maintenance: Floor tile missing in cell # 204

105 CMR 451.350	Structural Maintenance: Door window damaged in cell # 220

First Room

Medical Records Room

105 CMR 451.344	Illumination in Habitable Areas: Inadequate lighting, several light fixtures not 	functioning properly

105 CMR 451.353	Interior Maintenance: One light shield missing

Medical Records Break Room

No Violations Noted

HSU Unit

Office

No Violations Noted

Office Bathroom

105 CMR 451.330	Room Temperature: Room temperature 510F in bathroom

Nurses’ Station

105 CMR 451.353	Interior Maintenance: Ceiling vent dirty

Detox Room 114

105 CMR 451.322*	Cell Size: Inadequate floor space in dorm room

Medical Cells

105 CMR 451.322	Cell Size: Inadequate floor space in dorm rooms

Doctor’s Office 110

105 CMR 451.110(B)*	Hygiene Supplies at Toilet and Handwash Sink: No waste receptacle at handwash sink

105 CMR 451.123*	Maintenance: Hot water control missing from sink fixture

105 CMR 451.126	Water Supply: No hot water supplied to handwash sink

Search and Interview Room

No Violations Noted

Shower Room

105 CMR 451.123	Maintenance: Soap scum on walls in shower units

Biohazard Room

No Violations Noted

Laundry Room

105 CMR 451.353	Interior Maintenance: Floor tiles missing

105 CMR 451.383(B)	Fire Safety System: Facility not in compliance with 780 CMR Massachusetts Building Code provisions for fire safety, storage less than 18 inches from ceiling

Clinical Area

Waiting Area

105 CMR 451.353	Interior Maintenance: Ceiling rusted

Nurses’ Bathroom

105 CMR 451.123	Maintenance: Ceiling vent dirty

Inmate Bathroom

105 CMR 451.123	Maintenance: Ceiling vent dirty

105 CMR 451.110(A)	Hygiene Supplies at Toilet and Handwash Sink: No toilet paper on holder

X-Ray Room # 1

105 CMR 451.344	Illumination in Habitable Areas: Inadequate lighting, one light fixture not functioning 	properly

Dental Room # 2

105 CMR 451.126	Hot Water: Hot water temperature recorded at 950F

105 CMR 451.350	Structural Maintenance: Ceiling tiles missing

Nurses’ Break Room

No Violations Noted

Trauma Room # 4

105 CMR 451.350	Structural Maintenance: Wall damaged above air conditioner unit

105 CMR 451.344	Illumination in Habitable Areas: Inadequate lighting, one light fixture not functioning 	properly

Trauma Room # 6

105 CMR 451.344	Illumination in Habitable Areas: Inadequate lighting, one light fixture not functioning 	properly

105 CMR 451.350	Structural Maintenance: Floor tiles damaged

Lab #7

No Violations Noted

Treatment Room # 8

No Violations Noted

Treatment Room # 9

No Violations Noted

Treatment Room # 10

No Violations Noted

RN Clinic # 11

105 CMR 451.350	Structural Maintenance: Floor tiles missing

FC 4-204.112(A)	Design and Construction, Functionality: No functioning thermometer in refrigerator

Cottages

Laurel Building

105 CMR 451.330	Room Temperature: Room temperature inconsistent throughout the cottage, room 	temperature measured in excess of 800F in some areas

105 CMR 451.350*	Structural Maintenance: Windows not weather tight and structurally sound throughout 	the cottage

Common Area

105 CMR 451.353	Interior Maintenance: Ceiling panels not installed properly in several areas

Officer’s Room

No Violations Noted

Kitchenette

105 CMR 451.126	Hot Water: Hot water temperature recorded at 1700F

Refrigerator Room

FC 3-501.16(B)	Limitation of Growth of Organisms, Temperature and Time Control: Refrigerator 	temperature recorded at 450F and freezer temperature recorded at 360F

Slop Sink Room (A)

No Violations Noted

Storage Room (A)

No Violations Noted

Dog Supply Storage Room (A)

No Violations Noted

Interview Room (A)

No Violations Noted

Caustic Room (C)

No Violations Noted

Shower Room A & B

105 CMR 451.123	Maintenance: Floor finish damaged in shower stall # 2 and 3

105 CMR 451.130*	Hot Water: Shower water temperature recorded at 1360F

Shower Room B & C

105 CMR 451.130*	Hot Water: Shower water temperature recorded at 1360F

Hallway A Cells

105 CMR 451.353	Interior Maintenance: Ceiling covered with plastic in an attempt to control the room 	temperature in several cells

Hallway B Cells

105 CMR 451.353	Interior Maintenance: Ceiling covered with plastic in an attempt to control the room 	temperature in several cells

Hallway C Cells

105 CMR 451.353	Interior Maintenance: Ceiling covered with plastic in an attempt to control the room 	temperature in several cells

Algon Building

105 CMR 451.330	Room Temperature: Room temperature inconsistent throughout the cottage, room 	temperature measured in excess of 800F in some areas

105 CMR 451.350*	Structural Maintenance: Windows not weather tight and structurally sound throughout 	the cottage

Common Area

105 CMR 451.353	Interior Maintenance: Ceiling panels not installed properly in several areas

Officer’s Room

No Violations Noted

Kitchenette

FC 4-501.114(C)(2)	Maintenance and Operation; Equipment: Quaternary ammonium solution greater than 	the manufacturers recommended concentration

Refrigerator Room

FC 4-204.112(A)	Design and Construction, Functionality: No functioning thermometer in refrigerator

Slop Sink Room (A)

105 CMR 451.353	Interior Maintenance: Floor finish damaged

Kaivac Machine Storage Room (A)

105 CMR 451.353	Interior Maintenance: Vent dirty

105 CMR 451.353	Interior Maintenance: Floor dirty

Storage Room (A)

No Violations Noted

Interview Room (A)

No Violations Noted

Caustic Room (C)

No Violations Noted

Shower Room A & B	Occupied at the time of inspection

Shower Room B & C

105 CMR 451.130	Hot Water: Shower water temperature recorded at 1150F

Hallway A Cells

105 CMR 451.353	Interior Maintenance: Ceiling covered with plastic in an attempt to control the room 	temperature in several cells

Hallway B Cells

105 CMR 451.353	Interior Maintenance: Ceiling covered with plastic in an attempt to control the room 	temperature in several cells

Hallway C Cells

105 CMR 451.353	Interior Maintenance: Ceiling covered with plastic in an attempt to control the room 	temperature in several cells

Town Line Building

105 CMR 451.330	Room Temperature: Room temperature inconsistent throughout the cottage, room 	temperature measured in excess of 800F in some areas

105 CMR 451.350*	Structural Maintenance: Windows not weather tight and structurally sound throughout 	the cottage

Common Area

105 CMR 451.353	Interior Maintenance: Ceiling panels not installed properly in several areas

Officer’s Room

No Violations Noted

Kitchenette

FC 4-501.114(C)(2)	Maintenance and Operation; Equipment: Quaternary ammonium solution greater than 	the manufacturers recommended concentration

Refrigerator Room

No Violations Noted

Slop Sink Room (A)

No Violations Noted

Storage Room (A)

No Violations Noted

Office (A)

No Violations Noted

Correctional Recovery Academy (A)

No Violations Noted

Caustic Room (C)

No Violations Noted

Shower Room A & B

105 CMR 451.123	Maintenance: Lower wall and floor finish damaged

Shower Room B & C	Occupied at the time of inspection

Hallway A Cells

105 CMR 451.353	Interior Maintenance: Ceiling covered with plastic in an attempt to control the room 	temperature in several cells

Hallway B Cells

105 CMR 451.353	Interior Maintenance: Ceiling covered with plastic in an attempt to control the room 	temperature in several cells

105 CMR 451.353	Interior Maintenance: Ceiling paint damaged in cell # 21

Hallway C Cells

105 CMR 451.353	Interior Maintenance: Ceiling covered with plastic in an attempt to control the room 	temperature in several cells

Pioneer Building

105 CMR 451.330	Room Temperature: Room temperature inconsistent throughout the cottage, room 	temperature measured in excess of 800F in some areas

105 CMR 451.350*	Structural Maintenance: Windows not weather tight and structurally sound throughout 	the cottage

Common Area

105 CMR 451.353	Interior Maintenance: Ceiling panels not installed properly in several areas

Officer’s Room

No Violations Noted

Kitchenette

FC 4-501.114(C)(2)	Maintenance and Operation; Equipment: Quaternary ammonium solution greater than 	the manufacturers recommended concentration

Refrigerator Room

No Violations Noted

Slop Sink Room (A)

No Violations Noted

Storage Room (A)

No Violations Noted

Interview Room (A)

105 CMR 451.350	Structural Maintenance: Floor tiles damaged

Caustic Room (C)

No Violations Noted

Shower Room A & B

105 CMR 451.123	Maintenance: Ceiling paint damaged in shower rooms

105 CMR 451.123	Maintenance: Soap scum on walls in shower # 1 and 2

Shower Room B & C	Occupied at the time of inspection

Hallway A Cells

105 CMR 451.353	Interior Maintenance: Ceiling covered with plastic in an attempt to control the room 	temperature in several cells

105 CMR 451.350	Structural Maintenance: Floor tile damaged in cell # 2

Hallway B Cells

105 CMR 451.350	Structural Maintenance: Ceiling water damaged in cell # 22

105 CMR 451.353	Interior Maintenance: Ceiling covered with plastic in an attempt to control the room 	temperature in several cells

Hallway C Cells

105 CMR 451.353	Interior Maintenance: Ceiling covered with plastic in an attempt to control the room 	temperature in several cells

Modular Building – Overflow Unit

Common

105 CMR 451.350	Structural Maintenance: Floor tiles damaged near the entry way and bathroom

Dorm Area

No Violations Noted

Shower Room

105 CMR 451.353	Interior Maintenance: Ceiling rusted on metal supports

Janitor’s Closet

No Violations Noted

Bathroom

No Violations Noted

Brewster Building

Brewster 1

Common Area

105 CMR 451.350	Structural Maintenance: Floor tiles damaged

105 CMR 451.353	Interior Maintenance: Outlet cover loose near television unit

Control Room

No Violations Noted

Control Bathroom

Occupied at the time of inspection

Storage Room

No Violations Noted

Fire System Room

No Violations Noted

Bathroom

105 CMR 451.123	Maintenance: Toilet paper holders damaged

105 CMR 451.123	Maintenance: Toilet stall door missing on stall # 3

105 CMR 451.126	Water Supply: No hot water supplied to handwash sink # 3

Shower Room

105 CMR 451.123	Maintenance: Standing water observed on floor outside shower stalls

105 CMR 451.123	Maintenance: Shower head missing in shower stall # 1

105 CMR 451.123	Maintenance: Shower curtain damaged in shower stall # 3

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, floor drain clogged

105 CMR 451.130	Hot Water: Shower water temperature recorded at 1180F

Kitchenette Area

FC 4-501.114(C)(2)	Maintenance and Operation; Equipment: Quaternary ammonium solution greater than 	the manufacturers recommended concentration

FC 4-601.11(c)	Cleaning of Equipment and Utensils, Objective: Non-food contact surface dirty,

counter top dirty

FC 5-202.12(A)	Plumbing System, Design: Handwashing sinks water temperature recorded at 1350F

Slop Sink Room

No Violations Noted

Room # 1

105 CMR 451.101	Blankets: Blanket damaged on bed # 1

105 CMR 451.322	Cell Size: Inadequate floor space in dorm room

105 CMR 451.350	Structural Maintenance: Floor tiles damaged

Room # 2

105 CMR 451.101	Blankets: Blanket damaged on bed # 5

105 CMR 451.322*	Cell Size: Inadequate floor space in dorm room

105 CMR 451.350*	Structural Maintenance: Floor tiles damaged

Room # 3

105 CMR 451.322*	Cell Size: Inadequate floor space in dorm room

105 CMR 451.350*	Structural Maintenance: Floor tiles damaged

105 CMR 451.350	Structural Maintenance: Vent cover damaged

105 CMR 451.353	Interior Maintenance: Interior vent dirty

Room # 4

105 CMR 451.101	Blankets: Blanket damaged on bed # 6

105 CMR 451.322*	Cell Size: Inadequate floor space in dorm room

105 CMR 451.350*	Structural Maintenance: Floor tiles damaged

Room # 5

105 CMR 451.101	Blankets: Blanket damaged on bed # 5

105 CMR 451.322*	Cell Size: Inadequate floor space in dorm room

105 CMR 451.350*	Structural Maintenance: Floor tiles damaged

Room # 6

105 CMR 451.322*	Cell Size: Inadequate floor space in dorm room

105 CMR 451.330	Room Temperature: Room temperature 840F

105 CMR 451.350*	Structural Maintenance: Floor tiles damaged

105 CMR 451.353	Interior Maintenance: Interior vent dirty

Room # 7

105 CMR 451.322*	Cell Size: Inadequate floor space in dorm room

105 CMR 451.330	Room Temperature: Room temperature 620F

105 CMR 451.350*	Structural Maintenance: Floor tiles damaged

Room # 8

105 CMR 451.322*	Cell Size: Inadequate floor space in dorm room

105 CMR 451.350*	Structural Maintenance: Floor tiles damaged

Room # 9

105 CMR 451.322*	Cell Size: Inadequate floor space in dorm room

105 CMR 451.350*	Structural Maintenance: Floor tiles damaged

Room # 10

105 CMR 451.322	Cell Size: Inadequate floor space in dorm room

105 CMR 451.350	Structural Maintenance: Floor tiles damaged

Brewster 2

Common Area

105 CMR 451.345	Illumination in Common Passage Ways and Areas: Inadequate lighting, one light 	fixture not functioning properly

Control Room

No Violations Noted

Control Bathroom

No Violations Noted

Razor Storage Room

No Violations Noted

Storage Room

No Violations Noted

Fire System Room

No Violations Noted

Bathroom

105 CMR 451.123	Maintenance: Toilet stall door missing on stall # 2

Shower Room

105 CMR 451.123	Maintenance: Vent fan dirty

105 CMR 451.123	Maintenance: Standing water observed on floor outside shower stalls

105 CMR 451.123	Maintenance: Shower curtain damaged in shower stall # 3

Kitchenette Area

FC 5-205.15(B)	Plumbing System, Operations and Maintenance: Plumbing system not maintained in 	good repair, facet leaking

Slop Sink Room

105 CMR 451.353	Interior Maintenance: Electrical outlet cover missing

Room # 1

105 CMR 451.322*	Cell Size: Inadequate floor space in dorm room

105 CMR 451.350	Structural Maintenance: Floor tiles damaged

Room # 2

105 CMR 451.141*	Screens: Screen damaged

105 CMR 451.322*	Cell Size: Inadequate floor space in dorm room

105 CMR 451.350*	Structural Maintenance: Floor tiles damaged

105 CMR 451.353	Interior Maintenance: Vent dirty

Room # 3

105 CMR 451.322*	Cell Size: Inadequate floor space in dorm room

105 CMR 451.344	Illumination in Habitable Areas: Inadequate lighting, one light fixture not functioning 	properly

105 CMR 451.353*	Interior Maintenance: Vent dirty

Room # 4

105 CMR 451.322*	Cell Size: Inadequate floor space in dorm room

105 CMR 451.350*	Structural Maintenance: Floor tiles damaged

Room # 5

105 CMR 451.322*	Cell Size: Inadequate floor space in dorm room

105 CMR 451.350*	Structural Maintenance: Floor tiles damaged

Room # 6

105 CMR 451.104	Beds: Bed frame not in good repair on bed # 7 and 8

105 CMR 451.322*	Cell Size: Inadequate floor space in dorm room

105 CMR 451.350	Structural Maintenance: Floor tiles damaged

105 CMR 451.330	Room Temperature: Room temperature 800F

Room # 7

105 CMR 451.322*	Cell Size: Inadequate floor space in dorm room

105 CMR 451.350*	Structural Maintenance: Floor tiles damaged

105 CMR 451.353	Interior Maintenance: Vent dirty

Room # 8

105 CMR 451.141*	Screens: Screen damaged

105 CMR 451.322*	Cell Size: Inadequate floor space in dorm room

105 CMR 451.350*	Structural Maintenance: Floor tiles damaged

Room # 9

105 CMR 451.141*	Screens: Screen damaged

105 CMR 451.322*	Cell Size: Inadequate floor space in dorm room

105 CMR 451.350*	Structural Maintenance: Floor tiles damaged

Room # 10

105 CMR 451.141*	Screens: Screen damaged

105 CMR 451.322*	Cell Size: Inadequate floor space in dorm room

105 CMR 451.350*	Structural Maintenance: Floor tiles damaged

105 CMR 451.353	Interior Maintenance: Vent dirty

Old Administration Building

A Corridor

Inmate Bathroom # 117

105 CMR 451.123	Maintenance: No toilet paper holder and toilet paper on floor in the stall # 2

105 CMR 451.126*	Hot Water: Hot water temperature recorded at 900F

Pre-Release Office

No Violations Noted

Inmate Weight Room # 118

105 CMR 451.344	Illumination in Habitable Areas: Inadequate lighting, one light fixture not functioning 	properly

105 CMR 451.353	Interior Maintenance: Wall paint damaged

Fire Equipment Room and Bathroom # 119

105 CMR 451.126*	Hot Water: Hot water temperature recorded at 1060F

Back Storage Closets

Hallway

105 CMR 451.350	Structural Maintenance: Doorway water damaged

Officer’s Room # 121

105 CMR 451.353	Interior Maintenance: Several ceiling tiles missing

Closet # 122 - 1 & 2

No Violations Noted

Closet # 122 - 3 & 4

No Violations Noted

Janitor’s Closet 122-6

105 CMR 451.353	Interior Maintenance: Ceiling damage repaired not finished in a workman like manner

Closet 122-7

No Violations Noted

Closet 122-8	Locked - Room not accessible at the time of inspection

CO Office 124

105 CMR 451.353	Interior Maintenance: Wall paint damaged

B Corridor

105 CMR 451.331	Radiators and Heating Pipes: Pipes not insulated properly

105 CMR 451.345	Illumination in Common Passage Ways and Areas: Inadequate lighting, one light 	fixture not functioning properly

Tool Control Office 107

105 CMR 451.353	Interior Maintenance: One light shield missing

Classroom 111

105 CMR 451.344	Illumination in Habitable Areas: Inadequate lighting, one light fixture not functioning 	properly

105 CMR 451.350	Structural Maintenance: Wall damaged

Gym 112

105 CMR 451.344	Illumination in Habitable Areas: Inadequate lighting, several light fixtures not 	functioning properly

Operations near the Gym

105 CMR 451.350	Structural Maintenance: Floor tiles damaged near refrigerator

105 CMR 451.353	Interior Maintenance: Ceiling tiles missing near bathroom and in office

FC 3-501.16(B)	Limitation of Growth of Organisms, Temperature and Time Control: Refrigerator 	temperature recorded at 460F

Operations Bathroom

No Violations Noted

Disciplinary Office 113

105 CMR 451.344	Illumination in Habitable Areas: Inadequate lighting, one light fixture not functioning 	properly

Staff Bathroom 114

105 CMR 451.126	Hot Water: Hot water temperature recorded at 700F

Slop Sink outside Staff Bathroom 114

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, drain clogged

Work Assignment 114

105 CMR 451.350	Structural Maintenance: Ceiling tiles missing

105 CMR 451.350	Structural Maintenance: Floor tiles damaged

Activity Room 115

105 CMR 451.331	Radiators and Heating Pipes: Pipes not insulated properly

105 CMR 451.350	Structural Maintenance: Ceiling damaged

Classroom 116

No Violations Noted

C Corridor

Classroom

No Violations Noted

D Corridor

Cosmetology 130

105 CMR 451.126*	Hot Water: Hot water temperature recorded at 1060F in hair wash and bathroom sinks

105 CMR 451.350*	Structural Maintenance: Ceiling damaged

105 CMR 451.353*	Interior Maintenance: Ceiling paint damaged

105 CMR 451.353	Interior Maintenance: Desk draw # 10 not functioning properly

Classroom 131

105 CMR 451.344	Illumination in Habitable Areas: Inadequate lighting, one light fixture not functioning 	properly

Protestant Chaplain’s Office 137

105 CMR 451.344	Illumination in Habitable Areas: Inadequate lighting, one light fixture not functioning 	properly

Office 138

No Violations Noted

Catholic Chaplain’s Office 139

No Violations Noted

Needs Office 141

No Violations Noted

Office 142

No Violations Noted

Office 143

105 CMR 451.344	Illumination in Habitable Areas: Inadequate lighting, one light fixture not functioning 	properly

105 CMR 451.353	Interior Maintenance: One light shield not functioning properly

Family Service Office 146

105 CMR 451.344	Illumination in Habitable Areas: Inadequate lighting, one light fixture not functioning 	properly

Staff Bathroom 147

No Violations Noted

Waiting Room 148

105 CMR 451.331	Radiators and Heating Pipes: Pipes not properly insulated

Second Floor

IPS	Locked - Not accessible at the time of inspection

Intensive Treatment Unit	Under renovation at the time of inspection

Psychology Corridor

Offices

No Violations Noted

Kitchenette

105 CMR 451.353	Interior Maintenance: Ceiling paint damaged

Bathroom

No Violations Noted

B Corridor

Staff Bathroom

105 CMR 451.123	Maintenance: Vent fan dirty

105 CMR 451.126	Hot Water: Hot water temperature recorded at 910F

Classroom 201

No Violations Noted

Office 206

No Violations Noted

Law Library 208

No Violations Noted

Library 209

105 CMR 451.350	Structural Maintenance: Ceiling tiles damaged

Law Library 211

No Violations Noted

Education Area 212

Bathroom

105 CMR 451.123	Maintenance: Light shield missing

Classrooms

No Violations Noted

Offices

No Violations Noted

Industries 213

105 CMR 451.123	Maintenance: Light fixture not functioning properly in staff and inmate bathroom

Building and Trades 214	Program closed - Locked at the time of inspection

Classroom 215-2

105 CMR 451.350	Structural Maintenance: Windows not weather tight and structurally sound

Classroom 215-4

105 CMR 451.344	Illumination in Habitable Areas: Inadequate lighting, several light fixtures not functioning properly

Classroom 215-7

105 CMR 451.331	Radiators and Heating Pipes: Pipes not properly insulated

Computer Room 215-8

105 CMR 451.350	Structural Maintenance: Floor tiles missing and damaged

105 CMR 451.353	Interior Maintenance: Light shield missing

Bathroom 215-9

105 CMR 451.123	Maintenance: Floor no longer easily cleanable, floor tiles damaged and missing

105 CMR 451.123	Maintenance: Light shield missing

105 CMR 451.123	Maintenance: Vent and light area dirty

Janitor’s Closet 216

No Violations Noted

Parole Hallway 218

105 CMR 451.353*	Interior Maintenance: Ceiling paint damaged in several offices

Parole Bathroom

No Violations Noted

First Floor

Store Room

105 CMR 451.353	Interior Maintenance: Pipe leaking above sanitizer prep area

Food Service Area

Hallway

105 CMR 451.331	Radiators and Heating Pipes: Pipes not properly insulated

Inmate Dinning Room

FC 4-202.11(A)(2)	Design and Construction, Cleanability: Damaged food-contact surface no longer	easily cleanable, red table top damaged

FC 6-501.11	Maintenance and Operation; Repairing: Facility not in good repair, one bench 	damaged

Serving Line

FC 3-304.12(A)	Preventing Contamination from Utensils: Service utensils handle stored below the 	food and container line, bowl left in cereal container

FC 4-202.11(A)(2)*	Design and Construction, Cleanability: Damaged food-contact surface no longer	easily cleanable, red table top damaged

FC 6-501.11	Maintenance and Operation; Repairing: Facility not in good repair, floor tiles 	damaged

FC 4-501.11(A)	Maintenance and Operation, Equipment: Equipment not maintained in a state of good 	repair, cover missing from ice cooler and ice not covered properly

FC 6-501.111(B)	Maintenance and Operations; Pest Control: Several dead and live insects observed on 	sticky traps

FC 6-501.12(A)*	Maintenance and Operation; Cleaning: Facility not cleaned properly, food debris and 	wrapper observed between the food service counter and half wall

FC 6-501.12(A)	Maintenance and Operation; Cleaning: Facility not cleaned properly, interior surfaces 	of secured utensil storage cabinet dirty

Mechanical Warewashing Room

FC 4-501.114(C)(2)	Maintenance and Operation; Equipment: Quaternary ammonium solution lower than 	the manufacturers recommended concentration

FC 6-501.11*	Maintenance and Operation; Repairing: Facility not in good repair, floor tiles 	damaged

FC 6-501.11	Maintenance and Operation; Repairing: Facility not in good repair, one light fixture 	not functioning properly

FC 6-501.12(A)	Maintenance and Operation; Cleaning: Facility not cleaned properly, standing water 	observed on floor

Culinary Arts

Kitchen

FC 3-304.12(A)	Preventing Contamination from Utensils: Service utensils handle stored below the 	food and container line in the dry goods containers

FC 4-501.11(A)	Maintenance and Operation, Equipment: Equipment not maintained in a state of good 	repair, middle steamer tray leaking

FC 4-601.11(c)	Cleaning of Equipment and Utensils, Objective: Non-food contact surface dirty, 	interior of dry good containers dirty

FC 5-205.11(B)	Plumbing System, Operations and Maintenance: Handwashing sink used for an	unapproved purpose, lettuce observed in the back handwash sink

FC 6-501.11	Maintenance and Operation; Repairing: Facility not in good repair, one light fixture 	not functioning properly

FC 6-501.111(B)	Maintenance and Operations; Pest Control: Rodent droppings observed on the dry 	good containers and in the back corner

Staff Dinning Room

No Violations Noted

Basement

Laundry Area

No Violations Noted

Inmate Bathroom

No Violations Noted

Main Kitchen

Hallway

FC 6-501.11	Maintenance and Operation; Repairing: Facility not in good repair, windows not 	weather tight and covered over to reduce draft

Paper Goods Storage Room

No Violations Noted

Dry Storage Room

FC 6-404.11*	Location and Placement; Distressed Merchandise: Dented cans not properly 	segregated

Freezer and Refrigerator Hallway

FC 6-501.11	Maintenance and Operation; Repairing: Facility not in good repair, ceiling tiles water 	stained

Freezer Unit

FC 4-601.11(c)	Cleaning of Equipment and Utensils, Objective: Non-food contact surface dirty,	ceiling and cooler fan dirty

Refrigerator Unit

No Violations Noted

Food Service Staff Office

FC 6-501.11	Maintenance and Operation; Repairing: Facility not in good repair, ceiling paint 	damaged

Back Pots and Pans Storage Area

FC 4-501.11(A)	Maintenance and Operation, Equipment: Equipment not maintained in a state of good 	repair, Cambro insulated food storage container door damaged

FC 6-202.15(A)(2)*	Design, Construction, and Installation; Functionality: Outer door not weather and 	vermin tight

FC 6-501.12(A)	Maintenance and Operation; Cleaning: Facility not cleaned properly, floor dirty under 	pots and pans storage racks

Bakery Area

FC 5-205.11(B)	Plumbing System, Operations and Maintenance: Handwashing sink used for an	unapproved purpose, onions observed in 2-compartment handwashing sink

FC 6-501.12(A)	Maintenance and Operation; Cleaning: Facility not cleaned properly, standing water 	observed near ramp

Refrigerator Unit # 5

FC 3-305.11(A)(2)	Preventing Contamination from Premises: Food exposed to dust, fans in cooler dusty

Freezer Unit # 6

No Violations Noted

Inmate Dinning Area

No Violations Noted

Dry Goods Storage Room

FC 6-501.111(B)	Maintenance and Operations; Pest Control: Several dead and live insects observed on 	sticky traps

FC 6-501.12(A)	Maintenance and Operation; Cleaning: Facility not cleaned properly, interior surfaces 	of secured utensil storage cabinet dirty

FC 6-501.12(A)	Maintenance and Operation; Cleaning: Facility not cleaned properly, standing water 	observed on floor

Broom Storage Area

FC 6-202.11(A)	Design, Construction, and Installation; Functionality: Light bulbs not shatter-resistant 	or protected by light shields in maintenance area

Slop Bucket Refrigerator

No Violations Noted

Prep-Table Handwash Sink near Can Opener

FC 5-205.15(B)	Plumbing System, Operations and Maintenance: Plumbing system not maintained in 	good repair, no hot water provided

Prep-Counter Handwash Sink near 3-Compartment Sink

FC 6-501.11	Maintenance and Operation; Repairing: Facility not in good repair, paper towel holder 	damaged and not secured properly to table

3-Compartment Sink

FC 4-501.11(A)	Maintenance and Operation, Equipment: Equipment not maintained in a state of good 	repair, wash bay drain plug not functioning properly

FC 4-501.114(C)(2)*	Maintenance and Operation; Equipment: Quaternary ammonium solution greater than 	the manufacturers recommended concentration in sanitizing bay

FC 6-501.11	Maintenance and Operation; Repairing: Facility not in good repair, one light fixture 	not functioning properly

Warmers

No Violations Noted

Back Area – Officer’s Area

FC 6-202.15(A)(2)*	Design, Construction, and Installation; Functionality: Outer door not weather and 	vermin tight

Inmate Bathroom

FC 6-301.12	Numbers and Capacity; Handwashing Facilities: No hand drying method available at 	handwashing sink, no paper towels available

FC 6-501.11	Maintenance and Operation; Repairing: Facility not in good repair, cold water control 	damaged

Staff Bathroom

FC 6-301.12	Numbers and Capacity; Handwashing Facilities: No hand drying method available at 	handwashing sink, no paper towels available

FC 6-501.11	Maintenance and Operation; Repairing: Facility not in good repair, heating pipes not 	insulated properly

FC 6-501.11	Maintenance and Operation; Repairing: Facility not in good repair, handwash sink 	water worn and no longer easily cleanable

Power Plant Building # 3

Bathroom

No Violations Noted

Break Room

105 CMR 451.344	Illumination in Habitable Areas: Inadequate lighting, one light fixture not functioning 	properly

Maintenance Building # 4

Tool Crib

No Violations Noted

Paint Room

No Violations Noted

Bathroom in Office

No Violations Noted

Inmate Bathroom

105 CMR 451.123	Maintenance: Pipes not properly insulated

Staff Bathroom

No Violations Noted

Break Room

FC 4-501.11(A)*	Maintenance and Operation, Equipment: Equipment not maintained in a state of good 	repair, kick plate missing from refrigerator unit

FC 4-601.11(c)	Cleaning of Equipment and Utensils, Objective: Non-food contact surface dirty, 	gasket dirty

Vehicle Trap

Bathroom

105 CMR 451.126	Hot Water: Hot water temperature recorded at 1400F

Observations and Recommendations

- Brooms stored to closely to the sprinkler heads in the Smith Building housing unit janitor’s closets, the Department recommends lowering the brooms to allow adequate clearance

- Water fountain control buttons were removed in the cottages for a security concern, the Department recommends an alternative be found to ensure all water fountains are easily activated

- Modular (overflow) building was not in use and operating on a backup generator at the time of inspection due to a damaged transformer

- Vent covers in Brewster 1 were inconsistent, the Department recommends all necessary parts be in place and consistent throughout the building

- The rug in the Psychology Corridor bathroom makes the floor not easily cleanable, the Department recommends rugs not be used in any bathrooms within the institution

- Several screws were left under the food service counter at the inmate food service line, the Department recommends the sharp screws be addressed to ensure safety of staff and inmates

- The sanitizer concentration was excessive throughout most of the facility, the Department recommends the sanitizer be tested prior to distribution to ensure proper concentration

This facility does not comply with the Department’s Regulations cited above. In accordance with 105 CMR 451.404, please indicate next to each entry on the inspection report a plan of correction. Said plan of correction must be submitted within 10 days of receipt of this letter and should detail the specific steps that will be taken and the date of expected compliance. The plan of correction should be submitted to my attention, at the address listed above.

To review the specific regulatory requirements please visit our website at www.mass.gov/dph/dcs and click on "Community Sanitation Regulations" (available in both PDF and RTF formats).

To review the Food Establishment regulations please visit the Food Protection website at www.mass.gov/dph/fpp and click on “Food Protection Regulations”. Then under “Retail” click “105 CMR 590.000 - State Sanitary Code Chapter X – Minimum Sanitation Standards for Food Establishments” and “1999 Food Code”.

This inspection report is signed and certified under the pains and penalties of perjury.

Sincerely,

Lauren Molotnikov

Environmental Health Inspector, CSP, BEH

cc:	Suzanne K. Condon, Associate Commissioner, Director, BEH

Steven Hughes, Director, CSP, BEH

JudyAnn Bigby, MD, Secretary, Executive Office of Health and Human Services

Ronald T. Duval, Acting Commissioner, DOC

Pamela Britt, FS/EHSO

Framingham Board of Health

Clerk, Massachusetts House of Representatives

Clerk, Massachusetts Senate

Mary Elizabeth Heffernan, EOPS