The Commonwealth of Massachusetts

Executive Office of Health and Human Services

Department of Public Health

Bureau of Environmental Health

Community Sanitation Program

23 Service Center

Northampton, MA 01060

Telephone 413 586-7525, ext. 3167

Facsimile 413 784-1037

TTY 800 769-9991

charlie.kaniecki@state.ma.us

DEVAL L. PATRICK GOVERNOR TIMOTHY P. MURRAY LIEUTENANT GOVERNOR JUDYANN BIGBY, MD SECRETARY JOHN AUERBACH COMMISSIONER

April 23, 2012

Anthony Mendonsa, Superintendent

Souza-Baranowski Correctional Center

P.O. Box 8000

Shirley, MA 01464

Re: Facility Inspection

Dear Superintendent Mendonsa:

In accordance with M.G.L. c. 111, §§ 5, 20, and 21, and Department of Public Health Regulations 105 CMR 451.000: Minimum Health and Sanitation Standards and Inspection Procedures for Correctional Facilities; 105 CMR 480.000: Storage and Disposal of Infectious or Physically Dangerous Medical or Biological Waste (State Sanitary Code, Chapter VIII); 105 CMR 590.000: Minimum Sanitation Standards for Food Establishments (State Sanitary Code Chapter X); the 1999 Food Code; and 105 CMR 205.000 Minimum Standards Governing Medical Records and the Conduct of Physical Examinations in Correctional Facilities; I conducted an inspection of Souza-Baranowski Correctional Center on April 17, 18, 19 & 20, 2012 accompanied by Wayne Hancock, EHSO. Violations noted are listed below (* indicates conditions documented on previous inspection reports).

ENTRANCE AREA

Bubbler

No Violations Noted

Female Bathroom A1-10

105 CMR 451.123	Maintenance: Toilet/Handwash sink damaged, faucet dripping

Male Bathroom A1-9

105 CMR 451.130*                    Plumbing not maintained in good repair, first sink out-of-order

105 CMR 451.350                      Structural Maintenance: Wall damaged, corners near floor

Janitor’s Closet A1-11

105 CMR 451.353*	Interior Maintenance: Mop stored in bucket

105 CMR 451.353*	Interior Maintenance: Unlabeled chemical bottle

105 CMR 451.353		Interior Maintenance: T-Matic Buffer missing ground plug

ADMINISTRATION AREA A2-6

2nd Floor

Kitchenette

No Violations Noted

Female Bathroom A2-22

105 CMR 451.353*	Interior Maintenance: Ceiling vent dusty

Male Bathroom A2-21

No Violations Noted

Female Locker Room A-44

Unable to Inspect - In Use

Hallway Bubbler

105 CMR 451.130	Plumbing not maintained in good repair

Men’s Locker Room A2–48

105 CMR 451.350	Structural Maintenance: Wall damaged behind toilet

Weight Room A2-37

105 CMR 451.353	Interior Maintenance: Unlabeled chemical bottle

105 CMR 451.353                      Interior Maintenance: Mirror damaged on wall

105 CMR 451.350	Structural Maintenance: Ceiling damaged, broke/missing tiles

105 CMR 451.350	Structural Maintenance: Wall damaged by mirror

105 CMR 451.353	Interior Maintenance: Damaged seats on Nautilus leg extender,

Sit-up bench & Cybex bench

1st Floor

Female Bathroom A1-31

105 CMR 451.353	Interior Maintenance: Ceiling vent dusty

Janitor’s Closet A1-43

105 CMR 451.350*	Structural Maintenance: Wall damaged

105 CMR 451.350*	Structural Maintenance: Paint peeling

105 CMR 451.353*	Interior Maintenance: Vent dusty

105 CMR 451.130	Plumbing: No backflow on threaded water bib

Men’s Locker Room A1-33

105 CMR 451.123*	Maintenance: Wall paint peeling in shower area

105 CMR 451.123*	Maintenance: Wall damaged

105 CMR 451.123*	Maintenance: Ceiling tile water damaged

105 CMR 451.353*	Interior Maintenance: Ceiling vent dusty

OUTER CONTROL A1-16

Bathroom A1-17

105 CMR 451.353*	Interior Maintenance: Unlabeled chemical bottle

105 CMR 451.350	Structural Maintenance: Floor damaged, tiles lifting

105 CMR 451.123	Maintenance: Bubbler dirty

INNER CONTROL B1-1B

FC 4-602.12(B)*		Cleaning of Equipment and Utensils; Frequency: Interior of microwave

oven dirty

Bathroom B1-39

105 CMR 451.353*	Interior Maintenance: Ceiling vent dusty

VISITING AREA

Non-Contact Visiting Area B1-22

105 CMR 451.344                      Illumination in Habitable Areas: Light fixture not working properly in two stalls

Contact Area

105 CMR 451.350	Structural Maintenance: Ceiling damaged, rust and loose paint

105 CMR 451.353	Interior Maintenance: Water leaking from ceiling in two areas

Bathrooms

105 CMR 451.353*	Interior Maintenance: Ceiling vent dusty in all bathrooms

Janitor’s Closet B1-12

105 CMR 451.353*	Interior Maintenance: Mop stored on floor

OPERATIONS AREA

Female Bathroom B1-48

105 CMR 451.353*	Interior Maintenance: Ceiling vent dusty

Male Bathroom B -49

105 CMR 451.353*	Interior Maintenance: Ceiling vent dusty

Janitor’s Closet

Unable to Inspect - Locked

MAIN KITCHEN

Inmate Dining Area

No Violations Noted

Tray Washing Room

No Violations Noted

North Side Serving

FC 3-304.14(B)(2)*	Preventing Contamination from Linens: Wet cloth not stored in sanitizer bucket

FC 4-501.114(A)*	Maintenance and Operation; Equipment: Chlorine Sanitizer solution tested less than recommended concentration

FC 4-501.11(B)*	Maintenance and Operation, Equipment: Equipment components not maintained in a 	state of good repair, warmer gaskets damaged

FC 4-501.11(B)	Maintenance and Operation, Equipment: Equipment components not maintained in a 	state of good repair, cooler gaskets damaged

FC 4-701.10	Sanitization of Equipment and Utensils, Objective: Food contact surfaces/utensils not 	properly sanitized, serving trays

FC 5-205.15(B)	Plumbing System, Operations and Maintenance: Plumbing system not maintained in 	good repair, prep sink leaking

FC 4-601.11(B)	Cleaning of Equipment and Utensils, Objective: Food contact surface dirty, cooking

equipment dirty plastic cup being stored inside food containers to dispense food stuffs

FC 4-601.11(c)	Cleaning of Equipment and Utensils, Objective: Non-food contact surface dirty,

Clean under counters

South Side Serving

FC 4-501.11(B)*	Maintenance and Operation, Equipment: Equipment components not maintained in a 	state of good repair, warmer gaskets damaged

FC 4-501.11(B)*	Maintenance and Operation, Equipment: Equipment components not maintained in a 	state of good repair, cooler gaskets damaged

FC 3-304.14(B)(2)	Preventing Contamination from Linens: Wet cloth not stored in sanitizer bucket

FC 5-202.12(A)	Plumbing System, Design: Handwashing sinks water temperature recorded

at 930F

Pot Washing Area

No Violations Noted

Kitchen Cook Area

FC 6-201.11*	Design, Construction and Installation: Floor not easily cleanable, floor tile damage in kettle area

FC 6-501.114(A)*	Maintenance and Operations; Maintaining Premises: Nonfunctional equipment not repaired or removed from premises, Blodgott Oven

FC 5-205.15(B)*	Plumbing System, Operations and Maintenance: Plumbing system not maintained in 	good repair, hose connected to sink faucet and hose left on floor

FC 4-501.11(B)*	Maintenance and Operation, Equipment: Equipment components not maintained in a 	state of good repair, gaskets damaged to blast chiller

FC 3-302.11(A)(4)*	Preventing Food and Ingredient Contamination: Preventing cross contamination, food 	not appropriately covered in left over cooler

FC 3-304.14(B)(2)	Preventing Contamination from Linens: Wet cloth not stored in sanitizer bucket

FC 6-501.11                    	Maintenance and Operation; Repairing: Facility not in good repair, flooring lifting and

wall separating near walk-in door

FC 6-501.12(A)	                          Maintenance and Operation; Cleaning: Facility not properly cleaned, milk cooler rusty

FC 6-501.11                    	Maintenance and Operation; Repairing: Facility not in good repair, 3 bay sink faucet

leaking

FC 4-601.11(A)	                          Cleaning of Equipment and Utensils, Objective: Food contact surface dirty, cutting

boards worn

FC 6-501.11                    	Maintenance and Operation; Repairing: Facility not in good repair, exposed wiring

FC 6-501.11                    	Maintenance and Operation; Repairing: Facility not in good repair, loose insulation on

piping in wash ware area

Bakery

FC 5-501.110	Refuse, Recyclables, and Returnables; Operations and Maintenance: Refuse storage 	not inaccessible to vermin, damaged trash container

FC 7-101.11	Poisonous or Toxic Materials; Original Containers: Cleaning chemicals not labeled properly, original manufactures label missing, fluff containers being used for rag sanitizer containers

FC 5-202.12(A)*	Plumbing System, Design: Handwashing sinks water temperature recorded at 1080F

FC 6-501.11*	Maintenance and Operation; Repairing: Facility not in good repair, electrical outlet damaged, face plate

FC 3-305.11(A)(2)*	Preventing Contamination from Premises: Food exposed to dust, fans in cooler dusty

FC 4-601.11(B)*	Cleaning of Equipment and Utensils, Objective: Food contact surface dirty, cooking

equipment dirty plastic cup being stored inside food containers to dispense food

product

FC 6-501.11*                    	Maintenance and Operation; Repairing: Facility not in good repair, 2 bay sink faucet

leaking

Dry Storage for Kitchen

FC 4-904.11(B)	                         Protection of Clean Items, Storing: Knives/Forks/Spoons not presented to avoid

contamination

Meat Cooler

FC 4-501.11(A)	Maintenance and Operation, Equipment: Equipment not maintained in a state of good 	repair, light out in meat cooler

FC 3-305.11(A)(2)	Preventing Contamination from Premises: Meat freezer, food exposed to dust, fans in left over cooler dusty

Produce Cooler

No Violations Noted

Dairy Cooler

No Violations Noted

Hallal Station

No Violations Noted

Storage (next to Office)

No Violations Noted

Office

No Violations Noted

Janitor’s Closet

105 CMR 451.350*	Structural Maintenance: Baseboard damaged

105 CMR 451.353	Interior Maintenance: Water on floor

105 CMR 451.130*	Plumbing: Plumbing not maintained in good repair, no hot water nozzle

Staff Bathroom/Locker Room

105 CMR 451.353*	Interior Maintenance: Ceiling vent dusty

105 CMR 451.353*	Interior Maintenance: Door rusty

Inmate Bathroom

105 CMR 451.123*	Maintenance: Baseboard damaged

105 CMR 451.123*	Maintenance: Generally dirty

105 CMR 451.123*	Maintenance: Floor damaged

105 CMR 451.123*	Maintenance: Door rusted and damaged

105 CMR 451.110(A)	Hygiene Supplies at Toilet and Handwash Sink: No soap at handwash sink

Staff Bathroom

No Violations Noted

CULINARY D1-36

FC 4-501.11(A)	Maintenance and Operation, Equipment: Equipment not maintained in a state of good repair, light not working over stove

Dry Goods D1-41

FC 6-501.114(A)	Maintenance and Operations; Maintaining Premises: Nonfunctional equipment not repaired or removed from premises, Travisen unit out of order

FC 6-201.16(A)	Design, Construction, and Installation; Cleanability: Walls/Ceiling covering not easily cleanable, ceiling damaged

105 CMR 451.383(B)	Fire Safety System: Facility not in compliance with State Building Code provisions on fire safety, boxes piled to ceiling, no 18 inch open space

Kitchen

FC 6-501.11	Maintenance and Operation; Repairing: Facility not in good repair, a wood box has been constructed over plumbing

FC 6-501.12(A)	Maintenance and Operation; Cleaning: Facility not properly cleaned, rubber floor mats are being stored next to the cook kettles

FC 6-501.11	Maintenance and Operation; Repairing: Facility not in good repair, electrical outlet covered with duct tape

FC 7-101.11	Poisonous or Toxic Materials; Original Containers: Cleaning chemicals not labeled properly, original manufactures label missing, fluff containers being used for rag sanitizer containers

FC 6-501.12(A)	                          Maintenance and Operation; Cleaning: Facility not properly cleaned, ice cooler rusty

near D1-42 area

Freezer

FC 3-302.11(A)(4)	Preventing Food and Ingredient Contamination: Preventing cross contamination, food not appropriately covered, uncovered meats

FC 6-202.11(A)	Design, Construction, and Installation; Functionality: Light bulbs not shatter-resistant or protected by light shields, shield missing

FC 6-501.14	Maintenance and Operation; Cleaning: Ventilation Systems, vent dusty

FC 6-501.11	Maintenance and Operation; Repairing: Facility not in good repair, cooler door damaged

Can Storage Area

FC 6-501.114(A)	Maintenance and Operations; Maintaining Premises: Nonfunctional equipment not repaired or removed from premises, used can washing area not being used to wash cans, converted to a storage area for the cans

Dumpster Area

No Violations Noted

Janitor’s Closet D1-44

FC 6-501.16*	Maintenance and Operation; Cleaning: Wet mop stored in bucket

105 CMR 451.353	Interior Maintenance: Unlabeled chemical bottle

Dishwasher Area D1-37

FC 6-301.12*	Numbers and Capacity; Handwashing Facilities: No hand drying method available at handwashing sink or soap

FC 4-903.11(B)(1)	Protection of Clean Items, Storing: Pots/Pans/Bowls not stored in the inverted/self-draining position

Serving Line D1-36A

FC 6-501.12(A)	Maintenance and Operation; Cleaning: Facility not cleaned properly, area under leaky soda line is covered in syrup

Staff Dining Area D1-25

FC 4-904.11(B)*	Protection of Clean Items, Storing: Knives/Forks/Spoons not presented to

avoid contamination, uncovered on tables

FC 6-501.14	Maintenance and Operation; Cleaning: Ventilation Systems, vents dusty

Male Staff Locker Room D1-27

105 CMR 451.350*	Structural Maintenance: Ceiling damaged, near shower and by entry door

105 CMR 451.353*	Interior Maintenance: Ceiling vent dusty

105 CMR 451.110(A)	Hygiene Supplies at Toilet and Handwash Sink: No paper towels at

handwash sink

Female Staff Locker Room D1-31

105 CMR 451.350*	Structural Maintenance: Ceiling damaged

105 CMR 451.344	Illumination in Habitable Areas: Inadequate lighting, missing light blub

Janitor’s Closet D1-26

No Violations Noted

GYM AREA D1-15

Control

FC 4-501.11(A)	Maintenance and Operation, Equipment: Equipment not maintained in a state of good 	repair, refrigerator gasket damaged

Janitor’s Closet D1-24

105 CMR 451.353*	Interior Maintenance: Ceiling vent dusty

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, drain cover missing

Inmate Bathroom D1-23

105 CMR 451.353*	Interior Maintenance: Ceiling vent dusty

SOUTH GYM D1 -17

Janitor’s Closet D1-22

105 CMR 451.353*	Interior Maintenance: Ceiling vent dusty

105 CMR 451.353*	Interior Maintenance: Unlabeled chemical bottle

105 CMR 451.353*	Interior Maintenance: Missing drain cover

Staff D1-19

Unable to Inspect - Locked

Room D1-20

105 CMR 451.353	Interior Maintenance: Mixed chemicals stored on floor

Room D1-21

No Violations Noted

NORTH GYM D1-13

No Violations Noted

Storage Room D1-14

No Violations Noted

WEIGHT ROOM D1-11

105 CMR 451.353*	Interior Maintenance: Seats damaged on 2 sit up machines, 1 pull

over machine & 1 pull down machine

INSIDE WAREHOUSE

Dry Goods

No Violations Noted

Freezer DG-69

No Violations Noted

Room DG-70

No Violations Noted

Room DG-68

No Violations Noted

TRASH DOCK

No Violations Noted

OUTSIDE WAREHOUSE

Refrigerator

FC 3-305.11(A) (2)*	Preventing Contamination from Premises: Food exposed to dust, fans in cooler dusty

FC 4-501.11(A)	Maintenance and Operation, Equipment: Equipment not maintained in a state of good 	repair, gasket damaged

Freezer

FC 6-501.11*	Maintenance and Operation; Repairing: Facility not in good repair, light not working properly

FC 4-501.11(A)	Maintenance and Operation, Equipment: Equipment not maintained in a state of good repair, wall damaged

FC 4-501.11(A)	Maintenance and Operation, Equipment: Equipment not maintained in a state of good repair, ice build-up on cooler coils

FC 4-501.11(A)	Maintenance and Operation, Equipment: Equipment not maintained in a state of good repair, water dripping from ceiling

Janitor’s Closet

105 CMR 451.353	Interior Maintenance: Drain cover, not attached

FC 6-501.16	Maintenance and Operation; Cleaning: Wet mop stored in bucket

Bathroom

105 CMR 451.123*	Maintenance: Ceiling damaged

105 CMR 451.331	Radiators and Heating Pipes: Pipes not properly insulated, loose insulation on pipe

105 CMR 451.123	Maintenance: Hole in wall with exposed wires

105 CMR 451.126		Hot Water: Hot water temperature recorded at 94oF

BARBER SHOP/VOC ED

Office C1-40

FC 4-602.12(B)	*	            Cleaning of Equipment and Utensils; Frequency: Interior of microwave oven dirty

FC 4-602.12(B)                          Cleaning of Equipment and Utensils; Dirty bubbler

105 CMR 451.353	Interior Maintenance: Ceiling vent dusty

Female Bathroom C1-37

105 CMR 451.110(A)*	Hygiene Supplies at Toilet and Handwash Sink: No toilet paper

Male Bathroom C1-38

No Violations Noted

Computer Room C1-34

105 CMR 451.353	Interior Maintenance: Ceiling vent dusty

Barber Shop C1-27

105 CMR 451.126*	Hot Water: Hot water temperature 1030F

105 CMR 451.353	Interior Maintenance: Chairs damaged # 4, 6 & 7

Janitor’s Closet C1-25

FC 6-501.16	Maintenance and Operation; Cleaning: Wet mop stored in bucket

Storage Room C1-29

No Violations Noted

Storage C1-30

No Violations Noted

RTV CLASS ROOMS C1-31

No Violations Noted

SCHOOL/LIBRARY C2-84

Female Bathroom C2-76

No Violations Noted

Male Bathroom C2-77

No Violations Noted

Inmate Bathrooms C2-75

No Violations Noted

Room C2-66

No Violations Noted

Room C2-64

Unable to Inspect - Locked

Janitor’s Closet C2-65

105 CMR 451.353*	Interior Maintenance: Ceiling vent dusty

105 CMR 451.123	Maintenance: Outlet GFI not operable

Room C2-62

105 CMR 451.353*	Interior Maintenance: Ceiling vent dusty

Staff Break Room C2-63

FC 4-903.11(A)(2)* 		Protection of Clean Items, Storing: Single-service items uncovered and not protected 			             from contamination

105 CMR 451.346                      Safe Wiring: Use of extension cord as temporary wiring, for photo copier, through a

doorway

Library C2-67A

No Violations Noted

Room C2-74

Unable to Inspect – No Access

BOOKING/PROPERTY D6-74A

Room D6-24

Unable to Inspect - Locked

Female Bathroom D6-60

No Violations Noted

Male Bathroom D6-62

No Violations Noted

Janitor’s Closet D6-62

105 CMR 451.126*	Hot Water: Hot water temperature 910F recorded at sink

FC 6-501.16	Maintenance and Operation; Cleaning: Mop stored in bucket

105 CMR 451.353	Interior Maintenance: Unlabeled chemical bottle

105 CMR 451.353	Interior Maintenance: Chemical bottles on floor

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, faucet leaking

Cell #3 D6-63

105 CMR 451.353*	Interior Maintenance: Ceiling vent dusty

Group Holding D6-65

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, toilet leaking

105 CMR 451.353	Interior Maintenance: Ceiling vent dusty

Adm. 1

Unable to Inspect – In Use

Protocol Room D6-50

No Violations Noted

Adm. 2 D6-41

105 CMR 451.130*	Plumbing not maintained in good repair, cold water not working

Scrub Room

No Violations Noted

Laundry D6-40

105 CMR 451.350*	Structural Maintenance: Ceiling damaged

105 CMR 451.353	Interior Maintenance: Chemical bottles on floor

105 CMR 451.350	Structural Maintenance: Ceiling damaged, water leak

105 CMR 451.350	Structural Maintenance: Floor damaged by water

105 CMR 451.123	Maintenance: Dryer vent damaged

Adm. 3 D6-42

105 CMR 451.130*	Plumbing: Plumbing not maintained in good repair, hot water not working

Staff Break room D6-36

No Violations Noted

Property Room Annex D6-43

105 CMR 451.123	Maintenance: Blocked ceiling vent

Room D6-44A

No Violations Noted

Property Room D6-46

No Violations Noted

Room D6-45

105 CMR 451.350	Structural Maintenance: Ceiling damaged, tile missing

105 CMR 451.350	Structural Maintenance: Wall damaged with wiring exposed

Female Staff Bathroom D6-48

No Violations Noted

Male Bathroom D6-49

No Violations Noted

Janitor’s Closet D6-47

FC 6-501.16	Maintenance and Operation; Cleaning: Wet mop stored in bucket

105 CMR 451.353	Interior Maintenance: Unlabeled chemical bottle

105 CMR 451.353	Interior Maintenance: Chemical bottles on floor

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, faucet leaking

105 CMR 451.383(B)	Fire Safety System: Facility not in compliance with State Building Code provisions on 	fire safety, storage within 18 inches of ceiling

LAUNDRY D1-5A

105 CMR 451.353*	Interior Maintenance: All washers are leaking

Inmate Bathroom D1-7

105 CMR 451.353	Interior Maintenance: Ceiling vent dusty

Staff Bathroom D1-9

105 CMR 451.126*	Hot Water: Hot water temperature recorded at 930F

Office D1-8

105 CMR 451.350*	Structural Maintenance: Ceiling damaged

105 CMR 451.353*	Interior Maintenance: Ceiling vent dusty

105 CMR 451.350*	Structural Maintenance: Wall damaged

105 CMR 451.350	Structural Maintenance: Floor damaged, water lifting tiles

Janitor’s Closet D1-46

105 CMR 451.130*	Plumbing: Plumbing not maintained in good repair, sink leaking

105 CMR 451.353*	Interior Maintenance: Unlabeled chemical bottle

105 CMR 451.353	Interior Maintenance: Ceiling vent dusty

Supply Room

No Violations Noted

TRAINING ROOM C1-6

FC 4-602.12(B)*	Cleaning of Equipment and Utensils; Frequency: Interior of microwave oven dirty

105 CMR 451.353	Interior Maintenance: Ceiling vent dusty

FC 4-601.11(c)	Cleaning of Equipment and Utensils, Objective: Vending machine drawer

dirty

Janitor’s Closet C1-9

105 CMR 451.353*	Interior Maintenance: Ceiling vent dusty

105 CMR 451.130*	Plumbing: Plumbing not maintained in good repair, sink leaking

105 CMR 451.353	Interior Maintenance: Paint & paper products stored on floor

Inmate Bathroom C1-11

105 CMR 451.123	Maintenance: Outlet GFI not operable

Staff Bathroom C1-10

105 CMR 451.353*	Interior Maintenance: Ceiling vent dusty

105 CMR 451.123*	Maintenance: Hole in ceiling

105 CMR 451.126*	Hot Water: Hot water temperature recorded at 870F

105 CMR 451.123	Maintenance: Outlet GFI not operable

INDUSTRIES CG-10

Inmate Bathroom

105 CMR 451.353*	Interior Maintenance: Ceiling vent dusty

Bubbler

105 CMR 451.130*	Plumbing: Plumbing not maintained in good repair, excessive water

pressure, near inmates break cage

Break Room CG-7

105 CMR 451.353*	Interior Maintenance: Ceiling vent dusty

FC 4-102.11(B)(2)	Materials for Construction and Repair; Multiuse: Unused single-service article not 	protected against contamination, left open, uncovered on table

Janitor’s Closet C-7

105 CMR 451.353*	Interior Maintenance: Missing drain cover

FC 6-501.16	Maintenance and Operation; Cleaning: Wet mop stored in bucket

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, faucet leaking

Staff Female Bathroom

105 CMR 451.126*	Hot Water: Hot water temperature recorded at 1030F

Male Bathroom

No Violations Noted

Tool Bin CG-9

105 CMR 451.353	Interior Maintenance: 001193 Rotor wiring damaged,

105 CMR 451.353	Interior Maintenance: A number of extension cords damaged

FL 21 & Fl 34

105 CMR 451.353	Interior Maintenance: Band saw and table saw missing grounding plugs

MAINTENANCE CG-13

105 CMR 451.350*	Structural Maintenance: Ceiling tiles missing and some damaged

FC 4-602.12(B)*	Cleaning of Equipment and Utensils; Frequency: Dirty microwave oven

FC 4-601.11(A)*	Cleaning of Equipment and Utensils, Objective: Food contact surface dirty, coffee maker

Female Bathroom/Locker CG-25

105 CMR 451.350*	Structural Maintenance: Ceiling damaged

105 CMR 451.353*	Interior Maintenance: Ceiling vent dusty

105 CMR 451.110(A)	Hygiene Supplies at Toilet and Handwash Sink: No soap at handwash sink

105 CMR 451.353	Interior Maintenance: Light cover damaged in sink area

Male Bathroom/Locker CG-24

No Violations Noted

Janitor’s Closet

105 CMR 451.353*	Interior Maintenance: Mop stored in bucket

105 CMR 451.353	Interior Maintenance: Ceiling vent dusty

105 CMR 451.130	Plumbing: No backflow preventer on threaded water bib

RECORDS AND CLASSIFICATION C2-14A

105 CMR 451.350*	Structural Maintenance: Ceiling tiles water stained throughout the area

Hallway-Janitor’s Closet C2-53

105 CMR 451.350*	Interior Maintenance: Unlabeled chemical bottle

Break Room hallway near C2-36

No Violations Noted

Male Bathroom C2-42

105 CMR 451.126	Hot Water: Hot water temperature recorded at 90oF

105 CMR 451.340	Illumination: Insufficient lighting, one light not working

Female Bathroom C2-41

No Violations Noted

Janitor’s Closet C2-35

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, faucet leaking

Break Room C2-49

FC 4-602.12(B)		             Cleaning of Equipment and Utensils; Frequency: Interior of microwave oven dirty

FC 4-601.11(A)	Cleaning of Equipment and Utensils, Objective: Food contact surface dirty, dirty coffee machine

105 CMR 451.123	Maintenance: Bubbler dirty

Spectrum C2-15C

Male Bathroom C2-27

105 CMR 451.353*	Interior Maintenance: Ceiling vent dusty

105 CMR 451.126*	Hot Water: Hot water temperature recorded at 860F

Female Bathroom C2-26

No Violations Noted

Inmate Bathroom

105 CMR 451.353*	Interior Maintenance: Ceiling vent dusty

Janitor’s Closet C2-24

105 CMR 451.353*	Interior Maintenance: Mop stored in bucket

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, faucet leaking

H.S.U

Officer’s Side B2-1A

Janitor’s Closet B2-64

105 CMR 451.353	Interior Maintenance: Mop stored in bucket

105 CMR 451.130	Plumbing: No backflow preventer on threaded water bib

Staff Bathroom B2 -90

No Violations Noted

X-Ray

105 CMR 451.130	Plumbing: No backflow preventer on threaded water bib

Trauma Room B2-15

105 CMR 451.350	Structural Maintenance: Wall damaged

Outpatient

No Violations Noted

Exam Room

No Violations Noted

Room B2-24

Unable to Inspect - Locked

Room B2-23

Unable to Inspect - Locked

Room B2-22

Unable to Inspect - Locked

PT Room B2-30

No Violations Noted

Dental Room B2-5

No Violations Noted

Inmate Bathroom B2-17

No Violations Noted

Pharmacy B2-31

No Violations Noted

Female Bathroom

105 CMR 451.110(B)	Hygiene Supplies at Toilet and Handwash Sink: No waste receptacle at handwash sink

105CMR 480.100                       Storage: Red bag waste container being used as a bathroom waste receptacle

Men’s Room

No Violations Noted

Nurse’s Side

Nurse’s Break Room B2-81

FC 4-903.11(A)(2) *		Protection of Clean Items, Storing: Single-service items uncovered and not protected 			             from contamination

FC 4-601.11(A)*	Cleaning of Equipment and Utensils, Objective: Food contact surface dirty, dirty coffee maker

Janitor’s Closet B2-91

No Violations Noted

Staff Bathroom B2-60

No Violations Noted

Mini Pharmacy B2-58

No Violations Noted

Storage B2-56A

No Violations Noted

Waiting Area B2-36

No Violations Noted

Break Room/storage B2-8

No Violations Noted

HSU Records

Unable to Inspect - Locked

Isolation/Inpatient

105 CMR 451.353*	Interior Maintenance: Vents covered

Janitor’s Room

No Violations Noted

Utility Room/B2-80

No Violations Noted

Isolation Cell B2-69

105 CMR 451.350	Structural Maintenance: Wall damaged

Cells B2-83

105 CMR 451.353	Interior Maintenance: Door splash guard damaged in cell #15

105 CMR 451.103	Mattresses damaged, in cells # 8 & 11

Shower 1 B2-61

105 CMR 451.123*	Maintenance: Floor damaged

Shower 2

Unable to Inspect – Limited Access

Shower 3

Unable to Inspect – In Use

CHAPEL C2-9

Inmate Bathroom C2-8

105 CMR 451.110(B)	Hygiene Supplies at Toilet and Handwash Sink: No waste receptacle at handwash sink

Storage Closet C2-7

Unable to Inspect – Limited Access

MOSQUE C2-87

105 CMR 451.126*	Hot Water: Hot water temperature 950F

Inmate Bathroom

105 CMR 451.110(B)*	Hygiene Supplies at Toilet and Handwash Sink: No waste receptacle at handwash sink

C2-6

Unable to Inspect – Limited Access

C2-10

105 CMR 451.350*	Structural Maintenance: Ceiling tiles water stained

NORTH STP M F2-19

105 CMR 451.320*	Cell Size: Inadequate floor space in all cells

Staff Bathroom

No Violations Noted

Men’s Bathroom F2-21

No Violations Noted

Female Bathroom F2-20

No Violations Noted

Janitors Closet F2-19

105 CMR 451.353*	Interior Maintenance: Mop stored in bucket

Kitchen Area F2-8

FC 4-602.12(B)*		Cleaning of Equipment and Utensils; Frequency: Dirty microwave oven

105 CMR 451.126*	Hot Water: Hot water temperature recorded at 1340F

105 CMR 451.353*	Interior Maintenance: Ceiling vent dusty

FC 6-501.114(A)	Maintenance and Operations; Maintaining Premises: Nonfunctional equipment not 	repaired or removed from premises, ice machine

Visiting Bathroom F2-24

Unable to Inspect – In Use

Control F2-16

105 CMR 451.353*	Interior Maintenance: Ceiling vent dusty

FC 4-602.12(B)		             Cleaning of Equipment and Utensils; Frequency: Interior of microwave

oven dirty

FC 4-501.11(B)	                          Maintenance and Operation, Equipment: Equipment components not

maintained in a state of good repair, damaged refrigerator door

Staff Bathroom in Control

105 CMR 451.110(A)	Hygiene Supplies at Toilet and Handwash Sink: No soap at

handwash sink, bar soap being used

Recreation Deck F2-10A

No Violations Noted

Office

No Violations Noted

Cells

105 CMR 451.353	Interior Maintenance: Cracked wall cell # M3-09

Showers M3 S1-S4

105 CMR 451.123*	Maintenance: Paint peeling in all showers

F2M-103

105 CMR 451.353*	Interior Maintenance: Ceiling vent dusty

105 CMR 451.130	Plumbing: No backflow preventer on threaded water bib

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, faucet leaking

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, drain cover missing

105 CMR 451.383(B)	Fire Safety System: Facility not in compliance with State Building Code provisions on fire safety, boxes piled to ceiling, no 18 inch open space

NORTH STP L F2-L100

105 CMR 451.320*	Cell Size: Inadequate floor space in cells

Recreation Deck

105 CMR 451.360*	Protective Measures: Effective measures against the presence of birds on the premises not taken, bird feces on the deck

Janitor’s Closet

105 CMR 451.130	Plumbing: No backflow preventer on slop sink

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, faucet leaking

105 CMR 451.383(B)	Fire Safety System: Facility not in compliance with State Building Code provisions on fire safety, boxes piled to ceiling, no 18 inch open space

Cells

105 CMR 451.103*	Mattresses: Mattress damaged in cell # L3-13

105 CMR 451.353*	Interior Maintenance: Vent blocked in cell # L3-05, 06, 22 & 23

105 CMR 451.350	Structural Maintenance: Wall damaged, paint cell # L3-24

Showers S1-4

105 CMR 451.123*	Maintenance: Peeling paint in all showers

L2M2 POD F1-20A

Female Bathroom

Unable to Inspect - Locked

Male Bathroom

Unable to Inspect - Locked

Nurse’s Station

Unable to Inspect - Locked

L2 CELL BLOCK F1-L111

105 CMR 451.350*	Structural Maintenance: Ceiling damaged above Officer’s desk

105 CMR 451.320*	Cell Size: Inadequate floor space in all cells

Storage F1-L100

FC 4-602.12(B)*                        Cleaning of Equipment and Utensils; Frequency: Interior of microwave oven dirty

Janitor’s Closet

105 CMR 451.353*	Interior Maintenance: Ceiling vent dusty

105 CMR 451.130*	Plumbing: Plumbing not maintained in good repair, faucet leaking

105 CMR 451.353*	Interior Maintenance: Missing drain cover

Staff Bathroom

105 CMR 451.130*	Plumbing: Plumbing not maintained in good repair, floor drain blocked and rusty

105 CMR 451.126		Hot Water: Hot water temperature recorded at 134oF

105 CMR 451.110(A)	Hygiene Supplies at Toilet and Handwash Sink: No soap at

handwash sink, bar soap being used

Common Sink

105 CMR 451.353*	Interior Maintenance: Cabinet damaged

Recreation Deck

105 CMR 451.360*	Protective Measures: Effective measures against the presence of birds on the premises not taken, bird feces on the deck

Bubbler

No Violations Noted

Cells

105 CMR 451.353	Interior Maintenance: Vent blocked in cell # L2-13,

105 CMR 451.350	Structural Maintenance: Wall damaged in cell # L2-11, 20 & 64

105 CMR 451.104	Beds: Inmates sleeping on floor, in cell # L2-07

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, water leaking between cells # L2-

55 & L2-56

105 CMR 451.340	Illumination: Insufficient lighting, lower light out in cell # L2-53

105 CMR 451.340	Illumination: Insufficient lighting, light blocked in cell # L2-24

105 CMR 451.103	Mattresses: Mattress damaged, in cell # L2-22

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, low water pressure in cell # L2-48

105 CMR 451.350	Structural Maintenance: Wall damaged, paint in cell # L2-11 & 26

105 CMR 451.102	Pillows and Linens: Pillow/linens damaged in cell # L2-53

Showers

105 CMR 451.123*	Maintenance: Peeling paint in all showers

M2 CELL BLOCK F1-M111

105 CMR 451.320*	Cell Size: Inadequate floor space in all cells

Storage F1-M100

FC 4-602.12(B)*		Cleaning of Equipment and Utensils; Frequency: Interior of microwave oven dirty

FC 4-102.11(B)(2)*		Materials for Construction and Repair; Multiuse: Unused single-service article not 			             protected against contamination

Janitor’s Closet F1-M105

105 CMR 451.130*	Plumbing: Plumbing not maintained in good repair, faucet leaks

105 CMR 451.353*	Interior Maintenance: Missing drain cover

105 CMR 451.353*	Interior Maintenance: Mop stored in bucket

Staff Bathroom

105 CMR 451.110(A)	Hygiene Supplies at Toilet and Handwash Sink: No soap at handwash sink,

bar soap being used

Common Sink

105 CMR 451.130*	Plumbing: Plumbing not maintained in good repair, sprayer damaged

105 CMR 451.353*	Interior Maintenance: Cabinet damaged

Recreation Deck

105 CMR 451.360*	Protective Measures: Effective measures against the presence of birds on the premises not taken, bird feces covers the deck

Bubbler

105 CMR 451.130*	Plumbing: Plumbing not maintained in good repair, excessive water pressure

Cells

105 CMR 451.353*	Interior Maintenance: Vents blocked in cell # M2-59 & 62

105 CMR 451.353	Interior Maintenance: Water leaking from ceiling outside cell # M2-55

105 CMR 451.353	Interior Maintenance: Water leaking from ceiling, floods cell # M2-46

105 CMR 451.353	Interior Maintenance: Floor drain blocked in front of cell # M2-49

Showers M2-S1-4

105 CMR 451.123*	Maintenance: Peeling paint in all showers

105 CMR 451.123*	Maintenance: Soap scum on all shower walls

105 CMR 451.123*	Maintenance: Wall vent dusty in all showers

105 CMR 451.123*	Maintenance: Mold like substance in shower # 4

L1M1 POD

Unit Team FG-23

Unable to Inspect - Locked

Female Bathroom

Unable to Inspect - Locked

Male Bathroom

Unable to Inspect - Locked

Nurse’s Station F6-24

105 CMR 451.103	Mattresses: Mattress damaged

Janitor’s Closet

Unable to Inspect - Locked

L1 CELL BLOCK FG-20A

105 CMR 451.320*	Cell Size: Inadequate floor space in all cells

Storage FG L100

FC 4-501.11(A)	Maintenance and Operation, Equipment: Equipment not maintained in a state of good 	repair, refrigerator gasket damaged, door not closing

Janitor’s Closet FG-105

105 CMR 451.130*	Plumbing: Plumbing not maintained in good repair, pipes leaking and ceiling water stained

105 CMR 451.350*	Structural Maintenance: Ceiling damaged

105 CMR 451.353*	Interior Maintenance: Ceiling vent dusty

105 CMR 451.353*	Interior Maintenance: Missing drain cover

105 CMR 451.353*	Interior Maintenance: Ceiling is covered in a mold like substance

105 CMR 451.353*	Interior Maintenance: Light not functioning correctly

Staff Bathroom FG-L10

No Violations Noted

Staff Work Station

105 CMR 451.123	Maintenance: Chair damaged

105 CMR 451.350	Structural Maintenance: Ceiling damaged in common areas

Common Sink

105 CMR 451.130*	Plumbing: Plumbing not maintained in good repair, sprayer broken

105 CMR 451.353*	Interior Maintenance: Cabinet damaged

Recreation Deck

No Violations Noted

Bubbler

No Violations Noted

Cells

105 CMR 451.353	Interior Maintenance: Vent blocked in cell #L1-04 & 09

105 CMR 451.353	Interior Maintenance: Floor drain blocked in front of cell # L1-11

105 CMR 451.103	Mattresses: Mattress damaged in cell # L1-25 & 36

105 CMR 451.102	Pillows and Linens: Pillow/linens damaged in cell # L1-48

105 CMR 451.350	Structural Maintenance: Wall damaged cell # L1-28

Showers

105 CMR 451.123*	Maintenance: Paint removed or peeling in all showers

105 CMR 451.123*	Maintenance: Ceiling damaged in # 1, 3, 4, 5 & 7

105 CMR 451.130*	Plumbing: Plumbing not maintained in good repair, shower leaking in cell

#3, 5 & 6

M1 CELL BLOCK FG-M111

105 CMR 451.320*	Cell Size: Inadequate floor space in all cells

Storage FG M100

FC 4-102.11(B)(2)*		Materials for Construction and Repair; Multiuse: Unused single-service article not 				protected against contamination

FC 4-602.12(B)*	            Cleaning of Equipment and Utensils; Frequency: Interior of microwave oven dirty

Janitor’s Closet FG-M105

105 CMR 451.350	Structural Maintenance: Ceiling not easily cleanable

105 CMR 451.130*	Plumbing: Plumbing not maintained in good repair, water leaking from upstairs

105 CMR 451.353*	Interior Maintenance: Missing drain cover

Staff Bathroom FG-M106

No Violations Noted

Common Sink

105 CMR 451.130*	Plumbing: Plumbing not maintained in good repair, sprayer broken

105 CMR 451.353*	Interior Maintenance: Cabinet damaged

Recreation Deck

No Violations Noted

Bubbler

No Violations Noted

Cells

105 CMR 451.353	Interior Maintenance: Vents blocked in cell # M1-02, 20, 36 & 40

105 CMR 451.353	Interior Maintenance: Ceiling vents dusty in cell # M1-21, 46, 54 & 60

Showers M1 S1-8

105 CMR 451.123*	Maintenance: Peeling paint in shower # 1, 2, 4, 5, 6 & 7

105 CMR 451.350	Structural Maintenance: Floor damaged lifting in front of shower # S4

N2P2 POD

Unit Team

FC 4-102.11(B)(2)*		Materials for Construction and Repair; Multiuse: Unused single-service article not 			             protected against contamination

Female Bathroom

105 CMR 451.353*	Interior Maintenance: Ceiling vent dusty

Male Bathroom

No Violations Noted

Nurse’s Station

No Violations Noted

N2 CELL BLOCK F1-N111

105 CMR 451.320*	Cell Size: Inadequate floor space in all cells

Storage F1-N100

105 CMR 451.353*	Interior Maintenance: Ceiling vent dusty

105 CMR 451.353*	Interior Maintenance: Unlabeled chemical bottle

Janitor’s Closet F1-N06

105 CMR 451.353*	Interior Maintenance: Missing drain cover

105 CMR 451.353	Interior Maintenance: Mop stored in bucket

Staff Bathroom F1-N06

105 CMR 451.353*	Interior Maintenance: Ceiling vent dusty

105 CMR 451.353*	Interior Maintenance: Blocked floor drain

Staff Work Station

105 CMR 451.123	Maintenance: Chair damaged

Common Sink

105 CMR 451.130*	Plumbing: Plumbing not maintained in good repair, sprayer broken

Recreation Deck

No Violations Noted

Bubbler

No Violations Noted

Cells

105 CMR 451.353*	Interior Maintenance: Vents blocked in cell # N2-01, 3, 4, 10, 28, 32, 35, 39, 41, 47, 55, 62 & 63

105 CMR 451.102	Pillows and Linens: Pillow/linens damaged in cell # N2-05

105 CMR 451.350	Structural Maintenance: Ceiling damaged in cell # N2-05 & N2-21

105 CMR 451.353	Interior Maintenance: Outlet burned in cell # N2-05

105 CMR 451.101	Blankets: Blanket damaged; in cell # N2-36

105 CMR 451.353	Interior Maintenance: Wall dirty in cell # N2-05, 32, 33, 38, 44, 61, 63

105 CMR 451.353	Interior Maintenance: Blocked floor drains outside cell #N2-12, 13, 17 & 29

Showers S1-8

Showers 1, 3, 5 ,7 not inspected in use

105 CMR 451.123*	Maintenance: Peeling paint in all showers

105 CMR 451.123	Maintenance: Ceiling damaged in shower # 8

P2 CELL BLOCK F1-P111

105 CMR 451.320*	Cell Size: Inadequate floor space in all cells

Storage F1-P100

FC 4-602.12(B) 		Cleaning of Equipment and Utensils; Frequency: Interior of microwave

oven dirty

Staff Work Station

105 CMR 451.123	Maintenance: Chair damaged

105 CMR 451.353	Interior Maintenance: Ceiling dirty in common areas

Janitor’s Closet

105 CMR 451.353*	Interior Maintenance: Mop stored in bucket

105 CMR 451.353*	Interior Maintenance: Missing drain cover

Staff Bathroom F1-106

No Violations Noted

Common Sink

105 CMR 451.130*	Plumbing: Plumbing not maintained in good repair, sprayer missing

105 CMR 451.353*	Interior Maintenance: Cabinet water damaged

Recreation Deck

No Violations Noted

Bubbler

No Violations Noted

Cells

105 CMR 451.350	Structural Maintenance: Wall damaged in cell # P2-62

105 CMR 451.353*	Interior Maintenance: Vents blocked in cell # P2 – 25, 26, 29, 39, 41, 43, 46 & 52

105 CMR 451.101	Blankets: Blanket damaged in cell #  P2-24 & 36

105 CMR 451.353	Interior Maintenance: Wall dirty cell # P2-02, 06, 09, 10, 18, 27 & 31

105 CMR 451.353	Interior Maintenance: Ceiling dirty cell # P2-06, 09 & 18

105 CMR 451.353	Interior Maintenance: Blocked floor drains outside cell # P2-17, 26 & 27, 58 & 59

Showers P2S1-8

Showers Unable to Inspect – In Use 1, 2, 6 & 8

105 CMR 451.123*	Maintenance: Peeling paint in all showers

105 CMR 451.123*	Maintenance: Ceiling & wall damaged in shower #5

105 CMR 451.123*	Maintenance: Soap scum on shower wall # 3

N1P1 POD

Female Bathroom

Unable to Inspect - Locked

Male Bathroom

Unable to Inspect - Locked

Nurse’s Station

Unable to Inspect – Locked

Janitor’s Closet

105 CMR 451.353*	Interior Maintenance: Missing drain cover

105 CMR 451.350*	Structural Maintenance: Ceiling damaged, water leak

N1 CELL BLOCK FG-N111

105 CMR 451.320*	Cell Size: Inadequate floor space in cells

105 CMR 451.350*	Structural Maintenance: Missing ceiling tiles

Storage

FC 4-602.12(B)*	             Cleaning of Equipment and Utensils; Frequency: Interior of microwave oven dirty

FC 4-501.11(A)*	Maintenance and Operation, Equipment: Equipment not maintained in a state of good 	repair, microwave damaged

105 CMR 451.353	Interior Maintenance: Ceiling vent dusty

Janitor’s Closet FG-N105

105 CMR 451.353*	Interior Maintenance: Light not functioning

105 CMR 451.353*	Interior Maintenance: Ceiling vent dusty

105 CMR 451.350*	Structural Maintenance: Missing ceiling

105 CMR 451.353*	Interior Maintenance: Missing drain cover

Staff Bathroom

105 CMR 451.353	Interior Maintenance: Ceiling vent dusty

Common Sink

105 CMR 451.130*	Plumbing: Plumbing not maintained in good repair, sprayer broken

105 CMR 451.353*	Interior Maintenance: Cabinet damaged

Recreation Deck

No Violations Noted

Bubbler

No Violations Noted

Cells

105 CMR 451.102*	Pillows and Linens: Linens damaged in cell # N1-57

105 CMR 451.353*	Interior Maintenance: Vents blocked in cell # N1-26, 53 & 60

105 CMR 451.103	Mattresses: Mattress damaged in cell # N1-30

105 CMR 451.353	Interior Maintenance: Blocked floor drains outside cell # N1-11, 22 & 23

105 CMR 451.350	Structural Maintenance: Ceiling damaged, water leaking in cell # N1-16, 33 &

N1-45

105 CMR 451.350	Structural Maintenance: Ceiling damaged, water leaking common area

105 CMR 451.353	Interior Maintenance: Floor dirty in cell # N1-08

105 CMR 451.350	Structural Maintenance: Ceiling damaged, water leaking into light in

cell # N1-19

Showers S1-8

105 CMR 451.123*	Maintenance: Peeling paint in all showers

105 CMR 451.130*	Plumbing: Plumbing not maintained in good repair, shower leaking in # 5

105 CMR 451.123*	Maintenance: Ceiling damaged in # 1

105 CMR 451.123	Maintenance: Blocked vent in shower # 2

P1 CELL BLOCK FG-P111

105 CMR 451.320*	Cell Size: Inadequate floor space in all cells

Storage FG-P100

105 CMR 451.353*	Interior Maintenance: Ceiling vent dusty

FC 4-102.11(B)(2)*		Materials for Construction and Repair; Multiuse: Unused single-service article not 			             protected against contamination

Janitor’s Closet FG-P105

105 CMR 451.353*	Interior Maintenance: Ceiling vent dusty

105 CMR 451.350*	Structural Maintenance: Ceiling damaged

105 CMR 451.353*	Interior Maintenance: Missing drain cover

105 CMR 451.353	Interior Maintenance: Mop stored in bucket

Staff Bathroom FG-P106

105 CMR 451.353	Interior Maintenance: Ceiling vent dusty

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, toilet leaking

Common Sink

105 CMR 451.130*	Plumbing: Plumbing not maintained in good repair, sink not operable

105 CMR 451.353*	Interior Maintenance: Cabinet has water damaged

Recreation Deck

No Violations Noted

Bubbler

No Violations Noted

Cells

105 CMR 451.353	Interior Maintenance: Vents blocked in cell # P1-15, 28, 35, 40 & 51

105 CMR 451.353	Interior Maintenance: Blocked floor drains outside in cell # P1-04, 10-11, 16,

17 & 28

105 CMR 451.350	Structural Maintenance: Ceiling damaged, water leaking in cells # P1-40, 45 &

61

105 CMR 451.353	Interior Maintenance: Wall dirty in cell # P1-18 & 19

Showers

105 CMR 451.123*	Maintenance: Peeling paint in all showers

105 CMR 451.123*	Maintenance: Soap scum on all shower walls

105 CMR 451.123	Maintenance: Ceiling damaged in all showers

105 CMR 451.123	Maintenance: Wall vent dusty in all showers

105 CMR 451.123	Maintenance: Floor damaged in # 7

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, shower leaking in #8

105 CMR 451.350	Structural Maintenance: Floor damaged in front of shower # 7

SOUTH SMU J E2-4

Recreation Deck

105 CMR 451.360*	Protective Measures: Effective measures against the presence of birds on the premises not taken, bird feces on the deck

Male Bathroom E2-20

No Violations Noted

Female Bathroom E2-21

No Violations Noted

Scrub Room

No Violations Noted

Janitor’s Closet E2-19

105 CMR 451.353*	Interior Maintenance: Unlabeled chemical bottle

105 CMR 451.123	Maintenance: Toilet/Handwash sink damaged, faucet dripping

Kitchen

FC 4-903.11(A)(2)* 		Protection of Clean Items, Storing: Single-service items uncovered and not protected 			             from contamination, not stored inverted

FC 4-501.11(A)	                          Maintenance and Operation, Equipment: Equipment not maintained in a state

of good repair, ice machine leaking

FC 3-304.12(A)	                          Preventing Contamination from Utensils: Ice scoop not stored properly

Visitor’s Bathroom E-29

No Violations Noted

Protocol Room

No Violations Noted

Cells

105 CMR 451.103	Mattresses: Mattress damaged in cell # J3-04

105 CMR 451.104	Beds: Bed not in good repair in cell # J3-23

105 CMR 451.101	Blankets: Blanket damaged in cell # J3-13

105 CMR 451.123	Maintenance: Damaged paint in cell # J3-12, 19, 22, 24 & 26

105 CMR 451.353	Interior Maintenance: Vents blocked in cell # J3-08, 14, 16, 22 & 26

Showers J3-S1-4

105 CMR 451.123*	Maintenance: Soap scum on shower walls

105 CMR 451.123*	Maintenance: Peeling paint in all showers

105 CMR 451.123*	Maintenance: Generally dirty

Janitor’s Closet

105 CMR 451.353*	Interior Maintenance: Ceiling vent dusty

SOUTH SMU K E2-10B

Recreation Deck

105 CMR 451.360*	Protective Measures: Effective measures against the presence of birds on the premises not taken, bird feces on the deck

Janitor’s Closet E2-K103

105 CMR 451.353*	Interior Maintenance: Ceiling vent dusty

105 CMR 451.353*	Interior Maintenance: Mop stored on floor

105 CMR 451.130	Plumbing: No backflow preventer on threaded water bib

105 CMR 451.383(B)	Fire Safety System: Facility not in compliance with State Building Code provisions on fire safety, boxes piled to ceiling

Cells

105 CMR 451.350	Structural Maintenance: Wall paint peeling in cell # K3-01 & 04

105 CMR 451.353	Interior Maintenance: Vent blocked in cell # K3-10

105 CMR 451.350	Structural Maintenance: Wall damaged in cell # K3-02, 16, 17, 27, 28 & 29

105 CMR 451.350	Structural Maintenance: Flooring in cell # K3-23

105 CMR 451.353	Interior Maintenance: Ceiling dirty in cell # K3-03, 22 & 25

105 CMR 451.101	Blankets: Blanket damaged in cell # K3-26 & 28

Showers K3-S1-4

105 CMR 451.123*	Maintenance: Peeling paint in all showers

105 CMR 451.123*	Maintenance: Soap scum on all shower walls

G2H2 POD South

Janitor’s Closet

105 CMR 451.130*	Plumbing: Plumbing not maintained in good repair, sink leaking

Bathrooms

No Violations Noted

Nurse’s Station E1-9

105 CMR 451.103	Mattresses: Mattress damaged

G2 CELL BLOCK

105 CMR 451.320*	Cell Size: Inadequate floor space in all cells

Storage

FC 4-602.12(B)*		Cleaning of Equipment and Utensils; Frequency: Interior of microwave oven dirty

Janitor’s Closet E1 G105

105 CMR 451.353*	Interior Maintenance: Ceiling vent dusty

105 CMR 451.353*	Interior Maintenance: Mop stored in bucket

105 CMR 451.353*	Interior Maintenance: Missing drain cover

Staff Bathroom

105 CMR 451.353*	Interior Maintenance: Ceiling vent dusty

Common Sink

105 CMR 451.130*	Plumbing: Plumbing not maintained in good repair, sprayer broken

105 CMR 451.130*	Plumbing: Plumbing not maintained in good repair, sink leaking

Recreation Deck

No Violations Noted

Bubbler

No Violations Noted

Cells

105 CMR 451.350	Structural Maintenance: Hole in wall in cell # G2-39

105 CMR 451.103	Mattresses: Mattress damaged in cell # G2-31

105 CMR 451.353	Interior Maintenance: Vents blocked in cells # G2-09, 12, 13, 24, 27, 47 & 58

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, low pressure in

cell # G2-28

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, water leak in

cell # G2-53

Showers G2-S1-8

105 CMR 451.123*	Maintenance: Peeling paint in all showers

105 CMR 451.123*	Maintenance: Soap scum on all shower walls

105 CMR 451.130*	Plumbing: Plumbing not maintained in good repair, shower leaking in # 3

105 CMR 451.123*	Maintenance: Hole in ceiling in shower #1 & 3

105 CMR 451.123*	Maintenance: Ceiling damaged in shower # 2

H2 CELL BLOCK E1-H111

105 CMR 451.320*	Cell Size: Inadequate floor space in all cells

Storage E1-4100

No Violations Noted

Janitor’s Closet E1-H105

105 CMR 451.353*	Interior Maintenance: Ceiling vent dusty

105 CMR 451.123	Maintenance: Toilet/Handwash sink damaged, faucet dripping

Staff Bathroom E1-H106

105 CMR 451.110(A)	Hygiene Supplies at Toilet and Handwash Sink: No soap at

handwash sink, bar soap being used

105 CMR 451.126		Hot Water: Hot water temperature recorded at 140oF

Common Sink

105 CMR 451.130*	Plumbing: Plumbing not maintained in good repair, faucet missing

Recreation Deck

No Violations Noted

Bubbler

No Violations Noted

Cells

105 CMR 451.353	Interior Maintenance: Vents blocked in cell # H2-02, 04, 26, 30, 47, 56 & 58

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, water leaking from ceiling due to

faulty plumbing in cell # H2-13

105 CMR 451.344	Illumination in Habitable Areas: Light fixture not working properly in cell # H2-07,

08 & 21

Showers H2-S1-4

105 CMR 451.123*	Maintenance: Peeling paint in all showers

105 CMR 451.123*	Maintenance: Soap scum on all shower walls

105 CMR 451.123*	Maintenance: Ceiling damaged in showers # 5 & 8

105 CMR 451.123*	Maintenance: Baseboard damaged in showers # 4 & 8

105 CMR 451.123*	Maintenance: Hole in ceiling in shower # 1

J2K2 POD E1-5111

Bathrooms E1-23

Unable to Inspect - Locked

Nurse’s Station

105 CMR 451.103	Mattresses: Mattress damaged

J2 CELL BLOCK

105 CMR 451.320*	Cell Size: Inadequate floor space in all cells

105 CMR 451.350*	Structural Maintenance: Water stained on ceiling in common area

Storage E1-5100

105 CMR 451.353*	Interior Maintenance: Ceiling vent dusty

FC 4-602.12(B)*	             Cleaning of Equipment and Utensils; Frequency: Interior of microwave oven dirty

Janitor’s Closet E1-J105

105 CMR 451.353*	Interior Maintenance: Mop stored in bucket

105 CMR 451.353*	Interior Maintenance: Missing drain cover

105 CMR 451.353	Interior Maintenance: Ceiling vent dusty

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, faucet leaking

Staff Bathroom E1-J106

105 CMR 451.126		Hot Water: Hot water temperature recorded at 140oF

Common Sink

105 CMR 451.130*	Plumbing: Plumbing not maintained in good repair, no faucet

105 CMR 451.353*	Interior Maintenance: Cabinet rotted

Recreation Deck

No Violations Noted

Bubbler

105 CMR 451.130*	Plumbing: Plumbing not maintained in good repair, no water

Cells

105 CMR 451.353	Interior Maintenance: Wall vent blocked in cell # J2-03, 08, 21, 32, 37, 44, 50, 51, 52, 53 & 63

105 CMR 451.353	Interior Maintenance: Blocked floor drains outside cell #J2-16 & 17

105 CMR 451.353	Interior Maintenance: Ceiling damaged in common area

Showers J2-S1-8

105 CMR 451.123*	Maintenance: Peeling paint in all showers

105 CMR 451.123*	Maintenance: Ceiling damaged in # 1, 3, 4, 5, 6, 7 & 8

105 CMR 451.130*	Plumbing: Plumbing not maintained in good repair, shower leaking in #7

105 CMR 451.360*	Protective Measures: Drain flies observed in # J2-07

105 CMR 451.123	Maintenance: No light in # J2-S7

105 CMR 451.123	Maintenance: Shower # J2-S1 out of order

K2 CELL BLOCK E1-K1

105 CMR 451.320*	Cell Size: Inadequate floor space in all cells

105 CMR 451.350*	Structural Maintenance: Ceiling damaged in the block common area

Storage E1-K100

FC 4-602.12(B)*		Cleaning of Equipment and Utensils; Frequency: Interior of microwave

oven dirty

Janitor’s Closet E1-K105

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, faucet leaking

Staff Bathroom

105 CMR 451.123*	Maintenance: Sink cracked

105 CMR 451.126	Hot Water: Hot water temperature recorded at 142 oF

Common Sink

105 CMR 451.130*	Plumbing: Plumbing not maintained in good repair, sprayer broken

Recreation Deck

No Violations Noted

Bubbler

No Violations Noted

Cells

105 CMR 451.353*	Interior Maintenance: Blocked vent in cell # K2-14, 24, 27, 28, 36 & 50

105 CMR 451.353	Interior Maintenance: No power in cell # K2-34

Showers K2-S1-6

105 CMR 451.123*	Maintenance: Peeling paint in all showers

105 CMR 451.123*	Maintenance: Soap scum on walls in all showers

105 CMR 451.123*	Maintenance: Tile damaged outside of shower # 7

105 CMR 451.123*	Maintenance: Ceiling damaged in showers # 2, 4, 5 & 6

105 CMR 451.123*	Maintenance: Mold like substance in showers # 1, 2 & 6

105 CMR 451.360	Protective Measures: Drain flies observed in shower # 6

G1H1 POD EG 6A

Janitor’s Closet

Unable to Inspect - Locked

Bathrooms EG-8

Unable to Inspect - Locked

Nurse’s Station E6-9

105 CMR 451.103	Mattresses: Mattress damaged

G1 CELL BLOCK EG-6111

105 CMR 451.320*	Cell Size: Inadequate floor space in all cells

Storage

FC 4-903.11(A)(2) 		Protection of Clean Items, Storing: Single-service items uncovered and not protected 			             from contamination

105 CMR 451.353*	Interior Maintenance: Ceiling vent dusty

FC 4-602.12(B)		             Cleaning of Equipment and Utensils; Frequency: Interior of microwave oven dirty

Janitor’s Closet

105 CMR 451.353*	Interior Maintenance: Mop stored in bucket

105 CMR 451.353	Interior Maintenance: Missing drain cover

105 CMR 451.353*	Interior Maintenance: Ceiling vent dusty

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, faucet leaking

Staff Bathroom EG-6106

105 CMR 451.126	Hot Water: Hot water temperature recorded at 137oF

Common Sink

105 CMR 451.130*	Plumbing: Plumbing not maintained in good repair, faucet leaking

105 CMR 451.130*	Plumbing: Plumbing not maintained in good repair, sprayer broken

Recreation Deck

No Violations Noted

Bubbler

No Violations Noted

Cells

105 CMR 451.353	Interior Maintenance: Vent blocked in cell # G1-06, 30, 41, 44, 51, 56, 58 & 62

105 CMR 451.101	Blankets: Blanket damaged in cell # G1-48 & 49

Showers

105 CMR 451.123*	Maintenance: Peeling paint in showers # 1, 3, 4, 6 & 8

105 CMR 451.123*	Maintenance: Ceiling damaged in showers # 1, 2, 3 & 4

H1 CELL BLOCK E6-H111

105 CMR 451.320*	Cell Size: Inadequate floor space in all cells

Storage E6 H100

FC 4-903.11(A)(2)* 		Protection of Clean Items, Storing: Single-service items uncovered and not protected 			             from contamination

Janitor’s Closet E6-H105

105 CMR 451.353*	Interior Maintenance: Mop stored in bucket

105 CMR 451.353*	Interior Maintenance: Missing drain cover

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, faucet leaking

Staff Bathroom

105 CMR 451.126	Hot Water: Hot water temperature recorded at 137oF

Staff Work Station

105 CMR 451.123	Maintenance: Chair damaged

Common Sink

105 CMR 451.130*	Plumbing: Plumbing not maintained in good repair, sprayer broken

FC 4-602.12(B) 		Cleaning of Equipment and Utensils; Frequency: Interior of microwave

oven dirty

Recreation Deck

No Violations Noted

Bubbler

No Violations Noted

Cells

105 CMR 451.353	Interior Maintenance: Vent blocked in cell # H1-01, 09, 16, 47 & 61

105 CMR 451.350	Structural Maintenance: Wall damaged in cell # H1-23

Showers H1-S1-8

105 CMR 451.123	Maintenance: All showers not easily cleanable

105 CMR 451.123	Maintenance: Peeling paint in all showers

J1K1 POD EG-21A

Bathrooms

Unable to Inspect

Nurse’s Station

No Violations Noted

J1 CELL BLOCK EG-5111

105 CMR 451.320*	Cell Size: Inadequate floor space in all cells

Storage EG 5100

FC 4-602.12(B)*		Cleaning of Equipment and Utensils; Frequency: Interior of microwave

oven door damaged

FC 4-903.11(A)(2)* 		Protection of Clean Items, Storing: Single-service items uncovered and not protected 			             from contamination

Janitor’s Closet EG-5105

105 CMR 451.353*	Interior Maintenance: Missing drain cover

105 CMR 451.350*	Structural Maintenance: Ceiling damaged

Staff Bathroom EG-5106

105 CMR 451.353	Interior Maintenance: Ceiling vent dusty

Common Sink

105 CMR 451.130*	Plumbing: Plumbing not maintained in good repair, sprayer missing

Recreation Deck

No Violations Noted

Bubbler

105 CMR 451.130*	Plumbing: Plumbing not maintained in good repair, excessive water pressure

Cells

105 CMR 451.350	Structural Maintenance: Missing tile outside of cell # J1-17

105 CMR 451.353	Interior Maintenance: Blocked vent in cell # J1-04, 05, 22, 52 & 64

105 CMR 451.101	Blankets: Blanket damaged cell # J1-02 & 24

105 CMR 451.123	Maintenance: Toilet/Handwash sink damaged, toilet leaking in cell # J1-32

105 CMR 451.353	Interior Maintenance: Water leaking from ceiling in cell # J1-24, 25 & 26

105 CMR 451.353	Interior Maintenance: Wall dirty cell # J1 -20, 52, & 64

105 CMR 451.130*	Plumbing: Plumbing not maintained in good repair, floor drain blocked by

cell # J1-11

Showers

105 CMR 451.123*	Maintenance: Paint peeling in all showers

105 CMR 451.123*	Maintenance: Ceiling damaged in #2

K1 CELL BLOCK EG-K111

105 CMR 451.320*	Cell Size: Inadequate floor space in all cells

Storage EG K100

FC 4-602.12(B)*		Cleaning of Equipment and Utensils; Frequency: Interior of microwave

Oven dirty

Janitor’s Closet EG-K105

105 CMR 451.353*	Interior Maintenance: Unlabeled chemical bottle

105 CMR 451.350*	Structural Maintenance: Ceiling damaged

Staff Bathroom EG-K106

105 CMR 451.126	Hot Water: Hot water temperature recorded at 1380F

Common Sink

105 CMR 451.130*	Plumbing: Plumbing not maintained in good repair, sprayer damaged

Recreation Deck

No Violations Noted

Bubbler

No Violations Noted

Cells

105 CMR 451.353*	Interior Maintenance: Vent blocked in cell # K1-34, 48 & 55

105 CMR 451.350*	Structural Maintenance: Wall damaged between cell # K1-51

105 CMR 451.350*	Structural Maintenance: Wall paint peeling in cell # K1-38

105 CMR 451.101	Blankets: Blanket damaged cell # K1-36

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, flooding cell # K1-18

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, toilet leak in

cell # K1-31 & K1-52

105 CMR 451.353	Interior Maintenance: Wall dirty in cell # K1-38

Showers

105 CMR 451.123*	Maintenance: Paint peeling in all showers

105 CMR 451.123*	Maintenance: Ceiling damaged in showers # 1, 2 & 6

105 CMR 451.123*	Maintenance: Floor damaged in shower # 4

105 CMR 451.130*	Plumbing: Plumbing not maintained in good repair, shower leaking in # 6

Observations and Recommendations

- The inmate population was 1363 at the time of inspection

- The inmate’s bathroom had been removed from the Barber Shop area

- Cell J1-01 and K1-01 used for storage

This facility does not comply with the Department’s Regulations cited above. In accordance with 105 CMR 451.404, please indicate next to each entry on the inspection report a plan of correction. Said plan of correction must be submitted within ten working days of receiving this report and should detail the specific steps that will be taken and the date of expected compliance. The plan of correction should be submitted to my attention, at the address listed above.

To review the specific regulatory requirements please visit our website at www.mass.gov/dph/dcs and click on "Community Sanitation Regulations" (available in both PDF and RTF formats).

To review the Food Establishment regulations please visit the Food Protection website at www.mass.gov/dph/fpp and click on “Food Protection Regulations”. Then under “Retail” click “105 CMR 590.000 - State Sanitary Code Chapter X – Minimum Sanitation Standards for Food Establishments” and “1999 Food Code”.

This inspection report is signed and certified under the pains and penalties of perjury.

Sincerely,

Charles J Kaniecki

District Health Officer, CSP, BEH

cc:	Suzanne K. Condon, Associate Commissioner, Director, BEH

Steven Hughes, Director, CSP, BEH

JudyAnn Bigby, MD, Secretary, Executive Office of Health and Human Services

Luis S. Spencer, Commissioner, DOC

Wayne Hancock, EHSO

Shirley Board of Health

Clerk, Massachusetts House of Representatives

Clerk, Massachusetts Senate

Mary Elizabeth Heffernan, EOPS