The Commonwealth of Massachusetts

Executive Office of Health and Human Services

Department of Public Health

Bureau of Environmental Health

Community Sanitation Program

5 Randolph Street

Canton, MA 02021

Telephone: (781)828-7910

Facsimile: (781)828-7703

lauren.molotnikov@state.ma.us

DEVAL L. PATRICK GOVERNOR TIMOTHY P. MURRAY LIEUTENANT GOVERNOR JUDYANN BIGBY, MD SECRETARY JOHN AUERBACH COMMISSIONER

April 28, 2010

Frank G. Cousins, Jr., Sheriff

Essex County Correctional Facility

20 Manning Avenue

Middleton, MA 01949

Re: Facility Inspection

Dear Sheriff Cousins:

In accordance with M.G.L. c. 111, §§ 5, 20, and 21, and Department of Public Health Regulations 105 CMR 451.000: Minimum Health and Sanitation Standards and Inspection Procedures for Correctional Facilities; 105 CMR 480.000: Storage and Disposal of Infectious or Physically Dangerous Medical or Biological Waste (State Sanitary Code, Chapter VIII); 105 CMR 590.000: Minimum Sanitation Standards for Food Establishments (State Sanitary Code Chapter X); the 1999 Food Code; and 105 CMR 205.000 Minimum Standards Governing Medical Records and the Conduct of Physical Examinations in Correctional Facilities; I conducted an inspection of Essex County Correctional Facility on April 22 and 26, 2010 accompanied by Captain M. Wojcik, Deputy K. Lawrence, Captain Walsh, and Captain W. Garrett. Violations noted are listed below (* indicates conditions documented on previous inspection reports).

Administration Building

Front Lobby

Women’s Bathroom 1002

105 CMR 451.110(A)	Hygiene Supplies at Toilet and Handwash Sink: No soap at handwash sink

105 CMR 451.123*	Maintenance: Ceiling vent dirty

105 CMR 451.123*	Maintenance: Sprinkler head dirty

105 CMR 451.123	Maintenance: Light fixture not working properly

105 CMR 451.123	Maintenance: Sink fixture not properly sealed to wall, caulking damaged

105 CMR 451.126	Hot Water: Hot water temperature recorded at 950F

Men’s Bathroom 1003

105 CMR 451.123	Maintenance: Sink fixture not properly sealed to wall, caulking damaged

105 CMR 451.126	Water Supply: No hot water supplied to handwash sink

Administration Hallway-First Floor

Kitchenette 1007

FC 4-101.16	Materials for Construction and Repair; Multiuse: Sponges used in kitchen

FC 5-202.12(A)	Plumbing System, Design: Handwashing sinks water temperature recorded at 910F

FC 4-601.11(c)	Cleaning of Equipment and Utensils, Objective: Non-food contact surface dirty, 	refrigerator gasket dirty

Female Staff Bathroom 1013

105 CMR 451.123	Maintenance: Light switch cover loose

105 CMR 451.126	Hot Water: Hot water temperature recorded at 900F

Male Staff Bathroom 1014

105 CMR 451.123	Maintenance: Ceiling vent dirty

105 CMR 451.123	Maintenance: Ceiling, wall, and light fixture dirty from vent dust

105 CMR 451.126	Hot Water: Hot water temperature recorded at 900F

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, hot water control leaking

Weight Room 1029

No Violations Noted

Male Staff Locker Room 1030

105 CMR 451.123*	Maintenance: Drain cover missing from shower # 5

105 CMR 451.123*	Maintenance: Wall tiles damaged

105 CMR 451.123	Maintenance: Stall divider rusted

105 CMR 451.123	Maintenance: Ceiling vent dirty

105 CMR 451.130*	Plumbing: Plumbing not maintained in good repair, shower head missing in shower

# 3

105 CMR 451.130*	Plumbing: Plumbing not maintained in good repair, water controls missing from 	shower # 4

105 CMR 451.130*	Plumbing: Plumbing not maintained in good repair, water controls missing from sink 	# 4

Female Staff Locker Room 1031

105 CMR 451.123*	Maintenance: Wall tiles damaged

105 CMR 451.123	Maintenance: Light shield loose

Administration Area-Second Floor

Women’s Bathroom 2002

105 CMR 451.123	Maintenance: Sink fixture not properly sealed to wall, caulking damaged

105 CMR 451.123	Maintenance: Wall and ceiling dirty

105 CMR 451.123	Maintenance: Ceiling vent dirty

105 CMR 451.126	Hot Water: Hot water temperature recorded at 830F

Men’s Bathroom 2003

105 CMR 451.126	Hot Water: Hot water temperature recorded at 750F

Kitchenette 2011

FC 4-101.16	Materials for Construction and Repair; Multiuse: Sponges used in kitchen

FC 4-204.112(A)	Design and Construction, Functionality: No functioning thermometer in refrigerator

Control

105 CMR 451.344	Illumination in Habitable Areas: One light fixture not working properly

105 CMR 451.350	Structural Maintenance: Floor damaged

FC 3-501.16(B)	Limitation of Growth of Organisms, Temperature and Time Control: Refrigerator 	temperature recorded at 470F on the lower shelf

FC 4-204.112(A)	Design and Construction, Functionality: No functioning thermometer in refrigerator

FC 4-602.12(B)	Cleaning of Equipment and Utensils; Frequency: Interior of microwave oven dirty

FC 4-601.11(c)	Cleaning of Equipment and Utensils, Objective: Non-food contact surface dirty, 	gasket dirty on refrigerator unit

Control Bathroom

105 CMR 451.123	Maintenance: Floor dirty

105 CMR 451.123*	Maintenance: Ceiling vent dirty

105 CMR 451.126	Hot Water: Hot water temperature recorded at 910F

Food Service and Medical Building

Records Hallway

Male Staff Bathroom 1005

105 CMR 451.110(A)	Hygiene Supplies at Toilet and Handwash Sink: No soap at handwash sink

105 CMR 451.123	Maintenance: Ceiling vent dirty

105 CMR 451.126	Hot Water: Hot water temperature recorded at 680F

Female Staff Bathroom 1007

105 CMR 451.123	Maintenance: Ceiling paint damaged

105 CMR 451.126	Hot Water: Hot water temperature recorded at 930F

Intake Hallway

Slop Sink Room 1015

105 CMR 451.350	Structural Maintenance: Ceiling damaged

105 CMR 451.353	Interior Maintenance: Slop sink dirty

105 CMR 451.353	Interior Maintenance: Wet mop left in bucket

105 CMR 451.353	Interior Maintenance: No light shield provided in maintenance area

105 CMR 451.353	Interior Maintenance: Vent dirty

105 CMR 451.353	Interior Maintenance: Vent cover missing

Shift Commander’s Office 1039

No Violations Noted

Intake Unit

105 CMR 451.126	Hot Water: Hot water temperature recorded at 960F

105 CMR 451.353	Interior Maintenance: Sink fixture not secured properly to wall

105 CMR 451.353	Interior Maintenance: Counter top damaged

Property Room 1012A

105 CMR 451.353*	Interior Maintenance: Ceiling vent damaged

Shower Area

105 CMR 451.123	Maintenance: Wall tiles damaged and missing

105 CMR 451.123	Maintenance: Shower curtains damaged and missing

Cells

No Violations Noted

Storage Room

105 CMR 451.353	Interior Maintenance: Wet mop left in bucket

Food Service Area

Mechanical Warewashing Area

FC 3-304.14(B)(2)	Preventing Contamination from Linens: Wet cloth not stored in sanitizer bucket

FC 4-701.10	Sanitization of Equipment and Utensils, Objective: Trays not being properly sanitized, 	tray rack not designed to hold insulator trays

# FC 5-203.14*	Plumbing System, Design: No backflow prevention device on spray hose on rinse 	sink, spray hose extends below flood line

FC 5-205.15(B)	Plumbing System, Operations and Maintenance: Plumbing system not maintained in 	good repair, pipes not capped after removal of handwash sink

FC 6-501.11*	Maintenance and Operation; Repairing: Facility not in good repair, ceiling rusted

FC 6-305.11(A)	Numbers and Capacities; Dressing Area and Lockers: Shoes stored in undesignated 	area

FC 6-501.11	Maintenance and Operation; Repairing: Facility not in good repair, cleaning pads used 	to stabilizes metal counter top

FC 6-501.12(A)	Maintenance and Operation; Cleaning: Facility not properly cleaned, standing water 	observed on floor

FC 6-501.12(A)	Maintenance and Operation; Cleaning: Facility not properly cleaned, possible mold 	growth on wall above metal counter top

Manual Warewashing Room

FC 4-501.114(C)(2)*	Maintenance and Operation; Equipment: Quaternary ammonium compound (QAC)	solution greater than manufacturer’s recommended concentration in 3-compartment 	sink

FC 5-205.15(B)	Plumbing System, Operations and Maintenance: Plumbing system not maintained in 	good repair, drains held closed using Styrofoam cups

FC 6-305.11(A)*	Numbers and Capacities; Dressing Area and Lockers: Shoes stored in undesignated 	area

FC 6-501.11	Maintenance and Operation; Repairing: Facility not in good repair, ceiling tiles not 	installed properly

Spray Room

FC 5-203.14	Plumbing System, Design: No backflow prevention device on rinse hose

FC 5-205.15(B)	Plumbing System, Operations and Maintenance: Plumbing system not maintained in 	good repair, spray hose leaking

FC 6-501.11	Maintenance and Operation; Repairing: Facility not in good repair, floor damaged

Front Hoods and Tray Prep Area

FC 4-501.114(C)(2)	Maintenance and Operation; Equipment: Quaternary ammonium compound (QAC)	solution greater than manufacturer’s recommended concentration in sanitizer buckets

FC 6-202.11(A)*	Design, Construction, and Installation; Functionality: Light bulbs not shatter-resistant 	or protected by light shields

FC 6-501.11	Maintenance and Operation; Repairing: Facility not in good repair, floor damaged

FC 6-501.12(A)	Maintenance and Operation; Cleaning: Grease hoods not maintained properly

Kettle Hood Area

FC 6-202.11(A)*	Design, Construction, and Installation; Functionality: Light bulbs not shatter-resistant 	or protected by light shields

FC 6-501.12(A)	Maintenance and Operation; Cleaning: Grease hoods not maintained properly

Oven Hood Area

FC 6-202.11(A)*	Design, Construction, and Installation; Functionality: Light bulbs not shatter-resistant 	or protected by light shields

FC 6-501.12(A)*	Maintenance and Operation; Cleaning: Grease hoods not maintained properly

Walk-In Refrigerator

FC 3-305.11(A)(2)*	Preventing Contamination from Premises: Food exposed to dust, fans in cooler dusty

FC 3-305.11(A)(3)*	Preventing Contamination from Premises: Food stored in an inappropriate location, 	juice containers stored less than 6 inches from the floor

FC 4-501.11(A)*	Maintenance and Operation, Equipment: Equipment not maintained in a state of good 	repair, refrigerator gasket damaged

FC 6-202.11(A)*	Design, Construction, and Installation; Functionality: Light bulbs not shatter-resistant 	or protected by light shields

FC 6-501.11*	Maintenance and Operation; Repairing: Facility not in good repair, one light bulb and 	glass cover missing

Food Preparation and Baking Area

FC 4-501.114(C)(2)	Maintenance and Operation; Equipment: Quaternary ammonium compound (QAC)	solution greater than manufacturer’s recommended concentration outside freezer unit

FC 5-205.15(B)	Plumbing System, Operations and Maintenance: Plumbing system not maintained in 	good repair, faucet loose on 2-compartment sink

FC 5-202.12(A)	Plumbing System, Design: Handwashing sinks water temperature recorded at 830F

FC 6-501.11	Maintenance and Operation; Repairing: Facility not in good repair, floor damaged

FC 6-501.11	Maintenance and Operation; Repairing: Facility not in good repair, floor damaged

Boiler Room 1022

FC 6-501.11	Maintenance and Operation; Repairing: Facility not in good repair, insulation on pipes 	damaged

Freezer

FC 4-501.11(A)	Maintenance and Operation, Equipment: Equipment not maintained in a state of good 	repair, light shield damaged

FC 4-601.11(c)	Cleaning of Equipment and Utensils, Objective: Non-food contact surface dirty, 	freezer floor dirty

Milk Chest 1184

FC 4-501.11(A)*	Maintenance and Operation, Equipment: Equipment not maintained in a state of good 	repair, refrigerator gasket damaged

Dry Storage Room 1031

FC 6-501.12(A)	Maintenance and Operation; Cleaning: Facility not properly cleaned, ceiling dirty

Utensil Storage

FC 6-501.11	Maintenance and Operation; Repairing: Facility not in good repair, floor damaged

Slop Sink Room

FC 6-501.12(A)	Maintenance and Operation; Cleaning: Facility not properly cleaned, portable fan 	dirty

FC 6-501.12(A)	Maintenance and Operation; Cleaning: Facility not properly cleaned, slop sink dirty

Back Cage

FC 6-202.11(A)	Design, Construction, and Installation; Functionality: Light bulbs not shatter-resistant 	or protected by light shields

FC 6-501.12(A)	Maintenance and Operation; Cleaning: Facility not properly cleaned, shelves dusty

FC 6-501.12(A)	Maintenance and Operation; Cleaning: Facility not properly cleaned, fans dirty

Officer’s Room 1025

No Violations Noted

Staff Locker Room and Mop Closet 1026

FC 6-501.11	Maintenance and Operation; Repairing: Facility not in good repair, light shield loose

FC 6-501.11	Maintenance and Operation; Repairing: Facility not in good repair, floor damaged

Female Staff Bathroom 1199

FC 6-101.11(A)(1)	Materials for Construction and Repairs: Surface not easily cleanable, floor paint 	damaged

Male Staff Bathroom 1200

No Violations Noted

Spice Room 1027

    - Sources, Specifications; Specifications for Receiving: Spice bags secured using pieces of cloth

Inmates Bathroom 1029

FC 5-205.15(B)	Plumbing System, Operations and Maintenance: Plumbing system not maintained in 	good repair, no hot water provided at handwashing sink

Loading Dock

FC 6-202.15(A)(3)*	Design, Construction, and Installation; Functionality: Outer door not weather and 	vermin tight, roll down door

Barrel Room

No Violations Noted

Hallway

FC 6-501.11	Maintenance and Operation; Repairing: Facility not in good repair, floor damaged

Inmate Dinning Room

FC 2-402.11	Hygienic Practices; Hair Restraints: Food service personnel not wearing appropriate 	hair restraints, beard guards no in use at the start of inspection

FC 4-501.114(C)(2)	Maintenance and Operation; Equipment: Quaternary ammonium compound (QAC)	solution below manufacturer’s recommended concentration in several sanitizer 	buckets

FC 6-501.11	Maintenance and Operation; Repairing: Facility not in good repair, wall covering 	missing or damaged in several areas

FC 6-501.11	Maintenance and Operation; Repairing: Facility not in good repair, electrical outlet 	not installed properly

FC 6-501.11*	Maintenance and Operation; Repairing: Facility not in good repair, one light fixture 	not working properly

FC 6-501.12(A)	Maintenance and Operation; Cleaning: Facility not properly cleaned, floor dirty

Staff Dinning Room

FC 4-601.11(c)	Cleaning of Equipment and Utensils, Objective: Vending machine draw dirty

FC 5-202.12(A)	Plumbing System, Design: Handwashing sinks water temperature recorded at 1050F

FC 6-501.11	Maintenance and Operation; Repairing: Facility not in good repair, ceiling tiles water 	damaged

Health Service Unit

Entrance

105 CMR 451.353	Interior Maintenance: Vent dirty

Inmate Bathroom 2002

105 CMR 451.126	Hot Water: Hot water temperature recorded at 500F

105 CMR 451.126	Water Supply: No cold water supplied to handwash sink

105 CMR 451.123	Maintenance: Self-closer not working properly on door

105 CMR 451.123	Maintenance: Baseboard damaged

Waiting Lobby

105 CMR 451.353	Interior Maintenance: Thermostat cover damaged

Nurse’s Office 2003

No Violations Noted

Nurse’s Break Room 2004

105 CMR 451.353	Interior Maintenance: Ceiling water stained

FC 4-501.11(A)*	Maintenance and Operation, Equipment: Equipment not maintained in a state of good 	repair, refrigerator door not installed properly leaving a one inch open gap

I1-Isolation Room 2005

105 CMR 451.322*	Cell Size: Inadequate floor space in dorm room

I2-Isolation Room 2006

105 CMR 451.322*	Cell Size: Inadequate floor space in dorm room

105 CMR 451.103	Mattresses: Mattress not easily cleanable, mattress cover missing

Waiting Room 2007

No Violations Noted

Janitor’s Closet 2008

105 CMR 451.350	Structural Maintenance: Wall damaged behind faucet

105 CMR 451.353	Interior Maintenance: Vent dirty

105 CMR 451.353	Interior Maintenance: Wet mop left in bucket

Intake Processing Room 2041

105 CMR 451.126	Hot Water: Hot water temperature recorded at 940F

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, faucet loose

Interview Room

No Violations Noted

Nurse’s Desk

FC 4-501.11(A)	Maintenance and Operation, Equipment: Equipment not maintained in a state of good 	repair, refrigerator gasket loose

R1 2009

No Violations Noted

R2 2010

No Violations Noted

R3 2011

No Violations Noted

R4 2012

No Violations Noted

R5 2014

105 CMR 451.101	Blankets: One blanket damaged

105 CMR 451.114	Shared Toilet and Handwashing Facilities: Inadequate number of toilet facilities and 	handwash sinks per inmate population, one sink and one toilet for 13 beds

105 CMR 451.119	Bathing Facilities: Inadequate shower to inmate ratio, one shower for 13 beds

105 CMR 451.123	Maintenance: Floor tiles damaged and missing in bathroom

105 CMR 451.123	Maintenance: Exposed wood not easily cleanable on bathroom wall

105 CMR 451.322*	Cell Size: Inadequate floor space in dorm room

R6 2015

105 CMR 451.123	Maintenance: Lower door frame rusted in bathroom

105 CMR 451.123	Maintenance: Floor tiles damaged

105 CMR 451.123	Maintenance: Baseboard loose

105 CMR 451.123	Maintenance: Ceiling rusted

105 CMR 451.123	Maintenance: Ceiling vent dirty

105 CMR 451.126	Water Supply: No hot water supplied to handwash sink

105 CMR 451.322*	Cell Size: Inadequate floor space in dorm room

Inmate Shower 2017

105 CMR 451.123	Maintenance: Drain blocked

105 CMR 451.123	Maintenance: Wall not sealed around water controls

105 CMR 451.123	Maintenance: Shower tiles and grout damaged

105 CMR 451.123	Maintenance: Ceiling vent dirty

Staff Bathroom 2019

No Violations Noted

Back Hallway

Staff Bathroom

105 CMR 451.123	Maintenance: Ceiling vent dirty

Hallway Sink

105 CMR 451.126*	Hot Water: Hot water temperature recorded at 830F

Dentist Room 2029	Locked at the time of inspection

X-Ray Room	Radiation Control Inspection Certificate expired on December 31, 2009

Urine Lab Room 2032

105 CMR 451.126	Hot Water: Hot water temperature recorded at 690F

Exam Room 2033	Occupied at the time of inspection

Diabetic Room 2034

105 CMR 451.126	Hot Water: Hot water temperature recorded at 910F

Medical Waste Storage Room

No Violations Noted

Program Building (K)

Lower Programs

Classrooms

No Violations Noted

Inmate Bathroom

105 CMR 451.110(A)*	Hygiene Supplies at Toilet and Handwash Sink: No soap available at handwash sink 105 CMR 451.123	Maintenance: Wall not easily cleanable, seam cover missing and unfilled holes in wall 	covering

105 CMR 451.126*	Water Supply: No hot water supplied to handwash sink

Male Staff Bathroom 1015

105 CMR 451.123*	Maintenance: Ceiling vent dirty

105 CMR 451.123	Maintenance: Counter top not easily cleanable, unfinished counter top

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, faucet loose

Female Staff Bathroom 1016

105 CMR 451.123*	Maintenance: Ceiling vent dirty

105 CMR 451.123	Maintenance: No functioning toilet paper holder provided

Upper Programs

Bathroom 1277

105 CMR 451.126	Hot Water: Hot water temperature recorded at 870F

Male Staff Bathroom 2024

105 CMR 451.123	Maintenance: Ceiling water stained

105 CMR 451.126	Hot Water: Hot water temperature recorded at 1050F

Female Staff Bathroom 2025

No Violations Noted

Slop Sink Room 1278

105 CMR 451.123	Maintenance: Handwash sink dirty

105 CMR 451.123	Maintenance: Vent cover missing

Offices

105 CMR 451.353	Interior Maintenance: Ceiling tiles missing and water stained in office # 2009, 2028, 	and 2032

Vocational Education Building

First Floor

Laundry

105 CMR 451.130*	Plumbing: No backflow preventer on slop sink

105 CMR 451.350	Structural Maintenance: Ceiling water damaged

105 CMR 451.350	Structural Maintenance: Floor damaged in back room

105 CMR 451.353	Interior Maintenance: Floor covered with cleaning solution in back room

FC 4-501.11(A)	Maintenance and Operation, Equipment: Equipment not maintained in a state of good 	repair, refrigerator door handle missing and damaged

Voke Hallway

Staff Bathroom 0913

No Violations Noted

Slop Sink Room

105 CMR 451.353	Interior Maintenance: Wet mop left in bucket

Voke 1

105 CMR 451.101	Blankets: One blanket damaged

105 CMR 451.344	Illumination in Habitable Areas: Light fixtures not working properly

Voke 1 Bathroom

105 CMR 451.123	Maintenance: Soap scum on walls and floor in shower # 2, 3, 4, 5, and 6

105 CMR 451.123	Maintenance: Shower curtain missing on shower # 1 and 7

105 CMR 451.123	Maintenance: Flying insects observed in shower area

105 CMR 451.123	Maintenance: Wall tiles damaged in stall # 4

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, toilet # 3 out of order

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, sink # 2 leaking

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, faucet loose on sink # 2

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, hot water control leaking on sink 	# 3

Voke 2

105 CMR 451.128	Ice: Unsanitary storage and handling conditions, unsanitized ice scoop left in and used 	in ice machine

105 CMR 451.353	Interior Maintenance: Screen damaged

105 CMR 451.353	Interior Maintenance: Ceiling vent dirty

Voke 2 Bathroom

105 CMR 451.123	Maintenance: Soap scum on walls and floor in shower # 2, 3, 4, 5, 6, 7, and 8

105 CMR 451.123	Maintenance: Shower curtain missing on shower # 1 and 5

105 CMR 451.123	Maintenance: Ceiling vent dirty

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, sink # 3 on the left side faucet 	leaking

Warehouse 0918

105 CMR 451.353	Interior Maintenance: Light shield missing in a maintenance area

Supply and Supply Office

105 CMR 451.353	Interior Maintenance: Unlabeled chemical bottle

105 CMR 451.353	Interior Maintenance: Wet mop left in bucket

Voke 3

105 CMR 451.103	Mattresses: One mattress damage

105 CMR 451.353	Interior Maintenance: Portable fan dirty

Voke 3 Bathroom

105 CMR 451.123	Maintenance: Standing water observed on bathroom floor

105 CMR 451.123	Maintenance: Wall tiles damaged in stall # 1

105 CMR 451.123	Maintenance: Shower curtain missing on shower # 1 and 4

105 CMR 451.123	Maintenance: Cloths and plastic wrapped around shower heads in all shower stalls

105 CMR 451.123	Maintenance: Unfinished wooden board on sink

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, shower # 6 leaking

105 CMR 451.130	Hot Water: Shower water temperature recorded at 1150F

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, sink # 2 on the left side leaking

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, sink # 5 on the right side not 	draining properly

Second Floor

Hallway

105 CMR 451.124	Water Supply: Insufficient water supply in quantity and pressure from water fountain

Inmate Bathroom

No Violations Noted

Staff Bathroom 2005

No Violations Noted

Slop Sink Room 2006

105 CMR 451.350	Structural Maintenance: Ceiling water damaged

Voke 4 2007

105 CMR 451.128	Ice: Unsanitary storage and handling conditions, interior of ice machine dirty

Voke 4 Bathroom and Shower Room

105 CMR 451.123	Maintenance: Wall grout damaged in corner in shower room

Barber Shop 2008

105 CMR 451.130*	Plumbing: Plumbing not maintained in good repair, water controls missing from hair 	wash sink

Print Shop 2009

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, faucet loose

120 Building (F)

A&B Control

105 CMR 451.350*	Structural Maintenance: Ceiling tiles water damaged

FC 3-501.16(B)	Limitation of Growth of Organisms, Temperature and Time Control: Refrigerator 	temperature recorded at 500F

FC 4-501.11(A)	Maintenance and Operation, Equipment: Equipment not maintained in a state of good 	repair, light fixture not working properly in refrigerator unit

Control Bathroom

105 CMR 451.123	Maintenance: Ceiling tiles missing

105 CMR 451.123	Maintenance: Ceiling vent dirty

105 CMR 451.123	Maintenance: Unlabeled chemical bottle

105 CMR 451.126	Hot Water: Hot water temperature recorded at 1070F

A Block (Segregation Unit)

Common Area

105 CMR 451.128	Ice: Unsanitary storage and handling conditions, interior of ice machine dirty

105 CMR 451.128	Ice: Unsanitary storage and handling conditions, ice scoop not sanitized properly

105 CMR 451.345	Illumination in Common Passage Ways and Areas: Inadequate lighting, several lights 	not working properly

105 CMR 451.350	Structural Maintenance: Ceiling water damaged

105 CMR 451.350	Structural Maintenance: Baseboard loose near cell # 116

105 CMR 451.353	Interior Maintenance: Portable fan dirty

Slop Sink Room

105 CMR 451.353	Interior Maintenance: Unlabeled chemical bottle

Cells

105 CMR 451.101	Blankets: Blanket damaged in cell # 127, 131, 144, and 150

105 CMR 451.140	Adequate Ventilation: Inadequate ventilation, vent blocked in cell # 124, 125, 127, 	128, 141, 145, 151, 157, 158, 159, and 160

105 CMR 451.141	Screens: Screen damaged in cell # 137 and 139

105 CMR 451.350	Structural Maintenance: Floor tiles damaged in cell # 152

105 CMR 451.353	Interior Maintenance: Wall paint damaged in cell # 130

Shower Area

105 CMR 451.123	Maintenance: Light fixture not working properly in shower # 1

105 CMR 451.123	Maintenance: Standing water observed on floor in shower area

105 CMR 451.123	Maintenance: Soap scum on walls in shower # 2, 3, 4, 5, 6, 7, 8, and 9

105 CMR 451.123	Maintenance: Wall vents dirty

B Block

Common Area

105 CMR 451.128	Ice: Unsanitary storage and handling conditions, ice scoop not sanitized properly

105 CMR 451.128	Ice: Unsanitary storage and handling conditions, exterior and interior of ice machine 	dirty

105 CMR 451.353	Interior Maintenance: Uncapped wires near the phones

Slop Sink Room

105 CMR 451.350	Structural Maintenance: Slop sink damaged

105 CMR 451.353	Interior Maintenance: Unlabeled chemical bottle

105 CMR 451.353	Interior Maintenance: Light shield not provided in a maintenance area

Cells

105 CMR 451.140	Adequate Ventilation: Inadequate ventilation, vent blocked in cell # 204, 206, 209, 	215, 226, 232, 233, 240, 248, 250, 253, 255, and 256

105 CMR 451.141	Screens: Screen damaged in cell # 255, 256, 257, 258, and 260

105 CMR 451.350	Structural Maintenance: Wall paint damaged in cell # 219

Shower Area

105 CMR 451.123	Maintenance: Drain files observed in shower area

105 CMR 451.123	Maintenance: Ceiling dirty outside shower stalls

105 CMR 451.123	Maintenance: Light out in shower # 4

105 CMR 451.123	Maintenance: Light shield damaged in shower # 5

105 CMR 451.123*	Maintenance: Soap scum and possible mold growth on walls and floor in all shower 	stalls

60 Building (G)

Control

Control Bathroom

105 CMR 451.123	Maintenance: Ceiling vent dirty

Cell Block

Common Area

105 CMR 451.128	Ice: Unsanitary storage and handling conditions, ice scoop not sanitized properly

105 CMR 451.128	Ice: Unsanitary storage and handling conditions, exterior and interior of ice machine 	dirty

105 CMR 451.350	Structural Maintenance: Ceiling damaged

105 CMR 451.353	Interior Maintenance: Ceiling vents dirty

Slop Sink Room

105 CMR 451.344	Illumination in Habitable Areas: Light fixture not working properly

105 CMR 451.350	Structural Maintenance: Slop sink damaged

105 CMR 451.353	Interior Maintenance: Pipe insulation damaged

105 CMR 451.353	Interior Maintenance: Light shield not provided in a maintenance area

Cells

105 CMR 451.101	Blankets: Blanket damaged in cell # 324 and 325

105 CMR 451.102	Pillows and Linens: Linens damaged in cell # 312, 325, and 329

Lower Shower Area

105 CMR 451.123*	Maintenance: Soap scum and possible mold growth on walls and floor in all shower 	stalls

105 CMR 451.123*	Maintenance: Wall vent dirty

105 CMR 451.123	Maintenance: Light shield cracked

105 CMR 451.123	Maintenance: One light fixture not functioning properly

105 CMR 451.126	Hot Water: Hot water temperature recorded at 960F

105 CMR 451.130*	Plumbing: Plumbing not maintained in good repair, hand held shower head missing 	from handicap equipped shower

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, floor drain not functioning 	properly outside shower area

Upper Shower Area

105 CMR 451.123*	Maintenance: Ceiling paint damaged

105 CMR 451.123*	Maintenance: Soap scum and possible mold growth on walls and floor in all shower 	stalls

105 CMR 451.123	Maintenance: Wall paint damaged outside shower units

80 Building (H)

Lower 80-First Floor

Control

FC 4-501.11(A)	Maintenance and Operation, Equipment: Equipment not maintained in a state of good 	repair, refrigerator gasket damaged

Common Area

105 CMR 451.128	Ice: Unsanitary storage and handling conditions, ice scoop not sanitized properly

Storage Room

105 CMR 451.350	Structural Maintenance: Ceiling water damaged

105 CMR 451.353	Interior Maintenance: Pipe insulation damaged

Inmate Bathroom

105 CMR 451.123	Maintenance: Possible mold growth on grout and lower wall tiles in shower stall # 2, 	3, and 7

105 CMR 451.123	Maintenance: Shower curtain missing in shower stall # 5

105 CMR 451.123	Maintenance: Wall tiles cracked in toilet stalls

105 CMR 451.126	Hot Water: Hot water temperature recorded at 700F

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, toilet # 2 out of order at the time 	of inspection

Slop Sink Room

105 CMR 451.350	Structural Maintenance: Slop sink damaged

105 CMR 451.353	Interior Maintenance: Vent dirty

Staff Bathroom

105 CMR 451.126*	Hot Water: Hot water temperature recorded at 1070F

Dorm Rooms

Dorm Room # 401

No Violations Noted

Dorm Room # 402

105 CMR 451.140	Adequate Ventilation: Inadequate ventilation, ceiling vent blocked

105 CMR 451.350	Structural Maintenance: Wall cover damaged on seam near bed

Dorm Room # 403

105 CMR 451.140	Adequate Ventilation: Inadequate ventilation, ceiling vent blocked

105 CMR 451.353	Interior Maintenance: Ceiling vent dirty

Dorm Room # 404

105 CMR 451.102	Pillows and Linens: One pillow linens damaged

105 CMR 451.140	Adequate Ventilation: Inadequate ventilation, ceiling vent blocked

Dorm Room # 405

105 CMR 451.353	Interior Maintenance: Window dirty on the exterior surface

Dorm Room # 406

105 CMR 451.101	Blankets: One blanket damaged

105 CMR 451.140	Adequate Ventilation: Inadequate ventilation, ceiling vent blocked

105 CMR 451.350	Structural Maintenance: Floor tiles damaged

Dorm Room # 407

105 CMR 451.102	Pillows and Linens: One pillow damaged

105 CMR 451.140	Adequate Ventilation: Inadequate ventilation, ceiling vent blocked

105 CMR 451.350	Structural Maintenance: Ceiling damaged

105 CMR 451.353	Interior Maintenance: Ceiling vent dirty

Dorm Room # 408

105 CMR 451.140	Adequate Ventilation: Inadequate ventilation, ceiling vent blocked

105 CMR 451.344	Illumination in Habitable Areas: One light fixture not working properly

105 CMR 451.353	Interior Maintenance: Ceiling vent dirty

Dorm Room # 409

105 CMR 451.140	Adequate Ventilation: Inadequate ventilation, ceiling vent blocked

105 CMR 451.344	Illumination in Habitable Areas: One light fixture not working properly

105 CMR 451.353	Interior Maintenance: Ceiling vent dirty

Dorm Room # 410

105 CMR 451.140	Adequate Ventilation: Inadequate ventilation, ceiling vent blocked

105 CMR 451.353	Interior Maintenance: Ceiling vent dirty

105 CMR 451.353	Interior Maintenance: Window dirty on the exterior surface

Upper 80-Second Floor

Control

FC 3-501.16(B)	Limitation of Growth of Organisms, Temperature and Time Control: Refrigerator 	temperature recorded at 500F

FC 4-501.11(A)	Maintenance and Operation, Equipment: Equipment not maintained in a state of good 	repair, refrigerator gasket damaged

Control Bathroom

105 CMR 451.126	Hot Water: Hot water temperature recorded at 980F

105 CMR 451.123	Maintenance: Ceiling vent dirty

Common Area

105 CMR 451.128	Ice: Unsanitary storage and handling conditions, ice scoop not sanitized properly

105 CMR 451.128	Ice: Unsanitary storage and handling conditions, exterior and interior of ice machine 	dirty

105 CMR 451.345	Illumination in Common Passage Ways and Areas: Inadequate lighting, few light 	switches not working properly

105 CMR 451.353	Interior Maintenance: Water control missing from water fountain

Storage Room

105 CMR 451.350	Structural Maintenance: Ceiling tiles water damaged and missing

Inmate Bathroom

105 CMR 451.123	Maintenance: Soap scum and possible mold growth on grout and wall tiles in 	shower stall # 1, 2, 3, 4, 5, 6, and 7

105 CMR 451.123	Maintenance: Soap scum on shower curtain in shower stall # 3, 4, 5, and 7

105 CMR 451.123	Maintenance: Ceiling vent dirty

Staff Bathroom

No Violations Noted

Slop Sink Room

105 CMR 451.350	Structural Maintenance: Slop sink damaged

105 CMR 451.353	Interior Maintenance: Wet mop left in bucket

105 CMR 451.353	Interior Maintenance: Vent dirty

Dorm Rooms

Dorm Room # 411

105 CMR 451.140	Adequate Ventilation: Inadequate ventilation, ceiling vent blocked

105 CMR 451.353	Interior Maintenance: Ceiling vent dirty

Dorm Room # 412

105 CMR 451.101	Blankets: One blanket damaged

Dorm Room # 413

105 CMR 451.140	Adequate Ventilation: Inadequate ventilation, ceiling vent blocked

Dorm Room # 414

105 CMR 451.140	Adequate Ventilation: Inadequate ventilation, ceiling vent blocked

105 CMR 451.344	Illumination in Habitable Areas: Two light fixtures not working properly

105 CMR 451.353	Interior Maintenance: Ceiling vent dirty

105 CMR 451.353	Interior Maintenance: Window dirty

Dorm Room # 415

105 CMR 451.140	Adequate Ventilation: Inadequate ventilation, ceiling vent blocked

105 CMR 451.344	Illumination in Habitable Areas: One light fixture not working properly

Dorm Room # 416

105 CMR 451.140	Adequate Ventilation: Inadequate ventilation, ceiling vent blocked

105 CMR 451.353	Interior Maintenance: Ceiling vent dirty

Dorm Room # 417

105 CMR 451.140	Adequate Ventilation: Inadequate ventilation, ceiling vent blocked

105 CMR 451.344	Illumination in Habitable Areas: One light fixture not working properly

Dorm Room # 418

105 CMR 451.140	Adequate Ventilation: Inadequate ventilation, ceiling vent blocked

105 CMR 451.141	Screens: Screen damaged

Dorm Room # 419

105 CMR 451.140	Adequate Ventilation: Inadequate ventilation, ceiling vent blocked

105 CMR 451.141	Screens: Screen damaged

Dorm Room # 420

105 CMR 451.140	Adequate Ventilation: Inadequate ventilation, ceiling vent blocked

Gym Building (I)

Gym

No Violations Noted

Weight Area

No Violations Noted

Inmate Bathroom

105 CMR 451.123	Maintenance: Uncapped pipes, pipes left after removed of plumbing fixture

105 CMR 451.126	Hot Water: Hot water temperature recorded at 580F

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, sink # 3 out of order at the time of 	inspection

Staff Bathroom

105 CMR 451.123	Maintenance: Floor paint damaged

105 CMR 451.123	Maintenance: Wet mop left in bucket

105 CMR 451.126*	Hot Water: Hot water temperature recorded at 580F

240 Building (J)

A&B Control

FC 4-602.12(B)	Cleaning of Equipment and Utensils; Frequency: Interior of microwave oven dirty

105 CMR 451.353	Interior Maintenance: Ceiling water stained

Control Bathroom

105 CMR 451.123	Maintenance: Ceiling vent rusted

105 CMR 451.123	Maintenance: Ceiling water stained

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, faucet loose

A Block

Common Area

No Violations Noted

Slop Sink Room

105 CMR 451.353	Interior Maintenance: Flying insects observed near slop sink

Cells

105 CMR 451.102	Pillows and Linens: Pillow damaged in cell # 551

Shower Area

105 CMR 451.123*	Maintenance: Soap scum on walls in all shower stalls

105 CMR 451.123*	Maintenance: Standing water observed on floor in shower area

105 CMR 451.123	Maintenance: Ceiling paint damaged

105 CMR 451.130	Hot Water: Shower water temperature recorded at 1150F

B Block

Common Area

105 CMR 451.128	Ice: Unsanitary storage and handling conditions, ice scoop not sanitized properly

105 CMR 451.128	Ice: Unsanitary storage and handling conditions, exterior and interior of ice machine 	dirty

Slop Sink Room

No Violations Noted

Cells

105 CMR 451.102	Pillows and Linens: Towel damaged in cell # 639

105 CMR 451.140	Adequate Ventilation: Inadequate ventilation, vent blocked in cell # 651

105 CMR 451.350	Structural Maintenance: Sprinkler head rusted out in cell # 657

Shower Area

105 CMR 451.123*	Maintenance: Soap scum on walls in all shower stalls

105 CMR 451.123	Maintenance: Ceiling paint damaged

105 CMR 451.123	Maintenance: Wall vents dirty

105 CMR 451.130	Hot Water: Shower water temperature recorded at 1150F

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, shower # 1 running for an 	extended period of time resulting in standing water on the floor in the shower area

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, hand held shower head leaking in 	handicap equipped shower

C Block

Common Area

105 CMR 451.128	Ice: Unsanitary storage and handling conditions, ice scoop not sanitized properly

105 CMR 451.128	Ice: Unsanitary storage and handling conditions, exterior and interior of ice machine 	dirty

105 CMR 451.353	Interior Maintenance: Ceiling vents dirty

105 CMR 451.353	Interior Maintenance: Wall dirty outside cell # 717

Slop Sink Room

105 CMR 451.344	Illumination in Habitable Areas: Light fixture not working properly

105 CMR 451.353	Interior Maintenance: Wet mop left in slop sink

Cells

105 CMR 451.102	Pillows and Linens: Linens damaged in cell # 743

105 CMR 451.103	Mattresses: Mattress uncovered and not easily cleanable in cell # 719, 722, 723, 752, 	755, and 760

105 CMR 451.140	Adequate Ventilation: Inadequate ventilation, vent blocked in cell # 740, 742, and 744

Shower Area

105 CMR 451.123	Maintenance: Floor dirty in handicap equipped shower

105 CMR 451.123*	Maintenance: Wall vents dirty

105 CMR 451.123*	Maintenance: Soap scum and possible mold growth on walls and floors in all shower 	stalls

105 CMR 451.130	Hot Water: Shower water temperature recorded at 1150F

D Block

Common Area

105 CMR 451.128	Ice: Unsanitary storage and handling conditions, ice scoop not sanitized properly

105 CMR 451.128	Ice: Unsanitary storage and handling conditions, exterior and interior of ice machine 	dirty

105 CMR 451.353	Interior Maintenance: Ceiling vent dirty

Slop Sink Room

105 CMR 451.130	Plumbing: Plumbing not maintained in good repair, faucet leaking

105 CMR 451.353	Interior Maintenance: Unlabeled chemical bottles

105 CMR 451.353	Interior Maintenance: Pipe not insulated properly, insulation loose

Cells

105 CMR 451.101	Blankets: Blanket damaged in cell # 843 and 849

105 CMR 451.103	Mattresses: Mattress damage in cell # 836

105 CMR 451.103	Mattresses: Mattress uncovered and not easily cleanable in cell # 812, 834, 856, and 	857

105 CMR 451.140	Adequate Ventilation: Inadequate ventilation, vent blocked in cell # 850

Shower Area

105 CMR 451.123	Maintenance: Hose missing from handicap equip shower stall

105 CMR 451.123	Maintenance: Soap scum and possible mold growth on walls in all shower stalls

105 CMR 451.123	Maintenance: One light fixture not working properly

Outside the Fence

Warehouse

FC 3-501.16(B)	Limitation of Growth of Organisms, Temperature and Time Control: Potentially	hazardous food not held at the proper cold holding temperature, milk left out

Bathroom 1003

No Violations Noted

Slop Sink Room 1004

105 CMR 451.353	Interior Maintenance: Drain dirty

105 CMR 451.353	Interior Maintenance: Unlabeled chemical bottle

Walk-In Freezer

FC 4-501.11(A)	Maintenance and Operation, Equipment: Equipment not maintained in a state of good 	repair, ice build-up in freezer unit on ceiling, walls, and floor

FC 4-501.11(A)*	Maintenance and Operation, Equipment: Equipment not maintained in a state of good 	repair, freezer door and gasket damaged

Garage

FC 4-601.11(c)	Cleaning of Equipment and Utensils, Objective: Non-food contact surface dirty, 	refrigerator gasket dirty

Bathroom 1007

No Violations Noted

Observations and Recommendations

- Throughout the facility paper towels were not stored in the designated holders. Recommend placing paper towel inside the holders to ensure they stay clean and dry

- Recommend storing toilet paper and paper towels above cleaning chemical in storage room in the Intake Unit

- Shelves in the refrigerator unit in the main control room do not allow the air to freely move throughout the refrigerator unit, leaving the top shelf at 390F and the bottom drawer at 470F. Recommend using shelves that were intended for the refrigerator unit or taking steps to ensure the air is able to freely move throughout the unit

- Mechanical warewashing machine conveyer belt is not designed to hold the thick insulated trays used at this correctional facility. This appears to be preventing trays from being appropriately cleaned and sanitized as evident by the trays being place up against each other and falling over pooling water. Recommend the facility take further action to ensure each tray is cleaned and sanitized properly and that the mechanical warewashing machine meets the needs of the facility

- Hose used to fill drink containers stored in a plastic bag. Recommend storing the hose in a clean container that allows some airflow

- Recommend removing water from toilet in the Medical Waste Storage Room in the Health Service Unit

- Please note the following documents have been provided to Lori Lasoff, RN at the time of inspection-Guidelines for Medial Waste Management at Secure Lockup Facilities and example of record-keeping log for medical or biological waste

- Beds in dorm rooms are not labeled, making the communications of violations noted particularly difficult. Recommend labeling beds in dorm rooms

- Missing water controls on the hair wash sink in the Barber Shop 2008 make it impossible to properly adjust the water temperature, recommend replacing the water controls

- Please provided documentation confirming that all blankets supplied to inmates are fire retardant in accordance with 105 CMR 451.101

This facility does not comply with the Department’s Regulations cited above. In accordance with 105 CMR 451.404, please indicate next to each entry on the inspection report a plan of correction. Said plan of correction must be submitted within 10 days of receipt of this letter and should detail the specific steps that will be taken and the date of expected compliance. The plan of correction should be submitted to my attention, at the address listed above.

To review the specific regulatory requirements please visit our website at www.mass.gov/dph/dcs and click on "Community Sanitation Regulations" (available in both PDF and RTF formats).

To review the Food Establishment regulations please visit the Food Protection website at www.mass.gov/dph/fpp and click on “Food Protection Regulations”. Then under “Retail” click “105 CMR 590.000 - State Sanitary Code Chapter X – Minimum Sanitation Standards for Food Establishments” and “1999 Food Code”.

This inspection report is signed and certified under the pains and penalties of perjury.

Sincerely,

Lauren Molotnikov

Environmental Health Inspector, CSP, BEH

cc:	Suzanne K. Condon, Associate Commissioner, Director, BEH

Steven Hughes, Director, CSP, BEH

JudyAnn Bigby, MD, Secretary, Executive Office of Health and Human Services

Harold W. Clarke, Commissioner, DOC

Michael Mark, Superintendent

Environmental health and Safety Officer

Middleton Board of Health

Clerk, Massachusetts House of Representatives

Clerk, Massachusetts Senate

Mary Elizabeth Heffernan, EOPS