|  | Commonwealth of Massachusetts City/Town of Septic System Installation Checklist |
| --- | --- |
|  | DEP has provided this form for use by local Boards of Health if they wish to do so. |
|  | A. Applicant Information |
| Important: When filling out forms on the computer, use only the tab key to move your cursor - do not use the return key. | Name |
|  | Address |
|  | City | State | Zip Code |
|  | Disposal System Construction Permit # | Map | Lot |
|  | Installer |
|  | Designer |
|  | Board of Health Representative |
|  | Inspection Dates: |
|  | Tank: | Date | Leach Area: | Date |
|  | Final: | Date | Other: | Date |
|  | B. Application Checklist |
|  | 1. Pre-Construction Conference | Approved | N/A | Problem |
|  | Sieve analysis supplied for sand |  |  |  |
|  | Current approved plans (3 copies) |  |  |  |
|  | System staked prior to construction |  |  |  |
|  | On-site check for tank water-tightness |  |  |  |
|  | Abandonment of existing system (repairs) |  |  |  |
|  | Plan revision(s) |  |  |  |
|  | Conditions/Approvals |  |  |  |
|  | O/M Plan on file |  |  |  |
|  | DEP approval on file |  |  |  |
|  | B. Application Checklist (cont.) |
|  | 2. Construction Inspection |
|  | a) Building Sewer (310 CMR 15.222) |  | Approved | N/A | Problem |
|  | All waste pipes tied into building sewer | Basement check |  |  |  |
|  | Schedule 40 PVC 4” or cast iron | Verify by reading pipe |  |  |  |
|  | Minimum slope of 0.01-0.02 | Visual |  |  |  |
|  | Pipe laid in continuous straight line | Visual |  |  |  |
|  | Pipe laid on compact, firm base | Visual |  |  |  |
|  | Cleanouts precede all changes in alignment/grade | Verify by visual/tape |  |  |  |
|  | Cleanout provided every 100 ft. | Verify by visual/tape |  |  |  |
|  | Backfill material clean | Visual |  |  |  |
|  | b) Septic Tank (310 CMR 15.223) |  | Approved | N/A | Problem |
|  | Tank is set level with 6” stone under (15.228) | Check with level |  |  |  |
|  | Tank is required size/loading per plan | Verify with plan |  |  |  |
|  | Inlet and outlet are at proper location (15.227) | Verify with plan |  |  |  |
|  | Tank is water tight (15.226) | Test |  |  |  |
|  | Outlet tees extend 6” above flow line | Verify by visual/tape |  |  |  |
|  | Approved filter device placed at outlet | DEP list |  |  |  |
|  | Gas baffle installed at outlet tee | Visual |  |  |  |
|  | Inlet and outlet tees on center line | Visual |  |  |  |
|  | Tank is backfilled with acceptable material | Visual |  |  |  |
|  | Notes: |
|  | B. Application Checklist (cont.) |
|  | c) Distribution Box (310 CMR 15.232) |  | Approved | N/A | Problem |
|  | All outlet pipes at same elevation | Check by adding water |  |  |  |
|  | Number of outlets | per plan |  | Number of laterals | per plan |
|  | Inlet tee min. 1” over outlet | Visual and w/tape |  |  |  |
|  | D box set on level base | Visual |  |  |  |
|  | Top of D box 36” max depth | Visual and w/tape |  |  |  |
|  | D box is water-tight | Add water |  |  |  |
|  | D box has a minimum of 2” thick wall and 12” inside dimension |  |  |  |  |
|  | d) Pump Chamber (310 CMR 15.231) |  | Approved | N/A | Problem |
|  | Tank is set level | Visual and w/level |  |  |  |
|  | Proper volume is provided | Check plan and tank |  |  |  |
|  | Float elevations set per plan | Measure w/tape |  |  |  |
|  | Min. 2” delivery line to D box | Visual |  |  |  |
|  | Number of pumps: |  |  |  |  |
|  | Specified pump provided or designers approval for equal pump |  |  |  |  |
|  | Correct pump sequence |  |  |  |
|  | Covers set to grade |  |  |  |
|  | Electrical permit provided |  |  |  |
|  | 6” of stone beneath chamber | Visual |  |  |  |
|  | Chamber is water-tight | Test |  |  |  |
|  | Min. 9” cover provided | Visual |  |  |  |
|  | Correct loading provided per plan | Visual on tank |  |  |  |
|  | Notes: |
|  | B. Application Checklist (cont.) |
|  | e) Leaching Facility (310 CMR 15.240) |  | Approved | N/A | Problem |
|  | No frozen material used including back fill | Visual |  |  |  |
|  | No clay, tailings or stones larger than 6” for cover material |  |  |  |  |
|  | Soil at bottom/sides of excavation matches info on deep holes |  |  |  |  |
|  | All impervious layers removed | Visual |  |  |  |
|  | No remaining A/B horizons | Visual |  |  |  |
|  | Groundwater conditions match plan and deep holes | Visual/check plan |  |  |  |
|  | Vented if under impervious cover per plan (15.241) |  |  |  |  |
|  | Vent is protected from precipitation and animal entry |  |  |  |  |
|  | Cover of a minimum of 9” over leach area |  |  |  |
|  | Pipe slope equal to 0.005 | Check w/transit |  |  |  |
|  | Leach area per design (15.241) |  |  |  |
|  | Excavation is level and at required depth | Visual/check plan |  |  |  |
|  | Removal of 5 ft material and replacement (if in fill) | Visual/check plan |  |  |  |
|  | Back fill material is acceptable | Visual |  |  |  |
|  | Final contours correct per plan | Check with plan |  |  |  |
|  | Surface/subsurface drainage away from leach area |  |  |  |  |
|  | Final grade and side slopes are stable |  |  |  |
|  | Distribution lines are capped, vented, or connected together |  |  |  |  |
|  | Impermeable barrier (15.255[2]) |  |  |  |
|  | Retaining wall inspected by PE |  |  |  |
|  | Retaining wall is water-proofed |  |  |  |
|  | Retaining wall/barrier is at correct depth/height |  |  |  |  |
|  | B. Application Checklist (cont.) |
|  | f) Leaching trenches (310 CMR 15.251) | Approved | N/A | Problem |
|  | Number of trenches: |  |  |  |  |
|  | Depth of trenches: |  |  |  |  |
|  | Width of trenches: |  |  |  |  |
|  | Trench spacing per plan |  |  |  |
|  | Stone is double-washed [3/4” to 1½”] (15.247) |  |  |  |
|  | g) Leaching fields (310 CMR 15.242) |  |  |  |
|  | Length of field: |  |  |  |  |
|  | Width of field: |  |  |  |  |
|  | Min. of 2 distribution lines |  |  |  |
|  | Separation distance conforms to plan |  |  |  |
|  | Stone is double-washed [3/4” to 1½”] (15.247) |  |  |  |
|  | h) Leaching Pits (310 CMR 15.253) |  |  |  |
|  | Number of pits: |  |  |  |  |
|  | Depth of pits: |  |  |  |  |
|  | Stone is double-washed [3/4” to 1½”] (15.247) |  |  |  |
|  | Each pit has min. 1 20” access cover |  |  |  |
|  | Piping network and configuration of pits/chambers per plan |  |  |  |  |
|  | i) Tight Tank (310 CMR 15.260) |  |  |  |
|  | Tank is set level with 6” stone under | Visual and with level |  |  |  |
|  | Tank is proper size per plan | Visual with plan |  |  |  |
|  | Pumping contract has been provided |  |  |  |
|  | Covers to grade | Visual |  |  |  |
|  | A/V alarm set at 3/5 tank capacity | Check floats by raising |  |  |  |
|  | A/V alarm test on separate circuit | Set off alarm |  |  |  |
|  | B. Application Checklist (cont.) |
|  | j) Certificate of Compliance (310 CMR 15.021) |
|  | As Built Plan Submitted | Date |
|  | Signed by Installer | Date |
|  | Signed by Designer | Date |
|  | Certificate of Compliance Issued | Date |
|  | Notes: |